## Slide 1: cFS Use at Goddard
The Johns Hopkins University Applied Physics Laboratory
core Flight Software System Workshop
October 26, 2015
Alan Cudmore – NASA Goddard Space Flight Center

## Slide 2: cFS at Goddard
Early use of cFS
  OSAL
    Developed for Solar Dynamics Observatory (SDO) – Launched in 2010
    Used to share code between vxWorks on RAD750 and RTEMS on Coldfire CPUs
    First public release in 2004
  cFE - Development started in 2004
  First cFE User – Lunar Reconnaissance Orbiter (LRO)
    Launched June 2009
    vxWorks 6 on RAD750
    cFE was developed during LRO FSW development
    LRO developed cFE applications, some of which became cFS apps
  DISILCAS – Distributed System Integration Lab Communications Adapter Set
    Connects Engineering Test Unit (ETU) boxes and flight-like interfaces to other ETUs and flight-like interfaces (Geographically distributed)

## Slide 3: cFS at Goddard
Current cFS flagship Missions
  GPM - Global Precipitation Measurement
    Launched Feb 2014 -
    Full complement of cFS applications
    RAD750 – vxWorks 6.4
  MMS - Magnetospheric Multiscale Mission
    Launched March 2015
    Four identical spacecraft –
      Radiation Hardened Coldfire ( 40Mhz ) - RTEMS 4.10
      NASA EEPROM File System ( github.com/nasa/eefs)
    Full complement of cFS applications
    Officially began science operations September 4, 2015

## Slide 4: cFS at Goddard
Space Station Experiments
  NICER - Neutron star Interior Composition ExploreR Mission
    ISS Payload
    Using cFS , vxWorks, Broadreach PPC board
  GEDI - Global Ecosystem Dynamics Investigation Lidar
    ISS Payload – Under study / early development
    Using cFS, vxWorks, Broadreach PPC board
  Space Cube / Space Station Experiments
    STP-H4
    STP-H5

## Slide 5: cFS at Goddard
Cubesats and Balloon Missions
  Cubesats
    Dellingr
      Heliophysics “Skunkworks” Cubesat
      Using COTS components
      Nanomind A712 Processor Card
      FreeRTOS , cFS
    CeREs
      cFS on the CHREC Space Processor (CSP)
    Many more being proposed
  Balloon Platforms
    OPIS
    GHAPS – Mission Gondola for High Altitude Planetary Science

## Slide 6: cFS at Goddard
Testing the Dellingr Cubesat ACS FSW
  Problem: Dellingr only has one copy of the flight hardware, and almost no way to test the ACS in a dynamic environment
  The abstracted hardware interfaces allow the cFS based FSW to run on the flight computer or a Linux based PC
ACS cFS App
DHL
Dellingr
Hardware Lib
PC Running the 42
Simulator
Serial protocol
Actuator Cmds
Sensor Data
Hardware Calls
(serial,I2C, SPI)
Common Theme – Abstracting Flight Hardware

## Slide 7: cFS at Goddard
Upcoming work
  MUSTANG / PACE / Ocean Color Instrument
    Custom C&DH / Instrument computer
      Dual Core LEON3 architecture
      FPGA based LEON3FT I/O processor
    RTEMS 4.11
      Multi-Core support
      Dynamic Loader for cFE and cFS applications
      Flash file system
      Possibly Multi-processor communication between LEON3 CPUs

## Slide 8: cFS at Goddard
Technology and Training
  Technology Initiatives
    Multi-core Support co-developed with JHU/APL
    Memory Protection Process Model cFS co-developed with JHU/APL
    Partitioned system – cFS ported to PikeOS on LEON3
    Xenomai Linux – for future Balloon missions
    Software Bus Network updates
    Development Environment (IDE)
  Training –
    cFS Training course
      AKA – ”The Jonathan and Susie show”
    Pi-Sat
      Cubesat Prototype based on Raspberry Pi
      Developed and used by Summer Interns/Co-op students
Common Theme – Training kits

## Slide 9: Goddard as a cFS Customer
Flagship Missions (GPM, MMS, etc)
  Want to have the tested, heritage cFS
Instrument Subsystems
  In the absence of big missions, instruments may play a larger role
Cubesats
  This is a growing trend at GSFC, and the cFS has a large role.
  Heritage/testing plays a role to increase reliability
  Cost is a major factor
ISS/Balloon missions
  More willing to use leading edge technology
Technology development