## Slide 1: cFS Platforms OSAL and PSP
Cal Tech – APL/JPL/Aerospace
core Flight System Workshop
December 12, 2016
Alan Cudmore – NASA Goddard Space Flight Center

## Slide 2: Agenda
Brief history of the OSAL and PSP
Anatomy of a Device Driver
Current PSP Interfaces
Future PSP device interfaces
  cFS Library based device interfaces
  PSP Plugin device interfaces
Other PSP Needs
  Porting Guide and Documentation
  Test Suite

## Slide 3: Brief History of the OSAL & PSP
The Operating System Abstraction layer (OSAL) is a small software library that isolates an application from a supported Real Time Operating System
With the OSAL, flight software such as the core Flight System can be compiled for different operating systems without modifying the source
Currently the OSAL does is a standalone project and does depend on the cFE or cFS
OS_TaskCreate
taskSpawn
rtems_task_create
rtems_task_start
pthread_create
Implementation for vxWorks
Implementation for RTEMS
Implementation for POSIX ( linux, mac os X, etc.. )
OS function to create
a new task

## Slide 4: Brief History of the OSAL & PSP
The Platform Support Package (PSP) is a software library that adapts the cFE Core and cFS applications to a specific hardware and operating system platform*
The PSP was derived from the BSP and HAL directories in the original OSAL. It was named PSP to avoid confusion with an operating system BSP (vxWorks)
The PSP covers the minimum number of APIs to get the cFE/cFS running on a processor with an OS.
The PSP is currently a cFE/cFS specific library
*Some platforms such as linux may be more generic, allowing a PSP to
support more than one hardware platform.

## Slide 5: Brief History of the OSAL & PSP
The first version of the OSAL was created for the SDO mission.
  SDO has a RAD750 running vxWorks and multiple Coldfire CPUs running RTEMS
  SDO pre-dated cFE/cFS
OSAL and the Hardware Abstraction Layer
  The OSAL originally had a hardware abstraction layer (HAL) covering much of what the PSP does now
  Problem: As we developed the cFE, users asked for new versions of the OSAL to support new hardware platforms. It did not make sense to deliver a new version of the OSAL to support a new processor card.
  To make the releases more stable and modular, the HAL was forked to the cFE Platform Support Package (PSP)
Now the purpose of the OSAL is to cover just the operating system interfaces
The PSP became the glue logic that ties the cFE/cFS to a Processor Platform & OS

## Slide 6: Anatomy of a Device Driver
A device driver can take a few different forms
  Small microcontroller based drivers
    Usually Memory Mapped or I/O based device
    Can have interrupt and/or DMA support
    Example: Send data on the I2C bus on the Dellingr/Nanomind CPU
      int i2c_send(int handle, i2c_frame_t * frame, uint16_t timeout);
  Unix style device drivers
    In a POSIX style kernel, drivers live in kernel space and the user interacts through a standard open/close/read/write/ioctl API
  Some Real Time Operating Systems support both types of drivers
    Open/close/.. API is used even though there is no user/kernel space barrier

## Slide 7: Current PSP Device Interfaces
The PSP just covers the necessary interfaces to allow the cFS to run on a particular hardware platform with a particular OS
  Example: RAD750 3U board with vxWorks 6.x
Current PSP interfaces / functions include
  Startup and Restart APIs
    How do we startup the cFE?
    How does the cFE command a restart of the board?
  Memory access APIs
    EEPROM / Nonvolatile memory
    Special access for RAM
    Memory copy utilites ( abstracted to support different memory interfaces )
  Device I/O APIs
  Compiler definitions and switches

## Slide 8: Future PSP Device Interfaces
It will be hard to keep expanding the PSP API to support a growing collection of drivers for cFS applications
  For example: Do we want to add the API for “Bob’s super GPS & Gyro module” if it will only be used on one platform?
  The API would continue to expand (and contract) based on the hardware being supported
  We also don’t want to back port new APIs to old PSPs or have a bunch of “empty” APIs for unsupported devices on each platform
Based on that thought, a couple of options:
  cFS mission hardware libraries
  PSP device plugin model
  Or, a hybrid approach using both as needed

## Slide 9: Mission Hardware Library Option
OS Abstraction Layer
Platform Support Package
RTOS Board Support, File Systems, Drivers, Firmware Libraries, etc
core Flight Executive (cFE)
Processor , Memory, Peripherals, and other hardware
Real Time Operating System
Mission Hardware Library
( All Mission hardware accessed through this library)
cFE/cFS
Legend:
Vendor Supplied
cFE/cFS Reuse
New on Dellingr
cFS
Reuse
App
Mission
App

## Slide 10: Mission Hardware Library Option
Mission Hardware Library
  Pros
    Allows app developers more flexibility in adding and modifying mission specific hardware
    Library APIs can use services such as OSAL Tasks if needed
    Library APIs can use underlying OS, BSP, or firmware if needed
    Easy to incorporate simulator at this level
  Cons
    This model “breaks” the layering by introducing hardware specific code at the app layer ( but at least the apps stay generic )
    An implementation for each platform/OS has to be made
  This model was used for the Dellingr Cubesat, and has worked very well
    Two implementations of the Dellingr Hardware Library (DHL)
      Linux – with simulated hardware and interface to the 42 Dynamic Simulator
      Gomspace Nanomind – with actual hardware/firmware calls

## Slide 11: PSP Plug-in Device Model
OS Abstraction Layer
Platform Support Package
RTOS Board Support, File Systems, Drivers, Firmware Libraries, etc
core Flight Executive (cFE)
Processor , Memory, Peripherals, and other hardware
Real Time Operating System
Mission Hardware Library
(Code can generic APIs below)
cFE/cFS
Legend:
Vendor Supplied
cFE/cFS Reuse
New on Dellingr
cFS
Reuse
App
Mission
App
Plug-in
Plug-in
Plug-in
PSP Device
Plugin Calls

## Slide 12: PSP vs. Library based drivers PSP Plug-in Option
PSP Plug-in model
  Create a device driver model that is generic enough to support underlying layers – from FreeRTOS to RTEMS
  Devices do not have to be portable to all platforms and Operating Systems
  Create a standard API to add or remove a device
  Use a standard API to init/open and use a device

## Slide 13: PSP vs. Library based drivers Hybrid approach
OS Abstraction Layer
Platform Support Package
RTOS Board Support, File Systems, Drivers, Firmware Libraries, etc
core Flight Executive (cFE)
Processor , Memory, Peripherals, and other hardware
Real Time Operating System
Mission Hardware Library
( All Mission hardware accessed through this library)
cFE/cFS
Legend:
Vendor Supplied
cFE/cFS Reuse
New on Dellingr
cFS
Reuse
App
Mission
App
Common Sensor Library
(GPS, Gyro, Temp, etc )
Plug-in
Plug-in

## Slide 14: PSP vs. Library based drivers Hybrid approach
PSP Hybrid approach
  PSP Device Plugins
  cFS Mission Hardware Libraries
    Can include Mission Specific Libraries or more portable libraries such as
      Common Sensor Libraries ( for Sensor/Actuators )
      Simulator Interface Libraries
      Etc