## Slide 1: G&C, Glue, and 42 Independent Dynamics for Independent Testing
Mark Suder
Systems Engineer
TMC Technologies
NASA’s IV&V Program
Image Credit: NASA/JHU APL

## Slide 2: BLUF – Why?
NASA’s Independent Verification and Validation Program
  Key: Independence
    Managerially, financially, technically
  Software within the system focus
NASA IV&V Engineer opportunity:
  Single truth/FSW G&C Matlab/Simulink model developed by the PSP project
  Can IV&V have an independent truth source?

## Slide 3: Parker Solar Probe (PSP)
Swoop closer to the Sun’s surface than any spacecraft before it
Face brutal heat and radiation conditions
Protected by a 4.5-inch-thick carbon-composite shield
Withstand temperatures that reach nearly 2,500 degrees Fahrenheit
G&C pointing is incredibly important!

## Slide 4: Sensors/Actuators
Star Trackers
Reaction Wheel Motors/Tachometers
Solar Limb Sensors
Digital Sun Sensors
IMU/Gyroscopes/Accelerometers
Thrusters
Solar Array Motors/Potentiometers
High Gain Antenna Motor/Potentiometers

## Slide 5: 42 – An Independent Dynamics Source
Developed by Eric Stoneking, GSFC
A simulation of spacecraft attitude and orbital dynamics and control
Intended for use from concept studies through ops
Architecture Source: 42 Overview.pdf, “42, A General-Purpose Multi-body, Multi-spacecraft Simulation, Eric Stoneking, 2014”

## Slide 6: IV&V and JSTAR
IV&V
  Perform analysis of software artifacts for a project
  Requirements, Design, Code, Test, etc.
JSTAR developers
  Experts in simulations
  Build tools used by IV&V analysts to do their job
Sam Brown, IV&V Analyst, started the PSP Testbed
JSTAR developers:
  Re-architected and modularized environment
    Minimized PSP G&C FSW changes
    Easier to upgrade PSP G&C FSW
  Added sensor and actuator models

## Slide 7: Glue
PSP G&C – cFS style application developed by PSP project that uses cFS software bus messages
  Sensor data in
  Actuator data out
42 architecture:
  Allows call out to flight S/W each integration step
JSTAR wrote the Glue Code
  42 dynamics data – position, velocity, acceleration, attitude, sun vector, wheel speeds, joint positions
    Convert to body/sensor frame and then to sensor signals
    Pass in to PSP G&C as the software bus message data structures
  PSP G&C actuator control messages
    Received by glue code and converted to 42 actuator commands
    Thruster firing, reaction wheel torques, motor movements
PSP G&C
cFS Software Bus
Sensor Data
Actuator Data

## Slide 8: Inputs and Outputs
Parameter Files
  Ephemeris, mass props, etc.
  Data from PSP G&C parameters data and documents
Command Files
  Load ephemeris, report parameters, set control parameters
CSV Reports
  Easily plot inputs/outputs

## Slide 9: Video
Visualization can allow the analyst to “see” what the code is causing to happen. Resulting output files can be analyzed to understand behavior.

## Slide 10: Advantages/Disadvantages
Advantages
  Using PSP auto generated & hand generated code
  42 makes it easy to call external flight software… just set/get data at appropriate rates for PSP G&C
  Extensive CSV reporting of G&C inputs, outputs, intermediate results, 42 truth data
  Independent truth model
Disadvantages
  Took time / G&C expertise to develop

## Slide 11: IV&V Uses
Testing
  Ability to independently test how the software will behave under adverse conditions
Learning how the sensors/actuators really work and interact
  A huge benefit not necessarily thought of at the beginning

## Slide 12: Bottom Line
Bottom line – why this is important
  Provides independent testing capability based on IV&V identified need
42 –
Independent
Dynamics
PSP
G&C
Glue
Glue

## Slide 13: Future
Future on PSP
  IV&V analyst testing
Future on other missions
  Pathfinder, shows it is possible
  We went closed loop!

## Slide 14: The End!
Questions?