## Slide 1: Deep Neural Networks for Onboard Intelligence
Daniel Davila
daniel.davila@swri.org
Southwest Research Institute
This is a non-ITAR presentation, for public release
and reproduction from FSW website.

## Slide 2: How Do We Handle All This data?
Modern hardware capable of pushing out very high volume, high veracity data
Need to prioritize observation opportunities before they are lost
LSST – 20 TB / day
MASPEX – 2.5 GB / hr

## Slide 3: Convolutional Neural Network SparkNotes
A deep learning architecture
Come in many shapes and sizes
Applications include image recognition, object detection, and signal processing
Primary operation is convolution on matrices

## Slide 4: Why Machine Learning on FPGA?
Massive parallel computing power = Faster processing of data
Low power
Onboard processing
FPGAs commonly used in space

## Slide 5: Insitu Intelligence
Combines:
  Best practices in compact AI algorithm design
  Modern flight FPGA densities
  Access to ample ground data for training

## Slide 6: Model: Mass Spectrometer for Planetary Exploration
Targeted at planetary science missions
Majority of data collected by instrument is noise
Can neural network be used to automatically select relevant signal for transmission?

## Slide 7: Challenge: Spaceflight Hardware
Typical ground hardware:
Typical space hardware:

## Slide 8: Dataset Description
Information sparsity
Shifting baselines, noisy peaks, low SNR peaks

## Slide 9: Model Architecture
1D Conv Net Architecture
Ingests segments of length 120 as input
Iterates continuously over time series signal

## Slide 10: Network Compression
Goal: Minimize memory usage
  Determined by size of weights and intermediate layer outputs
Goal: Minimize hardware footprint
  Determined by width and depth of network

## Slide 11: Introduction of Fire Modules
Reduces footprint of conv layers by implementing squeeze mechanism
7x reduction in model size with same performance
Model Architecture | Number of Weight Parameters | Model File Size
Fully Convolutional Network | 616,386 | 1.5 Mb
Fully Convolutional Squeeze-net | 264,786 | 236 Kb

## Slide 12: Peak Compression Strategy
Need to define data field that can store information required to reconstruct peak locations
size = 2+ [extracted peak data] + [2 * n_peaks]

## Slide 13: Results: 10x Reduction in Data with 95% Information Retention

## Slide 14: What’s Next?
Explore anomaly detection for new observations
Explore higher dimensional data, such as 2D EO/IR imaging and video
Compare speed and scalability vs GPU
Improve parallelization
Technique | Ratio | Science Information Preserved
Rice Compression | 2.1 | 100%
FLAC | 1.9 | 100%
Neural Net | 10 | 90%
Co-addition | n | (100/n) %