## Slide 1: LADEE FSW Utilization of Lunar Laser Communication Bandwidth
Douglas Forman
Millennium Engineering and Integration Company (MEI)
LADEE FSW Payload I/F Developer
NASA-Ames Research Center
Moffett Field, CA
Craig Pires – LADEE C&DH Lead
Scott Christa – AerospaceComputing, Inc. (ACI)

## Slide 2: Overview
Lasercom Channel for FSW Telemetry Only
  More information on the LADEE lasercom
    Boroson, D.M. et al. “The Lunar Laser Communications Demonstration (LLCD).”
LADEE FSW Approach
  cFE / Payload Interfaces / Integration Testing
LLST (Lunar Laser Space Terminal) Interface
  Control Electronics
  High Speed FSW LLST Interface
LADEE FSW LLST I/F Implementation
  Constraints and Design Decisions
Operational Utilization
  Test, FSW SOH and Science Data
Future Implications

## Slide 3: LADEE FSW
CFE Software Bus
  Goddard Re-usable framework
Model Based Evolution
  Simulink/Autocode
    Closed Loop Simulation
    Auto-coded to Multiple Targets
CCSDS Cmd/Tlm
  ITOS Ground S/W

## Slide 4: “Loosely-Coupled” FSW Architecture
Command
& Mode
Processor
Actuator
Manager
State
Estimator
Safe Mode
Controller
Attitude
Control
System
Thermal
Control
System
Power
Control
System
Scheduler
Limit
Checker
Stored
Commands
Memory
Scrub
Memory
Manager
Memory
Dwell
Hardware
I/O
Health &
Safety
Data
Storage
File
Manager
Telemetry
Output
CCSDS File
Delivery
Checksum
Command
Ingest
House-
keeping
Software Bus
Telemetry
Gnd Cmds
Sensor Data
OFSW
System Support, O/S Services and Device Drivers
Battery
Charge
System
FSW Internal
FSW External
Simulink
Task
cFS
Task
Hand
Written
Task
KEY

## Slide 5: LADEE Payload Interfaces
UVS (Ultra-violet Spectrometer)
  NASA Ames
NMS (Neutral mass Spectrometer)
  Goddard Spaceflight Center
LDEX (Lunar Dust Environment Experiment)
  LASP (University of Colorado at Boulder)
LLST (Lunar Laser Space Terminal)
  MIT Lincoln Labs

## Slide 6: LADEE Travelling Road Show (TRS)
Early EDU Integration
  At Payload Sites
  Before ICDs finalized
Ensure H/W S/W compatibility
Lend EDU/SDU’s
  To Payload Teams
    Remote S/W Updates

## Slide 7: LADEE LLST H/W I/F
cPCI
RS422 CE I/F
Lasercom Control Electronics (CE)
Cmds
&
Tlm
LADEE
Avionics Interface Board
(FPGA Programmable)
Optical Module
LVDH High Speed FSW Telemetry
Optical Link
LADEE CPU Rad750

## Slide 8: LLST Control Electronics (CE) I/F
CCSDS cFE-compatible packets
  Over serial interface (RS422)
  Commands Passed directly to CE
    from cFE Software Bus
  Telemetry from CE
    Published directly to FSW cFE Software Bus
  1/Sec Attitude / Time Message
    State Estimator S/W Bus Message
      Adapted and sent to LLST CE
Files transfers
  Between FSW and CE via CFDP
  Goddard-provided CFDP engine
    Common code used in LADEE FSW and LLCD CE
    cFE wrapper in LADEE FSW
    Custom wrapper in LLCD CE Software
  Usage
    Uplinked Ephemeris Files

## Slide 9: HWIO Apps in FSW Architecture
Command
& Mode
Processor
Actuator
Manager
State
Estimator
Safe Mode
Controller
Attitude
Control
System
Thermal
Control
System
Power
Control
System
HWIO APPS
RWIO, STIO, IMUIO, ADIO,
CMDIO (CI), TLMIO (TO)
Payloads:
LDEXIO, UVSIO, NMSIO, LLCDIO,
HLLCDIO
Software Bus
Data to/from
Devices Over
Device Transports (i.e. RS422, LVDS, etc.)
OFSW
Device Drivers
Battery
Charge
System
FSW Internal
FSW External
Simulink
Task
cFS
Task
Hand
Written
Task
KEY

## Slide 10: LLST LADEE FSW High-Speed Interface
40 Megabits / Second
192 byte frames
Hardware generated footer
  Sequence Count and Checksum
4 wire physical interface
  3 Transmit Wires
    Clock, Data, FrameValidLine
  1 Receive Wire
    ReadyLine for Flow Control

## Slide 11: Filling the Bandwidth
Initial TRS Test with prototype FPGA
  H/W protocol demonstrated
    Discrepancies worked around with Break-out-Box (BOB)
  All of CPU devoted to feeding lasercom tlm
    cPCI Bottleneck between CPU and Interface Board
  Full bandwidth barely achieved
FSW Design Constraints
  Maximize FSW data fed to Lasercom I/F
  Minimize real-time cPCI traffic
  Minimize CPU utilization

## Slide 12: LADEE Telemetry Data Storage
cFE Data Storage Files
  Downlink via R/F
    cfdp type 2 (reliable: retransmits missed chunks)
  1 GB of SDRAM Mass Storage
    Formatted into DOS partitions
    Accessible over cPCI bus by CPU
CFDP over FSW lasercom I/F?
  No FSW lasercom uplink
    Could only do cfdp type 1 (un-reliable: send and forget)
  Requires multiple cPCI accesses
    Retrieval of files for chunking
    Transmitting chunks to lasercom I/F
  Requires non-trivial CPU utilization

## Slide 13: Final Lasercom I/F Design
FPGA transmits Memory Dump chunks
  Takes Flash Mass Storage Start, Stop Addresses as input
    Dumps all memory between Start and Stop Addresses
  CPU interrupted when full Transmission completes
Lasercom Device Driver (on CPU)
  Only cPCI access is writing Start/Stop addresses
  Restarts transmission if looping flag set
Ground Commands
  Set Start, Stop Addresses
  Set/Unset looping flags
Workstation (linux) Post Processing
  FPGA (H/W) headers processed and stripped
  Binary data written to file
  File mounted on workstation as a dos partition
  All files and directories accessible

## Slide 14: Operational Use
All Stored Telemetry Files downlinked in < 5 minutes
  1 GB divided into 5 partitions
Test data Partition
  13 megabytes allocated and filled
  20 distinct files generated from small samples
FSW SOH Partition
  Data useful for analyzing EDAC memory error
Science Partitions
  LLCD Control Electronics Telemetry Useful
  Other Science Data not fully populated
  May run Lasercom again before mission end

## Slide 15: Future Implications
Satellite Swarm Telemetry
  Simultaneous readings from many cubesats
    Sent to Mass Storage Lasercom Relay Node
  Lasercom Node organizes Swarm Data as file system
  Entire swarm state downlinked instantly
    Mounted as a directory of files on Ground
  Delay-Tolerant Networking (DTN)
  Store data on Lasercom Nodes
  Forward data in massive blobs
Interplanetary Lasercom