## Slide 1: Next Generation of Spaceflight Processors: Low Power, High Performance, with Integrated SpaceWire Router and Protocol Engines
Steve Parkes, Chris McClements,
STAR-Dundee Ltd, UK
Guy Mantelet, Nicolas Ganry
Atmel Aerospace, France

## Slide 2: Overview
SpaceWire
STAR-Dundee
Castor Overview
Castor Capabilities
Castor Applications

## Slide 3: SpaceWire
Computer network technology for spacecraft
  SpaceWire
Connects together data-handling elements onboard a spacecraft:
  Instruments
  Processors
  Mass memory
  Telemetry and Telecommand
Standard interface
  Simple
    Implementation requires few logic gates
  High performance
  Flexible architecture
Notes: SpaceWire is a data-handling network technology specifically designed or use onboard spacecraft.
It connects together instruments, processors, mass memory and the telemetry/telecommand subsystem.
SpaceWire provides a standard interface between all these elements, which simplifies integration and testing of the onboard data-handling system.
Instruments and other units designed with SpaceWire interfaces are easy to reuse on other spacecraft,
The SpaceWire standard was written by the University of Dundee with input from spacecraft engineers from across Europe.

## Slide 4: SpaceWire
SpaceWire standard
  Written by University of Dundee
  With inputs from international spacecraft engineers
SpaceWire missions
  Being used or designed into over 100 spacecraft
  Over $15 billion worth of spacecraft rely on it
    Scientific, Exploration, Earth observation, Commercial
Dundee SpaceWire technology designed into
  USA, European, Japanese and other spacecraft

## Slide 6: STAR-Dundee
Established Space Technology Company
  Incorporated 2002
  Supplier to NASA, ESA, JAXA and the global space industry
  Based in Dundee, Scotland, UK
  Management majority owned
SpaceWire
  Leading SpaceWire experts
  Developing standards
Highly Technical Staff
  50% staff PhD qualified
  80% technical R&D
  Capabilities
    Chip design, electronics, software, SpaceWire networks
  All production outsourced to accredited manufacturers
Notes: Originally a spin-out of Dundeee University.
Self funding.
Profitable form the outset and continue to be every year.
Growing organically.

## Slide 7: STAR-Dundee Products
IP Cores: VHDL & Flight Ready
  CODEC, Router, RMAP Initiator, RMAP Target
Interface & router devices
  USB-Brick, Router-USB Mk2
  PCI, cPCI, PCIe
Analysis Tools
  Link Analyser Mk2, Conformance Tester, IP Tunnel
Real-time Instrument Emulator / EGSE
  Real-time instrument emulation in a day!
Software
  Comprehensive software for all devices
  LabVIEW Drivers
Flight Chip Development Kits
  Router Development Kit (AT7910E)
  RTC Development Kit (SPARCv8 based AT7913E)
Notes: IP cores and cover everything needed to design, develop, integrate and test SpaceWire sub-systems

## Slide 8: Castor Overview
Complete system on chip for spaceflight
  Powerful processor core
  IEEE 754 Floating-Point Unit
  Memory Management Unit
  Substantial on-chip memory
  Interfaces to external memory
  SpaceWire router
  SpaceWire protocol engines
  MILSTD 1553 interface
  CAN and many more peripheral interfaces
Atmel AT6981 Castor
  90 nm technology
  Low-power, high-performance
  Radiation tolerant

## Slide 9: AT6981 Castor Architecture
SpW
Router
SpaceWire
Configuration Registers
SpW Engine
SpW Engine
SpW Engine
Switch
Matrix
Internal RAM 1
Internal RAM 2
CAN
CAN
Mil Std 1553
SPARC V8
I-Cache
Debug Port
Internal RAM 3
Mil Std 1553
External Memory Interface:
PROM, SRAM, SDRAM, DDRx
Debug SpW
RMAP/PnP Bus
APB Bridge
Internal RAM 4
D-Cache
Ethernet
Ethernet
Peripheral
Peripheral
Interfaces

## Slide 10: AT6981 Castor Processor
SpW
Router
SpaceWire
Configuration Registers
SpW Engine
SpW Engine
SpW Engine
Switch
Matrix
Internal RAM 1
Internal RAM 2
CAN
CAN
Mil Std 1553
SPARC V8
I-Cache
Debug Port
Internal RAM 3
Mil Std 1553
External Memory Interface:
PROM, SRAM, SDRAM, DDRx
Debug SpW
RMAP/PnP Bus
APB Bridge
Internal RAM 4
D-Cache
Ethernet
Ethernet
Peripheral
Peripheral
Interfaces

## Slide 11: Processor
SPARC® V8, LEON-FT Core
  32-bit architecture
  5 stage pipeline
  8 register windows
  Tightly coupled instruction and data cache
    32 kbyte multi-set instruction cache
    32 kbyte multi-set data cache
Integrated MMU with 32 table entries
Integrated IEEE 754 Floating-Point Unit
  32-bit single and 64-bit double precision
High processing power:
  >150 MIPS Dhrystone 2.1
  > 40 MFLOPS Whetstone
Advanced High-performance Bus (AHB)

## Slide 12: AT6981 Castor H-Matrix
SpW
Router
SpaceWire
Configuration Registers
SpW Engine
SpW Engine
SpW Engine
Switch
Matrix
Internal RAM 1
Internal RAM 2
CAN
CAN
Mil Std 1553
SPARC V8
I-Cache
Debug Port
Internal RAM 3
Mil Std 1553
External Memory Interface:
PROM, SRAM, SDRAM, DDRx
Debug SpW
RMAP/PnP Bus
APB Bridge
Internal RAM 4
D-Cache
Ethernet
Ethernet
Peripheral
Peripheral
Interfaces

## Slide 13: Interconnection Switch Matrix
Multiple AHB master and slave interfaces
Dynamically connects masters to slaves
  Concurrently
  Provided that no two masters access the same slave
    Prevented by arbitration mechanism
Masters
  Processors
  DMA controllers
Slaves
  Memory
  IO

## Slide 14: AT6981 Castor Memory
SpW
Router
SpaceWire
Configuration Registers
SpW Engine
SpW Engine
SpW Engine
Switch
Matrix
Internal RAM 1
Internal RAM 2
CAN
CAN
Mil Std 1553
SPARC V8
I-Cache
Debug Port
Internal RAM 3
Mil Std 1553
External Memory Interface:
PROM, SRAM, SDRAM, DDRx
Debug SpW
RMAP/PnP Bus
APB Bridge
Internal RAM 4
D-Cache
Ethernet
Ethernet
Peripheral
Peripheral
Interfaces

## Slide 15: Memory
Internal Memory
  Several banks
  Each separate slave on Interconnection Switch Matrix
  Total internal memory 1 Mbyte (TBC)
  EDAC protected
External Memory Interface
  PROM
  SRAM
  SDRAM
  DDRx
  EDAC protection for external memories if required

## Slide 16: AT6981 Castor SpaceWire
SpW
Router
SpaceWire
Configuration Registers
SpW Engine
SpW Engine
SpW Engine
Switch
Matrix
Internal RAM 1
Internal RAM 2
CAN
CAN
Mil Std 1553
SPARC V8
I-Cache
Debug Port
Internal RAM 3
Mil Std 1553
External Memory Interface:
PROM, SRAM, SDRAM, DDRx
Debug SpW
RMAP/PnP Bus
APB Bridge
Internal RAM 4
D-Cache
Ethernet
Ethernet
Peripheral
Peripheral
Interfaces

## Slide 17: SpaceWire Engines
Offloads processor from SpW comms
SpaceWire Remote Memory Access (RMAP)
RMAP Target
  Memory region or software based authorisation
RMAP Initiator
  Automatic initiation of multiple commands
DMA
  3x TX and 3x RX channels
Protocol Multiplexer
  Detects SpaceWire or user protocol
  Multiplexes received data accordingly
Time-Code Controller
  Regular and custom time-codes plus signalling codes

## Slide 18: Write Command
Destination Logical Address
Protocol Identifier
Packet Type, Command
Destination Key
Source Logical Address
Transaction Identifier
Transaction Identifier
Extended Write Address
Write Address (MS)
Write Address
Write Address
Write Address (LS)
Data Length (MS)
Data Length
Data Length (LS)
Header CRC
Data
Data
Data
Data
Data
Data
Data
Data
Data
Data CRC
EOP
First byte transmitted
Last byte transmitted
Above format is when using SpaceWire Logical Addressing

## Slide 19: Write Operation
Write Request
Write Data
Request
Write
Command
Write
Reply
Write Complete
Confirmation
RMAP
Source
RMAP
Destination
Write Data
Authorisation
Write Data
Write Data
Indication
USER
APPLICATION
USER
APPLICATION
SpaceWire
Network

## Slide 20: Write Reply
Source Logical Address
Protocol Identifier
Packet Type, Command
Status
Destination Logical Address
Transaction Identifier
Transaction Identifier
Reply CRC
EOP
First byte transmitted
Last byte transmitted
Above format is when using SpaceWire Logical Addressing

## Slide 21: SpaceWire Engines
Offloads processor from SpW comms
SpaceWire Remote Memory Access (RMAP)
RMAP Target
  Memory region or software based authorisation
RMAP Initiator
  Automatic initiation of multiple commands
DMA
  3x TX and 3x RX channels
Protocol Multiplexer
  Detects SpaceWire or user protocol
  Multiplexes received data accordingly
Time-Code Controller
  Regular and custom time-codes plus signalling codes

## Slide 22: AT6981 Castor SpaceWire
SpW
Router
RMAP Target
DMA Channel (x3)
RMAP Initiator
DMA Channel (x3)
DMA Channel (x3)
Protocol
Multiplexer
AHB
Interface
SpaceWire Engine 2
SpaceWire Engine 3
SpaceWire Engine 1
AHB
SpaceWire

## Slide 23: AT6981 Castor Peripherals
SpW
Router
SpaceWire
Configuration Registers
SpW Engine
SpW Engine
SpW Engine
Switch
Matrix
Internal RAM 1
Internal RAM 2
CAN
CAN
Mil Std 1553
SPARC V8
I-Cache
Debug Port
Internal RAM 3
Mil Std 1553
External Memory Interface:
PROM, SRAM, SDRAM, DDRx
Debug SpW
RMAP/PnP Bus
APB Bridge
Internal RAM 4
D-Cache
Ethernet
Ethernet
Peripheral
Peripheral
Interfaces

## Slide 24: Peripherals
Redundant pair of MILSTD 1553 interfaces
  Bus controller
  Or Remote Terminal
  DMA controller
Redundant pair of CAN Bus interfaces v2.0
  15 channels
  DMA controller
Ethernet
Lower speed peripherals
  SPI Serial Peripheral interface
  TWI Two wire interface (also called I2C)
  UART
  ADC & DAC interfaces
  Pulse width modulation
  GPIO

## Slide 25: Peripherals
Peripheral Bridge
APB
Timer
Watchdog
PMC
INT
PIO
RESET
System Control
DMA
ADC
DMA
DAC
PWM
DMA
SPI
DMA
TWI
DMA
UART
AHB Interconnection Switch Matrix

## Slide 26: AT6981 Castor Debug
SpW
Router
SpaceWire
Configuration Registers
SpW Engine
SpW Engine
SpW Engine
Switch
Matrix
Internal RAM 1
Internal RAM 2
CAN
CAN
Mil Std 1553
SPARC V8
I-Cache
Debug Port
Internal RAM 3
Mil Std 1553
External Memory Interface:
PROM, SRAM, SDRAM, DDRx
Debug SpW
RMAP/PnP Bus
APB Bridge
Internal RAM 4
D-Cache
Ethernet
Ethernet
Peripheral
Peripheral
Interfaces

## Slide 27: Debug and Test
Comprehensive debug support
Debug support unit
  Breakpoints
  Single stepping
  Register and memory access
  Trace memory
  Hardware watch-points
Accessible via
  JTAG
  Debug UART
  Debug SpaceWire (high-speed debug)

## Slide 28: AT6981 Castor Characteristics
Operating Temperature Range
  -55ºC to +125ºC (Tj max 145ºC)
Radiation Tolerance
  Total dose 300 Krads (Si)
  SEU error rate < 10-5 errors/device/day
  No SE latch-up below LET threshold of 70 MeV.cm2/mg
Low Power Consumption
  Dedicated mechanisms for adapting power consumption
  To level of processing performance
    Programmable clock for each major function
    Dedicate reset for each major function
  Estimated core power
    Core operating current target 5mA/MHz

## Slide 29: Software Development Environment
SDE from STAR-Dundee
Eclipse Development Platform
GNU Compiler Collection (GCC)
Target Development Hardware
C / C++ Language Module (CDT)
STARGate
SSDE
Plugins
Code Rocket
Code Visulation, Design & Documentation

## Slide 30: Code Rocket

## Slide 31: Code Rocket Design Views
Changes made to design reflected in code

## Slide 32: Code Rocket Design Views
Changes made to code reflected in design

## Slide 33: Target-Specific Debug Views
Device registers (showing AT7913 registers)

## Slide 34: Spaceflight Applications
Instrument
Instrument
Instrument
AOCS
Sensors
AOCS
Actuators
AOCS
Processing
Instrument
Processing
Housekeeping
Processing
Payload Control
Processing
Data Compression
Mass Memory
HK Telemetry
Encoding
Telecommand
Decoding
Communications
Payload Telemetry
Encoding
Single and double precision floating-point
Interfaces suitable for most AOCS sensors
Pulse Width Modulation
High processing power
  >150 MIPS
  >40 MFLOPS
On-chip memory
Interfaces to Spacecraft networks.
SpaceWire & MILSTD 1553 I/F
On-chip memory for command buffering
On-chip SpaceWire router
SpaceWire engines with DMA to off-load processor from command distribution
SpaceWire RMAP Initiator
Able to send repeated commands and gather replies without processor intervention
Perfect for gathering housekeeping data over SpaceWire network
Low power consumption
Plenty of processing capability
On-chip memory
On-chip peripherals
ADC & DAC interfaces
Interfaces to Spacecraft networks
SpaceWire RMAP Target

## Slide 35: AT6981 Castor Prototype
Photo of PXI Board

## Slide 36: Conclusions
Atmel AT6981 Castor
Highly capable processing system on-chip
Low power
High performance
Substantial on-chip memory
Extensive set of on-chip peripherals
SpaceWire router and protocol engines
Designed for spaceflight applications
Current status
  Design frozen, functional validation ongoing
  Evaluation kit available 1Q14
  SDE from STAR incorporating Code Rocket technology