## Slide 1: SpaceWire EGSE: Real-Time Simulation of SpaceWire Instruments in a Day
Stephen Mudie, Steve Parkes, Martin Dunstan
Notes: Introduce yourself and the EGSE.

## Slide 2: SpaceWire EGSE
What is SpaceWire EGSE:
  SpaceWire test and development unit developed by STAR-Dundee
Purpose:
  Rapidly emulate instruments or other SpaceWire equipment
  In real-time for test and integration
Generates user defined packets
  In pre-defined sequences at specific times and data rates
  E.g. packet 1 followed 10ms later by packet 2 at 100Mbps
Notes: EGSE description. Expand on purpose.

## Slide 3: SpaceWire EGSE
Camera
Mass
Memory
SpW
Notes: EGSE description. Expand on purpose.

## Slide 4: SpaceWire EGSE
EGSE
(simulating camera)
Mass
Memory
SpW
Notes: EGSE description. Expand on purpose.

## Slide 5: SpaceWire EGSE
How it works:
  User defines instrument behaviour in a script
  Software used to compile script and load resulting configuration file into EGSE unit
  Hardware functions independent of software resulting in real-time performance
Benefits:
  Reduce time and costs associated with traditional EGSE development
  All real-time behaviour is handled by hardware
Notes: An alternative to traditional EGSE development requiring a SpW interface card, software engineer, real-time operation system and significant development time. Reduce time and costs associated with traditional EGSE development

## Slide 6: SpaceWire EGSE Hardware
2 SpaceWire interfaces
4 external triggers (3 IN, 1 OUT)
128MB memory
2 Mictor logic analyser connectors
USB connection to host PC
Indicator LEDs
Notes: Hardware description.
2 SpW interfaces: tx and rx SpW traffic
4 ext triggers: interfacing with ext equipment
128MB memory: stores packet definitions
2 mictors: show device state
Indicator LEDs: status of SpW interfaces, ext triggers and USB port

## Slide 7: SpaceWire EGSE Front Panel

## Slide 8: SpaceWire EGSE Rear Panel

## Slide 9: SpaceWire EGSE Software
Compiler
  Compiles scripts into EGSE configuration files
Loader
  Loads EGSE configuration files onto hardware
Software API
  Create custom applications to control and interact with the EGSE
GUI
  Combines a text editor with most of the functions provided by the compiler, loader and API
Notes: Software description.

## Slide 10: SpaceWire EGSE Software GUI
Notes: Text editor
Compile + load toolbar buttons
Generate software events
View EGSE notifications
Time-code management

## Slide 11: SpaceWire EGSE Scripting Language
Packet Definitions
Variables
  Used to define packets with dynamic data
Packet Generation Schedules
State Machines
  Control current packet generation schedule
Events
  State machine reacts to events, controlling the packet generation schedule
Notes: Mainly consists of:

## Slide 12: SpaceWire EGSE: Simple Script
config
spw_tx_rate(1, 200Mbps)
spw_tx_rate(2, 200Mbps)
end config
packet pkt1
dec(1 2 3 4)
eop
end packet
schedule schedule1 @ 100Mbps
500ms send pkt1
end schedule
statemachine 1
initial state state1
do schedule1 repeatedly
end state
end statemachine
Set line rates to 200Mbit/s

## Slide 13: SpaceWire EGSE: Simple Script
config
spw_tx_rate(1, 200Mbps)
spw_tx_rate(2, 200Mbps)
end config
packet pkt1
dec(1 2 3 4)
eop
end packet
schedule schedule1 @ 100Mbps
500ms send pkt1
end schedule
statemachine 1
initial state state1
do schedule1 repeatedly
end state
end statemachine
Define packet named “pkt1” with 4 decimal bytes followed by EOP

## Slide 14: SpaceWire EGSE: Simple Script
config
spw_tx_rate(1, 200Mbps)
spw_tx_rate(2, 200Mbps)
end config
packet pkt1
dec(1 2 3 4)
eop
end packet
schedule schedule1 @ 100Mbps
500ms send pkt1
end schedule
statemachine 1
initial state state1
do schedule1 repeatedly
end state
end statemachine
Define schedule named “schedule1” that sends “pkt1” after 500ms at 100Mbit/s

## Slide 15: SpaceWire EGSE: Simple Script
config
spw_tx_rate(1, 200Mbps)
spw_tx_rate(2, 200Mbps)
end config
packet pkt1
dec(1 2 3 4)
eop
end packet
schedule schedule1 @ 100Mbps
500ms send pkt1
end schedule
statemachine 1
initial state state1
do schedule1 repeatedly
end state
end statemachine
SpW link 1 state machine has a single state that executes “schedule1” repeatedly

## Slide 16: SpaceWire EGSE: Simple Script
Notes: Data is 1,2,3,4
Link speed is 200Mbits/s
500ms between the transmission of each packet

## Slide 17: SpaceWire EGSE: Simple Script
Notes: Data is 1,2,3,4
Link speed is 200Mbits/s
500ms between the transmission of each packet

## Slide 18: SpaceWire EGSE: Simple Script
500ms
500ms
500ms
Notes: Data is 1,2,3,4
Link speed is 200Mbits/s
500ms between the transmission of each packet

## Slide 19: SpaceWire EGSE: Variables Script
variables
random = rnd08()
header = int08(2)
id = inc08(0)
crc = crc08()
end variables
packet pkt1
start(crc)
header
id
random * 8
stop(crc)
crc
eop
end packet
schedule schedule1 @ 100Mbps
500ms send pkt1
end schedule
statemachine 1
initial state state1
do schedule1 repeatedly
end state
end statemachine
Declare random variable

## Slide 20: SpaceWire EGSE: Variables Script
variables
random = rnd08()
header = int08(2)
id = inc08(0)
crc = crc08()
end variables
packet pkt1
start(crc)
header
id
random * 8
stop(crc)
crc
eop
end packet
schedule schedule1 @ 100Mbps
500ms send pkt1
end schedule
statemachine 1
initial state state1
do schedule1 repeatedly
end state
end statemachine
Declare constant variable value 2

## Slide 21: SpaceWire EGSE: Variables Script
variables
random = rnd08()
header = int08(2)
id = inc08(0)
crc = crc08()
end variables
packet pkt1
start(crc)
header
id
random * 8
stop(crc)
crc
eop
end packet
schedule schedule1 @ 100Mbps
500ms send pkt1
end schedule
statemachine 1
initial state state1
do schedule1 repeatedly
end state
end statemachine
Declare incrementing variable value 0

## Slide 22: SpaceWire EGSE: Variables Script
variables
random = rnd08()
header = int08(2)
id = inc08(0)
crc = crc08()
end variables
packet pkt1
start(crc)
header
id
random * 8
stop(crc)
crc
eop
end packet
schedule schedule1 @ 100Mbps
500ms send pkt1
end schedule
statemachine 1
initial state state1
do schedule1 repeatedly
end state
end statemachine
Declare CRC variable

## Slide 23: SpaceWire EGSE: Variables Script
variables
random = rnd08()
header = int08(2)
id = inc08(0)
crc = crc08()
end variables
packet pkt1
start(crc)
header
id
random * 8
stop(crc)
crc
eop
end packet
schedule schedule1 @ 100Mbps
500ms send pkt1
end schedule
statemachine 1
initial state state1
do schedule1 repeatedly
end state
end statemachine
Define packet
named “pkt1”:
Constant header
Incrementing ID
8 random bytes
CRC calculation

## Slide 24: SpaceWire EGSE: Variables Script

## Slide 25: SpaceWire EGSE: Variables Script
Constant
header

## Slide 26: SpaceWire EGSE: Variables Script
Incrementing
ID

## Slide 27: SpaceWire EGSE: Variables Script
Random
bytes

## Slide 28: SpaceWire EGSE: Variables Script
CRC

## Slide 29: SpaceWire EGSE: Schedules Script
packet pkt1
hex(11 11 11 11)
eop
end packet
packet pkt2
hex(22 22 22 22)
eop
end packet
packet pkt3
hex(33 33 33 33)
eop
end packet
Define 3 packets named “pkt1”, “pkt2” and “pkt3” each with unique data.

## Slide 30: SpaceWire EGSE: Schedules Script
schedule schedule1
1s send pkt1 * 5
end schedule
schedule schedule2
500ms send pkt1
1000ms send pkt2
1500ms send pkt3
end schedule
schedule schedule3
0ms send pkt3
+1s send pkt2
+1s send pkt1
end schedule
“schedule1” sends “pkt1” 5 times, 1s after schedule starts

## Slide 31: SpaceWire EGSE: Schedules Script
schedule schedule1
1s send pkt1 * 5
end schedule
schedule schedule2
500ms send pkt1
1000ms send pkt2
1500ms send pkt3
end schedule
schedule schedule3
0ms send pkt3
+1s send pkt2
+1s send pkt1
end schedule
“schedule2” sends “pkt1” 500ms, “pkt2” 1000ms and “pkt3” 1500ms after schedule starts

## Slide 32: SpaceWire EGSE: Schedules Script
schedule schedule1
1s send pkt1 * 5
end schedule
schedule schedule2
500ms send pkt1
1000ms send pkt2
1500ms send pkt3
end schedule
schedule schedule3
0ms send pkt3
+1s send pkt2
+1s send pkt1
end schedule
“schedule3” sends “pkt3” immediately, “pkt2” 1s after “pkt3” tx begins and “pkt1” 1s after “pkt2” tx begins

## Slide 33: SpaceWire EGSE: Schedules Script
statemachine 1
initial state state1
do schedule1
goto state2
end state
state state2
do schedule2
goto state3
end state
state state3
do schedule3
goto state1
end state
end statemachine
“state1” executes “schedule1”once then transitions to “state2”
“state2” executes “schedule2”once then transitions to “state3”
“state3” executes “schedule3”once then transitions to “state1”

## Slide 34: SpaceWire EGSE: Schedules Script

## Slide 35: SpaceWire EGSE: Schedules Script
schedule1

## Slide 36: SpaceWire EGSE: Schedules Script
schedule2

## Slide 37: SpaceWire EGSE: Schedules Script
schedule3

## Slide 38: SpaceWire EGSE: FSM and Events Script
events
swEvent0 = software_in(0)
end events
statemachine 1
initial state state1
do schedule1
on swEvent0 goto state2
end state
state state2
do schedule2
on swEvent0 goto state3
end state
state state3
do schedule3
on swEvent0 goto state1
end state
end statemachine
Declare software event named “swEvent0”

## Slide 39: SpaceWire EGSE: FSM and Events Script
events
swEvent0 = software_in(0)
end events
statemachine 1
initial state state1
do schedule1
on swEvent0 goto state2
end state
state state2
do schedule2
on swEvent0 goto state3
end state
state state3
do schedule3
on swEvent0 goto state1
end state
end statemachine
Change state when “swEvent0” is detected.
Notes: Mention other event types:
- software, state machine, ext trigger in, ext trigger out, time-code rx, time-code tx, received pattern matched, link error

## Slide 40: Other Features
Software events
Triggering on SpaceWire received packets
Triggering on received time-codes

## Slide 41: Solar Orbiter Simulation
Project Aims
  STAR-Dundee SpaceWire-EGSE unit
    Able to perform real-time instrument simulation in a day
  Wanted to explore its
    Capabilities
    Limitations
  With a view to enhancing its capabilities
  Simulate a complete on-board data-handling system

## Slide 42: Spacecraft selection
Evaluated missions for simulation
  Requirement: Extensive SpW OBDH network
Selected: ESA Solar Orbiter
  Routed SpaceWire Network
  Standard CCSDS packets
  Standard ECSS PUS services
  Documents available through BepiColombo heritage
Image Credit: ESA

## Slide 43: Solar Orbiter Mission Profile
ESA M-class mission
  ESA’s Cosmic Vision 2015-2025
  Contractor: Astrium UK Ltd.
Remote sensing
    EUI,
    METIS,
    PHI,
    SoloHI,
    SPICE,
    STIX
In situ
    EPD,
    MAG,
    RPW,
    SWA
Image Credit: ESA
Notes: M-class mission: ESA classification for a medium-sized mission
In-situ: (“in position”) -- ON BOOM
- EPD: Electronic Particle Detector
- MAG: Magnetometer
- RPW: Radio and Plasma Waves
- SWA: Solar Wind Plasma Analyser
Remote sensing: -- BEHIND SHIELD
- EUI: Extreme UV Imager
- METIS: Coronagraph
- PHI: Polarimetric and Helioseismic Imager
- SoloHI: Heliospheric Imager
- SPICE: Spectral Imaging of the Coronal Environment
- STIX: X-ray Spectrometer / Telescope

## Slide 44: Solar Orbiter SpaceWire Network
Image Credit: Paul Norridge, Astrium UK

## Slide 45: Solar Orbiter Mass Memory

## Slide 46: Solar Orbiter SSMM Simulation I

## Slide 47: Solar Orbiter SSMM Simulation II

## Slide 48: Solar Orbiter simulated OBDH network

## Slide 49: Demonstration Network

## Slide 51: EGSE Summary
New concept for SpaceWire instrument real-time emulation
Minimal development time
  A day or two for a instrument real-time emulation
Integrate with other test equipment via external triggers
Interacts with host software via
  Software events from host to EGSE
  Software events from EGSE to host
  Received SpaceWire packets can be passed to the host software
Real-time simulation of the Solar Orbiter
  Designed and developed by MSc Student
  Using STAR-Dundee SpaceWire-EGSE unit
  Some limitations on the simulation to make it realisable
  Results being used to enhance the SpaceWire-EGSE functionality