## Slide 1: SpaceFibre A Multi-Gigabit/s Network for Spaceflight Applications
Steve Parkes1, Chris McClements1,
Albert Ferrer2, Alberto Gonzalez2
1Space Technology Centre, University of Dundee, UK
2STAR-Dundee Ltd, UK and Spain

## Slide 2: Contents
SpaceFibre Need
SpaceFibre Standard
SpaceFibre Quality of Service
SpaceFibre Chips
SpaceFibre Test Equipment
SpaceFibre Validation
SpaceFibre Current and Planned Work

## Slide 4: The Need for SpaceFibre
Need for very-high data-rates
  Synthetic Aperture Radar (SAR)
  High-resolution multi-spectral imaging
Need for integrated control and data network
  Instrument data-handling
  Equipment control
  Housekeeping information
  Time distribution
  All over the same network
  Saving mass and power
Need for determinism
  To support AOCS and other control applications

## Slide 5: The Need for SpaceFibre
Need for long distances
  For launcher applications
Need for galvanic isolation and improved FDIR capabilities
  To improve overall reliability and robustness
Need for integrated Quality of Service
  To simplify software and system design
Need for backwards compatibility with existing data-handling technology
  SpaceWire

## Slide 6: SpaceFibre Key Features
SpaceFibre key features
  High performance
    2.5 Gbits/s current flight qualified technology
    20 Gbits/s with multi-laning
  Galvanic isolation
  Electrical and fibre-optic cables
  Low latency
    Broadcast codes
  Integrated QoS
    Bandwidth reservation
    Priority
    Scheduling
  Integrated FDIR support
  Low implementation cost
  Compatible with SpaceWire at packet level
SpaceFibre
Designed for Spaceflight
Applications

## Slide 7: SpaceFibre Standard
Quality Layer
Lane Layer
VC Interface
Multi-Lane Layer
Physical Layer
Broadcast Interface
Physical Interface
Network Layer
Packet Interface
Management Layer
Management
Interface
Broadcast Message Interface

## Slide 8: SpaceWire CODEC
SpaceWire CODEC
Packet Interface
Time-Codes
Management
Serial

## Slide 9: SpaceFibre IP Core
SpaceFibre IP Core
…
Virtual Channel Interfaces
Broadcast
Management
SerDes
Each VC like pair of SpW FIFOs.
Sends and Receives SpFi packets
Broadcasts short messages.
Time distribution, synchronisation, event signalling, error handling
Management interface configures VCs, BC, etc

## Slide 10: Network Layer
Packets
  Packages information to be sent over link
  Transfers packets over network
  <Dest. Address><Cargo><EOP>
  Same routing concepts as SpaceWire
  Path and logical addressing
Broadcast Messages
  Broadcasts short messages across network
  Can carry time-codes, time messages, events
Quality Layer
Lane Layer
Multi-Lane Layer
Physical Layer
Network Layer
Management Layer

## Slide 11: Management Layer
Configures, controls and monitors status
Quality Layer
Lane Layer
Multi-Lane Layer
Physical Layer
Network Layer
Management Layer

## Slide 12: Quality Layer
QoS and FDIR
Virtual Channels:
  Quality of service and flow control
Framing:
  Frames information to be sent over link
  Scrambles SpaceFibre packet data
Retry:
  Recovers from transient errors
  Can cope with bit error rate of 10-6
Quality Layer
Lane Layer
Multi-Lane Layer
Physical Layer
Network Layer
Management Layer

## Slide 13: Multi-Lane Layer
Runs several SpaceFibre lanes in parallel
Provides higher data throughput
Provides redundancy with graceful degradation
Quality Layer
Lane Layer
Multi-Lane Layer
Physical Layer
Network Layer
Management Layer

## Slide 14: Lane Layer
Lane control
  Lane initialisation and error detection
Encoding/Decoding:
  Encodes data into symbols for transmission
  8B/10B encoding
  DC balanced
Quality Layer
Lane Layer
Multi-Lane Layer
Physical Layer
Network Layer
Management Layer

## Slide 15: Physical Layer
Serialisation:
  Serialises SpaceFibre symbols
  Includes oversampling clock-data recovery
Fibre optic or electrical medium
Quality Layer
Lane Layer
Multi-Lane Layer
Physical Layer
Network Layer
Management Layer

## Slide 16: SpaceFibre Quality of Service
Integrated QoS scheme
  Priority
    VC with highest priority
  Bandwidth reserved
    VC with allocated bandwidth and recent low utilisation
  Scheduled
    Synchronised Time-slots
      E.g. by broadcast messages
    VCs allocated to specific time-slots
    In allocated time-slot, VC allowed to send

## Slide 17: SpaceFibre QoS
Integrated QoS scheme
  Priority
    VC with highest priority
  Bandwidth reserved
    VC with allocated bandwidth and recent low utilisation
  Scheduled
    Synchronised Time-slots
      E.g. by broadcast messages
    VCs allocated to specific time-slots
    In allocated time-slot, VC allowed to send

## Slide 18: Virtual Channels
VC sends when
  Source VC buffer has data to send
  Destination VC buffer has space in buffer
  QoS for VC results in highest precedence
A SpW packet flowing through one VC does not block another packet flowing through another VC
VC1
VC2
VC3
MAC
VC1
VC2
VC3
DEMUX

## Slide 19: QoS: Bandwidth Reserved
time
Precedence
Bandwidth Credit Counter

## Slide 20: QoS: Bandwidth Reserved
time
Precedence

## Slide 21: QoS Priority
time
Priority 1
Priority 2
Priority 3

## Slide 22: Scheduled Precedence
Time-slot
1
2
3
4
5
6
7
8
VC 1
VC 2
VC 3
VC 4
VC 5
VC 6
VC 7
VC 8

## Slide 23: Configured for Priority and BW Reserved Only
Time-slot
1
2
3
4
5
6
7
8
VC 1
VC 2
VC 3
VC 4
VC 5
VC 6
VC 7
VC 8

## Slide 24: Mixed Deterministic and Priority/BW-Reserved
Time-slot
1
2
3
4
5
6
7
8
VC 1
VC 2
VC 3
VC 4
VC 5
VC 6
VC 7
VC 8

## Slide 25: SpaceFibre FDIR
FDIR
  Fault detection
    Parity/disparity
    Invalid 8B/10B codes
    Enhanced Hamming distance
    CRC
    Over and under utilisation of expected bandwidth
  Fault isolation
    Galvanic isolation
    Data framing – time containment
    Virtual channels – bandwidth containment
  Fault recovery
    Link level retry
    Graceful degradation on lane failure
    Babbling idiot protection
    Error reporting

## Slide 26: SpaceFibre Chips
SpaceFibre interface design
  University of Dundee and STAR-Dundee
  Funded by ESA, EC, STAR-Dundee
Designed in tandem with SpaceFibre standard specification
Used to test and validate standard
Implemented as VHDL IP Core

## Slide 27: SpaceFibre Chips
SpaceFibre VHDL IP Core
  Compliant to current version of standard
  Interfaces
    Virtual channel interface
    Broadcast channel interface
    Management interface
  QoS
    Integrated priority and bandwidth reservation
    Scheduling with 64 time-slots
  Retry
    Rapid retry
  Single lane
    Multi-lane support will be provided early 2014
Available from STAR-Dundee Ltd

## Slide 28: VHiSSI Project
  VHiSSI (Very High Speed Serial Interface) Chip
  Radiation tolerant SpaceFibre device
  Uses UoD/STAR SpaceFibre VHDL IP Core
EC Framework 7 research project
International project team:
  University of Dundee
  Astrium GmbH
  STAR-Dundee Ltd
  Ramon Chips
  ACE-IC
  IHP
  Synergie CAD Instruments

## Slide 29: SpaceFibre Chips
VHiSSI chip specification
  Fully integrated SpaceFibre interface
    2.5 Gbits/s
    Including full QoS and FDIR capabilities
    Including two SerDes: nominal and redundant
  Versatile IO
    SpaceWire to SpaceFibre Bridge
    Parallel IO modes
      Including FIFO, Memory, DMA, Transaction modes
    Ideal for simple connection to FPGA
  Small size, 20 x 14 mm
  Radiation tolerant
Prototypes in 2014

## Slide 30: VHiSSI Architecture
SpaceWire
Bridge
FIFO & DMT
Interface
IO
Switch
Matrix
Mode
Switch
Matrix
SpaceFibre
Interface
JTAG
CNF[3:0]
SpaceWire
& Digital IO
JTAG
VHiSSI Chip
SpaceFibre
Nominal
SpaceFibre
Redundant
SerDes
SerDes
…
…
…
VC0
VCA
VCB
VCJ

## Slide 31: VHiSSI Applications
SpaceWire to SpaceFibre Bridge
VHiSSI
SpaceWire
To
SpaceFibre
Bridge
SpaceWire
Instrument
SpaceWire
Instrument
SpaceWire
Instrument
SpaceWire
Instrument
VHiSSI
SpaceWire
To
SpaceFibre
Bridge
SpaceWire
Equipment
SpaceWire
Equipment
SpaceWire
Equipment
SpaceWire
Equipment
SpaceFibre
SpaceWire
SpaceWire

## Slide 32: VHiSSI Applications
Instrument interface
Mass memory interface
Instrument
Interface
FPGA
SpW
Control/HK
Instrument
Data
Output
SpaceFibre
VHiSSI
Instrument
Mass Memory
Interface
Mass Memory Unit
VHiSSI
SpW
Control/HK
Data IO
Memory
Network

## Slide 33: SpaceFibre Applications
Instrument 2
Interface
Data Output
SpaceWire
To
SpaceFibre
Bridge
SpaceWire
Instrument
SpaceWire
Instrument
SpaceWire
Instrument
SpaceWire
Instrument
Data Output
Data Output
Local Instruments
Remote Instruments
Local Instrument
Instrument 1
Interface
Data Output
Local Instrument
Data Bus
To Memory
Mass Memory Unit
Mass Memory
Interface

## Slide 34: SpaceFibre Applications
Instrument 2
Interface
SpW Control/HK
Data Output
SpaceWire
To
SpaceFibre
Bridge
SpaceWire
Instrument
SpaceWire
Instrument
SpaceWire
Instrument
SpaceWire
Instrument
SpW Control/HK
Data Output
SpW Control/HK
Data Output
Local Instruments
Remote Instruments
Local Instrument
SpaceFibre
Router
Instrument 1
Interface
SpW Control/HK
Data Output
Local Instrument
Mass Memory
Interface
Data Bus
To Memory
Mass Memory Unit
Downlink Telemetry
Interface
SpW Control/HK
Data Output
Downlink Telemetry
Control
Processor
Interface
SpW Control/HK
Data Input/Output
Control Processor

## Slide 35: STAR Fire: SpaceFibre Test Equipment
VC/BC
IF
Reg
USB
3
Router
SpW
SpW
1
2
5
6
SpaceFibre
Port 1
(8 Virtual Channels)
SpF
Analyser
Mictor
VC/BC
IF
SpaceFibre
Port 2
(8 Virtual Channels)
Reg
7
8
Analyser
SpF
Mictor
RMAP Config
(RMAP Target)
4
Configuration Bus

## Slide 36: STAR Fire Word Viewer

## Slide 37: STAR Fire Frame Viewer

## Slide 38: SpaceFibre Validation

## Slide 39: Interoperability testing Dec 2012

## Slide 40: SpaceFibre running over 100m fibre

## Slide 41: ESA SpaceFibre Beta Test Projects
Next Generation Mass Memory, Astrium (D), IDA (D)
High Processing Power DSP, Astrium (UK)
High Performance COTS Based Computer, Step 2 (Prototyping and Validation), Astrium (Fr), CGS (I)
FPGA Based Generic Module and Dynamic Reconfigurator, Bielefeld University (D)
Leon with Fast Fourier Transform Co-processor, SSBV (NL)

## Slide 42: SpaceFibre Flight Engineering Model
SpaceFibre Demonstrator activities
  Cables and Connectors
  Demonstration Board and Testing
  Simulation and Validation

## Slide 43: Conclusions
SpaceFibre designed specifically for spaceflight applications
Multi-Gbit/s
Galvanic isolation
Integrated QoS
Integrated FDIR capabilities
Compatible with SpaceWire packet level
Efficient design
Several application demonstrators
Successful interoperability testing
Formal ECSS standardisation scheduled for 2014
Radiation tolerant chips currently under development
Test equipment and IP cores available now

## Slide 44: Acknowledgements
The research leading to these results has received funding from
  The European Space Agency under ESA contract numbers:
    17938/03/NL/LvH - SpaceFibre
    4000102641 - SpaceFibre Demonstrator
  The European Union Seventh Framework Programme (FP7/2007-2013) under grant agreement numbers
    263148 - SpaceWire-RT (SpaceFibre QoS)
    284389 - SpaceFibre-HSSI (VHiSSI chip)
We would also like to thank
  Martin Suess ESA project manager

## Slide 45: Thank You Any questions?