## Slide 1
Overview of the SMAP Science Data Manager (SDM)
Ed Benowitz
SMAP FSW Developer
NASA/Jet Propulsion Laboratory
Caltech
Copyright 2013 California Institute of Technology. Government sponsorship acknowledged.

## Slide 2: Introduction
SMAP Mission Overview
  SMAP Science instruments
Science Data Management Design
  Data Flow
  Hardware View
  Storage
  Transmission
Implementation
  Interactions
  Flight Software Responsibilities
  Lines of Code
  Local Fault Protection

## Slide 3: SMAP Mission Overview1
SMAP
  Soil Moisture Active Passive
Provides global measurements of soil moisture
These measurements assist with
  Understanding of the water, energy, carbon cycles
  Improved flood prediction
  Drought monitoring
  Weather models
  Climate prediction models

## Slide 4: SMAP Movie1

## Slide 5: SMAP Instruments1
Radar (SAR)
  Higher spatial resolution but lower soil moisture accuracy
Radiometer (RAD)
  Higher soil moisture accuracy, but coarse spatial resolution
Ground software will process data from the two instruments together
  Soil moisture will be retrieved at a spatial resolution of 10 km, and freeze-thaw state at a spatial resolution of 3 km
Reflector
  Spinning at 14.6 RPM

## Slide 6: Overall Science Data Flow
Spacecraft
Command and Data Handling (CDH)
SAR
RAD
CDH
X-Band
Radio
Ground
System

## Slide 7: Inside CDH, the Hardware View
CDH
Flight Computer
Board
NVM Storage Board
Non-volatile memory
RAM
DMA Engine
instrument interfaces
X-band
interfaces

## Slide 8: Science Data Storage
NVM Storage Board
NVM
RAM
SAR instrument interface
SAR FIFO
SAR NVM
Region
DMA
RAD
instrument interface
RAD FIFO
RAD NVM
Region
DMA

## Slide 9: Science Data Transmission
NVM Storage Board
NVM
RAM
Collector FIFO
SAR NVM
Region
RAD NVM
Region
X-band
interface
DMA

## Slide 10: Science Data Interactions
Science data is never seen on the flight computer board.
  The NVM board stores, buffers, and prepares science data for transmission
  The flight software running on the flight computer board orchestrates this by commanding the NVM board
Input
  An interrupt from the SAR/RAD input fifo indicates that data has arrived
  In response to the interrupt, flight software asks hardware to DMA from the SAR/RAD input FIFO to NVM
Output
  The ground commands a transmit
  Flight software asks hardware to DMA from NVM to the collector FIFO
  An interrupt from the collector FIFO indicates that it needs more data
  In response to the interrupt, flight software asks hardware to DMA from NVM to the collector FIFO
  Repeat until there is no more data to send for this comm pass

## Slide 11: Flight Software Responsibilities
Manage simultaneous science data input and transmission
  Share usage of limited hardware DMA engines
Manage and control DMAs
  Flight software keeps track of read, write, and erase addresses within NVM
  Software uses these addresses as part of a DMA request
Provide an abstraction for science data
  Although it is implemented with DMAs, RAM FIFOs, and NVM storage
    The entire storage appears as a giant fifo in NVM
  Do not allow overwrites of old data
Keep SAR and RAD science data separate
  Each type of science data (SAR/RAD) appears as an individual stream over the transmission
  Control hardware registers and counters to identify these streams
Overlap transmitted data for ease of ground assembly
Provide commanding for transmission and retransmission of data
  Prioritize science data (SAR vs RAD) for transmit
Provide telemetry
Provide fault monitoring and responses

## Slide 12: Flash File Systems vs SDM3
NVM storage has special usage. Flash file systems must deal with these issues as well.
 | Typical Flash File System | SMAP Science Data
Blocks must be erased before being written to | Yes | Yes
Bad blocks must be avoided | Yes | Yes
Random access | Yes | No. FIFO access only.
Wear leveling | Yes | Not explicitly needed, FIFO spreads out writes.

## Slide 13: Software Stats and Info
Approximately 7K physical lines of code, 3 K logical lines of code, 3K lines of comments
SMAP’s statechart autocoder2 was used for this module
Separate files within the module deal with
  Science data input
  Science data transmission
  NVM addressing and abstraction
  Inter-process communication

## Slide 14: Local Fault Protection
Monitoring
  DMA errors
  Input FIFO errors
  Collector FIFO errors
  X-band radio is unexpectedly not functioning
Responses
  Empty a fifo
  Reset a hardware interface
  Abort a transmit command

## Slide 15: Conclusion
Keeping science data within the NVM board allows us to perform high-rate storage and transmission.
Flight software orchestrates the simultaneous hardware actions and provides an abstraction for the operations team.

## Slide 16: References
[1] http://smap.jpl.nasa.gov
[2] Murray, A.; Jones, C.G.; Reder, L.; Shang-Wen Cheng, "The use of modeling for flight software engineering on SMAP," Aerospace Conference, 2011 IEEE , vol., no., pp.1,19, 5-12 March 2011
[3] http://en.wikipedia.org/wiki/Flash_file_system