## Slide 1: Implementing SpaceWire-D in RTEMS for the AT6981 Processor
David Gibson
David Paterson, Steve Parkes, Stuart Mills

## Slide 2: Overview
Introduction to AT6981 – Castor
Supporting RTEMS on Castor
  STAR SDE support
  Porting RTEMS
Introduction to SpaceWire-D
SpaceWire-D on Castor

## Slide 3: Introduction to Castor

## Slide 4: AT6981 – Castor
Complete system on chip for spaceflight
  Powerful processor core
  IEEE 754 Floating-Point Unit
  Memory Management Unit
  Substantial on-chip memory
  Interfaces to external memory
  SpaceWire router
  SpaceWire protocol engines
  MIL-STD-1553 interface
  CAN and many more peripheral interfaces
Atmel AT6981 Castor
  90 nm technology
  Low-power, high-performance
  Radiation tolerant

## Slide 5: AT6981 Castor Architecture
SpW
Router
SpaceWire
Configuration Registers
SpW Engine
SpW Engine
SpW Engine
Switch
Matrix
Internal RAM 1
Internal RAM 2
CAN
CAN
MIL-STD-1553
SPARC V8
I-Cache
Debug Port
Internal RAM 3
MIL-STD-1553
External Memory Interface:
PROM, SRAM, SDRAM, DDRx
Debug SpW
RMAP/PnP Bus
APB Bridge
Internal RAM 4
D-Cache
Ethernet
Ethernet
Peripheral
Peripheral
Interfaces

## Slide 6: SpaceWire Engines
Offloads processor from SpaceWire communications
SpaceWire Remote Memory Access (RMAP)
RMAP Target
  Memory region or software based authorisation
RMAP Initiator
  Automatic initiation of multiple commands
DMA
  3x transmit and 3x receive channels
Protocol Multiplexer/Demultiplexer
  Detects SpaceWire or user protocol
  Multiplexes received data accordingly
Time-Code Controller
  Regular & custom time-codes, signalling codes
SpaceWire Engine 3
SpaceWire Engine 2
AHB
Interface
RMAP
Target
RMAP Initiator
DMA Channel (x3)
Protocol Multiplexer/ Demultiplexer
SpaceWire Router
Time-Code Controller
AHB

## Slide 7: Debug and Test
Comprehensive debug support
Debug support unit
  Breakpoints
  Single stepping
  Register and memory access
  Trace memory
  Hardware watch-points
Accessible via
  JTAG
  Debug UART
  Debug SpaceWire (high-speed debug)

## Slide 8: Castor Prototype Board
LEON2-FT core (40MHz)
128KB on-chip RAM
256MB DDR RAM
3 x SpaceWire engines
Router
Time-code controller
SpaceWire debug port
UART debug port

## Slide 9: Supporting RTEMS on Castor

## Slide 10: STAR SDE Overview
Supports development of software for flight processors
  Based on Eclipse IDE, using GCC toolchain
Debug over UART or SpaceWire
Custom plug-ins provide access to processor-specific features, e.g.:
  Device internal register view
  Trace buffer view
  Processor cache view
Currently supported devices:
  Atmel AT697E/F
  Atmel AT7913E (SpW-RTC)
  Atmel ATF697FF

## Slide 11: STAR SDE Castor Support
Added register address map and register information
  E.g. bit field assignments for each register
Provided device-specific libraries and linker scripts for GCC toolchain

## Slide 12: STAR SDE Castor Support
View and edit LEON2-FT register values

## Slide 13: STAR SDE Castor Support
Control and debug all SpaceWire peripherals

## Slide 14: STAR SDE Castor Support
Trace Buffer

## Slide 15: STAR SDE Castor Support
LEON Cache

## Slide 16: Porting RTEMS to Castor
Creating a BSP
  Does a BSP for this board exist?
  Does a BSP for a similar board exist?
  Is the board’s CPU supported?
Board initialisation
Device drivers
  Clock
  Console
  Other devices

## Slide 17: Features of The Castor Port
Based on existing LEON2 BSPs
Clock and console drivers
SpaceWire DMA channel driver
SpaceWire RMAP Target & Initiator driver
Other device drivers to follow…
Port to AT7913 (RTC) performed in parallel

## Slide 18: Achievable Performance
Expected performance for a 200MHz clock:
  150 MIPS, 40 MFLOPS
  Low interrupt latency (~4µs)
  SpaceWire transmit/receive up to maximum theoretical data rate (maximum link speed 200 Mbits/s)
  Three engines operating in parallel, autonomously (assuming no port contention)

## Slide 19: Introduction to SpaceWire-D

## Slide 20: Deterministic SpaceWire
Want to use SpaceWire for control applications
Determinism is essential
Determinism means:
  Predictable
  Delivery within specified time constraints
A single SpaceWire link is deterministic
A larger network, with multiple masters, is not

## Slide 21: Time-Slots for Managing Access
SpaceWire time-codes used to define time-slots
Time-slot has same number as time-code that starts the time-slot
64 time-slots
Time-Slot 6
Time-Code 6
Time-Slot 7
Time-Code 7
Time-Code 8

## Slide 22: Determinism With Time-Slots
Time-slot in 1 to 15.625 ms range (typically)
  Epoch of 64 time-slots around 0.1 to 1 second
  Allows writing/reading between 20 and 300 KBytes per time-slot
    For a 200 Mbits/s network
Sufficiently timely for avionics applications

## Slide 23: Schedule
Schedule arranged to avoid conflicting use of network resources
In a single slot can have:
  Parallel Initiators with non conflicting Targets or groups of Targets
  Single Initiator that can send commands to any Target

## Slide 24: SpaceWire-D Services
Static Bus
  Deterministic
  Transaction group
Dynamic Bus
  Not deterministic
  Transaction group
Asynchronous Bus
  Not deterministic
  Individual transactions with priority
Packet Bus
  Not deterministic
  Sends and receives SpaceWire packets using RMAP

## Slide 25: Schedule
Schedule allocates time-slots to buses
Each initiator has a copy of the schedule
Targets only respond so do not need to know the schedule
Time-Slot
0
Bus
Static 0
1
2
Dynamic 1
Static 2
3
4
Async 3
Static 4
5
6
Async 5
Async 5
7
8
Dynamic 7
Empty
9
10
Dynamic 1
Dynamic 7
11
12
Packet 11
Packet 11
13
14
Packet 11
Packet 11
…
61
…
Static 61
62
63
Dynamic 7
Static 63

## Slide 26: FDIR
Initiator can check that all transactions completed by time next time-code received
Can do this because RMAP transactions can provide acknowledgement
If an error is detected,
  Can notify network manager
  If it happens again can cease sending and notify network manager
  Etc.
RMAP, time-code and schedule provide a means of detecting faults.

## Slide 27: SpaceWire-D Summary
Provides deterministic data delivery
  Using RMAP to provide basic communications
  Operates over existing SpaceWire network
  Using existing RMAP target devices
  SpaceWire-D initiators can be implemented in software
Allows SpaceWire to be used for:
  Time critical avionics applications (e.g. AOCS)
  Concurrently with payload data handling
Draft specification under review
  Written by University of Dundee under ESA contract
  Based on requirements from industrial partners

## Slide 28: SpaceWire-D Demo System
Being developed by the University of Dundee
  Under SpaceWire-D protocol definition ESA contract
Multiple initiators
  AT6981E Castor processors
Multiple targets
  Hardware targets
  Software targets
    Castor
    AT7913E RTC processors
Test all types of “virtual bus”
Explore effective scheduling algorithms

## Slide 29: SpaceWire-D on Castor

## Slide 30: SpaceWire-D on Castor
Networking software built with RTEMS 4.10.2 and the Castor BSP
Main components:
  API for opening/loading/closing buses and setting initiator, target and system parameters
  Bus controller for executing virtual buses
  Virtual bus data structures
  RMAP initiator driver
  SpaceWire router driver

## Slide 31: SpaceWire-D System Overview
Wait for a time-code to arrive
Execute an open bus or prepare an asynchronous bus queue (explained later)
Router Driver
Time-code IRQ
Bus Controller
New time-slot
RMAP Driver
Async. Bus Queue
Send RTEMS event
Dispatch
Schedule
Check for bus
Return bus

## Slide 32: SpaceWire-D API
Provides the services described in the standard
  For each type of bus:
    Open bus
    Load bus
    Close bus
Helper functions for configuring initiator, target and system parameters and building data structures

## Slide 33: Opening a Virtual Bus
Opening a bus takes 3 parameters
  A requested slot for a static bus or a list of slots for a dynamic, asynchronous or packet bus
  A slot size if the bus needs to execute large transactions across multiple time-slots
  A list of targets that the bus is allowed to initiate with

## Slide 34: Maintaining Determinism
In order to remain deterministic, an initiator should only open a bus that will not introduce the possibility of blocking
  i.e. the paths between an initiator and the targets should not conflict with other initiator/target pairs already operating in the same time-slot
  Research into scheduling algorithms is ongoing at the University of Dundee

## Slide 35: Independent Virtual Buses
Two virtual buses with no shared links can operate in the same time-slot without blocking
INI
TAR
TAR
TAR
INI
TAR
TAR
RTR
RTR
INI
RTR

## Slide 36: Independent Virtual Buses
Two virtual buses with no shared links can operate in the same time-slot without blocking
INI
TAR
TAR
TAR
INI
TAR
TAR
RTR
RTR
INI
RTR

## Slide 37: Loading a Static or Dynamic Bus
Loading a bus differs depending on the type of bus
Static bus:
  Takes a group of transactions and an execution mode
  Single-shot mode executes a transaction group once
  Repeating mode executes the transaction group in each time-slot until the bus is unloaded or closed
Dynamic bus:
  Can load two transaction groups
    Current group, executed in the next available time-slot
    Next group, replaces the current group once it has been executed

## Slide 38: Loading an Asynchronous Bus
Asynchronous bus:
  Loaded with single RMAP transactions
  Inserted into a priority queue, first ordered by priority (0-7) then by insertion time
  In the time-slot preceding an asynchronous bus, the queue is prepared:
    Extract a subset of transactions from the queue and sum their execution times until no more transactions will fit in a time-slot
    To calculate execution time, initiator, target and system details are required such as target response time, link speeds and the number of routers in initiator/target paths

## Slide 39: Asynchronous Queue Extraction
Example queue extraction
Priority | Counter | Time (µs)
0 | 0 | 600
0 | 1 | 500
1 | 2 | 125
1 | 5 | 50
2 | 3 | 150
3 | 4 | 300
3 | 7 | 100
5 | 6 | 90
Asynchronous Queue
Extract (1ms)
Priority | Counter | Time (µs)
0 | 0 | 600
1 | 2 | 125
1 | 5 | 50
2 | 3 | 150
 | Total | 925
Extracted Transactions
+ Overheads <= 1ms

## Slide 40: Asynchronous Queue Implementation
Implemented as a min-heap
Higher priority transactions that won’t fit can be temporarily removed from the queue in favour of lower priority transactions that will fit
Ordering is based on a priority level and an insertion time so reinsertion maintains the original ordering
Preparation takes place in preceding slots to minimise initiator response time when a time-code is received

## Slide 41: Closing a Virtual Bus
When the bus is no longer required it is closed
Frees any schedule slots associated with the bus

## Slide 42: SpaceWire-D Demo System
Castor-cPCI
Castor-PCIe
Castor-cPCI
Brick
Mk2
Link
Analyser Mk2

## Slide 43: Problems Encountered
Minimising initiator response time
  First iteration used events to notify a dispatcher task when a time-code arrived
  Dispatcher then used open/ioctl/close syscalls in the RMAP driver
  This design was too slow so it was changed to
    Remove syscalls and call driver functions directly
    Remove events and initiate the first block of transactions from the router ISR (~10µs)
  Reduced the initiator response time from ~380µs to ~25µs

## Slide 44: Current Performance at 40MHz
Initiator response time measured from a time-code received until the first RMAP command leaves the router
  ~25µs
Castor RMAP target response time measured from when a command is fully received until a reply leaves the router
  ~2µs
Initiator post-processing time measured from a reply being received until the next RMAP command leaves the router
  ~7µs

## Slide 45: Summary
Castor chips will be available next year
  STAR SDE support is almost complete
  RTEMS basic support is complete
    Additional drivers will be added in future
SpaceWire-D draft specification is under review
  Presented to the SpaceWire Working Group last week
SpaceWire-D implementation and testing on Castor ongoing
Any questions?