## Slide 1: Verification and Test with Model-Based Design
Flight Software Workshop 2015
Jay Abraham

## Slide 2: The software development process
Design
Coding
Integration
Requirements
Develop, iterate and specify requirements
Create high level and low level design components
Convert design to source code (C/C++ software)
Integrate software with complete system, commence system level tests

## Slide 3: Phase where errors are found
Requirements phase
Design phase
Coding phase
Testing phase
Relative number of errors detected
Source: How good is the software: A review of defect prevention techniques; Brad Clark, David Zubrow, Carnegie Mellon Software Engineering Institute; Software Engineering Symposium 2001
Errors are typically found late in the process!
40
30
20
10
0
Latent errors may remain in the software!
Notes: http://www.sei.cmu.edu/library/assets/defect-prediction-techniques.pdf

## Slide 4: Model-Based Design
Integration (Test)
IMPLEMENTATION (Coding)
MCU
DSP
FPGA
ASIC
Structured Text
VHDL, Verilog
C, C++
PLC, PAC
DESIGN
Environmental Models
Control Algorithms
Mechanical
Electrical
Supervisory Logic
RESEARCH
REQUIREMENTS
Continuous Verification and Validation
Design
Coding
Integration
Requirements
Models that describe your design
  Executable specification
  Evaluate and test in simulation
Start finding problems early
  Before getting to code
  Before hardware is ready

## Slide 5: Modeling and simulation with Model-Based Design
Reference: http://www.flightgear.org/

## Slide 6: Modeling and simulation with Model-Based Design
Reference: http://www.flightgear.org/

## Slide 7: Simulation and modeling with Model-Based Design
Now that you are done simulating, are you done?
Can you generate code for your controller and go directly to hardware?
Could there be other bugs in your design that could be detected earlier?
Could there be hidden bugs lurking in your design?

## Slide 8: Requirement errors and their consequences
Missing or incomplete requirements
  Design may not meet customer needs
Design lacks sufficient requirements
  Design may not work as expected
Inconsistent requirements
  Design may exhibit unintended behavior
Coding
Integration
Requirements
Design

## Slide 9: Finding and fixing requirement errors early
Bi-directionally trace requirements
  From requirements to design and visa-versa
  Check that all requirements map to design components
Confirm expected behavior with simulation-based tests
  Execute simulation-based tests that map to requirements
  Identify unintended behavior or deviations
Complement testing with formal methods
  Prove that design meets safety requirements
  Use counter examples to debug design
Coding
Integration
Requirements
Design

## Slide 10: Confirm requirements map to design
Identify missing requirements!
Design components that do not map to a requirement
Indicative of incorrect design, or misinterpreting requirements
Avoid finding unintended behaviors late in project phases
Produce requirements trace reports
Tool: Simulink Verification and Validation

## Slide 11: Finding and fixing requirement errors early
Bi-directionally trace requirements
  From requirements to design and visa-versa
  Check that all requirements map to design components
Confirm expected behavior with simulation-based tests
  Execute simulation-based tests that map to requirements
  Identify unintended behavior or deviations
Complement testing with formal methods
  Prove that design meets safety requirements
  Use counter examples to debug design
Coding
Integration
Requirements
Design

## Slide 12: Execute functional tests in simulation
Define test vectors in Excel and other formats
Pass / fail results
Time series test vectors
Tool: Simulink Test

## Slide 13: Execute functional tests in simulation
Sequence based tests and assessments
Tool: Simulink Test
Requirement  In the event of an failure condition of the position sensor or low hydraulic pressure, the Fault Detection Isolation and Recovery (FDIR) application shall select the primary actuator to isolated mode

## Slide 14: Finding and fixing requirement errors early
Bi-directionally trace requirements
  From requirements to design and visa-versa
  Check that all requirements map to design components
Confirm expected behavior with simulation-based tests
  Execute simulation-based tests that map to requirements
  Identify unintended behavior or deviations
Complement testing with formal methods
  Prove that design meets safety requirements
  Use counter examples to debug design
Coding
Integration
Requirements
Design

## Slide 15: Complement testing with formal methods
Graphical representation of safety requirements for thrust reverser
Tool: Simulink Design Verifier
If average airspeed > 150knots, deploy cannot be true
If two WOW sensors are false, deploy cannot be true
If either wheelspeed sensor < 10 knots, deploy cannot be true

## Slide 16: Counter example test generation
Tool: Simulink Design Verifier

## Slide 17: Implementation errors and their consequences
Example implementation errors
  Dead logic or unreachable states
  Overflow, divide by zero, other mathematical errors
Consequences
  Incorrect operation when presented with abnormal inputs
  Design may fail catastrophically (design is not robust)
Coding
Integration
Requirements
Design

## Slide 18: Finding and fixing implementation errors early
With formal methods, prove absence of
  Dead logic or unreachable states (with model checking)
  Overflow, divide by zero, out of bound arrays (with abstract interpretation)
Coding
Integration
Requirements
Design

## Slide 19: Confirm design is free of implementation errors
Prove absence of dead logic, unreachable states
Tool: Simulink Design Verifier

## Slide 20: Confirm design is free of implementation errors
Overflow proven to occur (colored RED)
Overflow proven not to occur (colored GREEN)
Overflow and divide by zero proven not to occur (colored GREEN)
Prove absence of overflow, divide by zero, and other design errors
Tool: Simulink Design Verifier

## Slide 21: Finding and fixing implementation errors early
Test completeness of design
  Simulation-based tests to confirm design testability
  All execution paths and conditions have been exercised
  Use coverage metrics to confirm design has been fully tested
Coding
Integration
Requirements
Design
System Under Test
Coverage Report
User defined
input vectors

## Slide 22: Confirm design is fully tested
Tool: Simulink Verification and Validation, Simulink Test

## Slide 23: Generate additional tests with formal methods
Top off functional tests with generated tests
  Use model checking to explore state space
  Generate missing test-cases to execute all paths
  Tests generated for decision, condition, MC/DC, table
User defined
input vectors
Generate input vectors
Cumulative Coverage Report
System Under Test
Tool: Simulink Design Verifier, Simulink Test

## Slide 24: Consistency issues and their consequences
Design fails to meet standards compliance
  Failure to certify development process and or software
Design model and code do not match
  Functional behavior is different (e.g. timing, logic, etc.)
  Differences between floating point simulation vs. fixed point
Integration
Requirements
Design
Coding

## Slide 25: Addressing consistency issues
Check design compliance to standards
  E.g. do input signals specify min/max?
  Certification standard: ISO 26262, DO-178C
  Industry standards: MISRA®, MAAB
Equivalence testing of model and code
  Software In the Loop (SIL): test that code compiled on host computer matches simulation results
  Processor In the Loop (PIL): test that code executing on target processor matches simulation results
Integration
Requirements
Design
Coding

## Slide 26: Check model complies with standards
Tool: Simulink Verification and Validation

## Slide 27: Confirm design and code consistency
Normal mode simulation model
Code generated from model, compiled on host
Test Vectors
Compare
Execute all tests to check equivalence of model to code
Tool: Simulink Test

## Slide 28: Integrated code concerns
Code generation automates coding process
  But generated code will be integrated with other code
  Examples: driver code, RTOS services, etc.
Deployed code
  Consists of handwritten and generated code
  Important to consider the interfaces to avoid functional and robustness problems
Potential issues to consider
  Runtime errors; non initialized variables, bad pointers, etc.
Integration
Requirements
Design
Coding

## Slide 29: Finding runtime errors before production
Formal methods based static code analysis
  Gain insight into the runtime behavior of the software
  Verify code without executing the software or running tests
Confirm integrated code is robust
  Prove software free of critical bugs (with abstract interpretation)
  Find critical runtime errors
Integration
Requirements
Design
Coding

## Slide 30: Verify robustness of integrated code
Formal methods with Abstract Interpretation can prove:
  c = a + b; will never overflow
  j = arr[i]; i will always be within array bounds
  *ptr = 12; will never be an illegal dereference
  w = x / (y + z); y never equal to -z or visa versa (divide by zero)
And many more …
Integration
Requirements
Design
Coding

## Slide 31: Verify robustness of integrated code
static void pointer_arithmetic (void) {
int array[100];
int *p = array;
int i;
for (i = 0; i < 100; i++) {
*p = 0;
p++;
}
if (get_bus_status() > 0) {
if (get_oil_pressure() > 0) {
*p = 5;
} else {
i++;
}
}
i = get_bus_status();
if (i >= 0) {
*(p - i) = 10;
}
}
Green: reliable safe pointer access
Red: faulty out of bounds error
Gray: dead unreachable code
Orange: unproven may be unsafe for some conditions
Purple: violation code rules
Polyspace formal methods static analysis
Tool: Polyspace Code Prover

## Slide 32: Summary of V&V with Model-Based Design
Design
Coding
Integration
Requirements
Confirm requirements map to design
Execute functional tests, perform formal verification, generate tests
With testing, confirm model and design are consistent
Verify robustness of integrated code