## Slide 1: Spacecraft Flight Data Recording – Research to Develop Effective Guidelines Flight Software Workshop 2016 Jet Propulsion Laboratory, Pasadena CA
Mr. Daniel Balderston
Dr. James Zalinski
The Aerospace Corporation
December 14, 2016
Notes: Title Slide

## Slide 2: Topics
A Typical Spacecraft Failure Story
Problem Statement
Research Goals and Approach
Considerations
Candidate Guidelines
Way Forward
Notes: The Head is for your main idea. It should always be in Arial Black, 26 point
The Subhead is for a subordinate idea. If you don’t need it, delete the box.
The text box

## Slide 3: Once upon a time … 22,000 miles above earth
Geosynchronous communications satellite experiences severe solar event
  SEUs, SELs, bit errors in flight processors and RAM
  Processor reset, safe mode entry
Normal mode recovery uses standard procedures to regain control
  Involves cold-start of flight processor to clear latched-up electronics
Post-event anomaly diagnosis
    Abrupt telemetry interruption, no precursor indicators were seen
    RAM was cleared by cold-start, no clues available
    Full FMECA process is exercised to identify root cause with confidence
      Limited by data available from time of event
After failure review concludes, normal operations continues
  Signature of failure and recovery steps are captured for rapid recovery next time
Subsequent solar events occur, with similar but different symptoms
  Requires fresh FMECA review to ensure root cause determined
> Shortening the time to find root cause will enhance availability (MTTR), … and may save the mission
Normal Ops
Diagnose
Recover
Normal Ops
Diagnose
Recover
Notes: The Head is for your main idea. It should always be in Arial Black, 26 point
The Subhead is for a subordinate idea. If you don’t need it, delete the box.
The text box

## Slide 4: Problem Statement
FMECA analysis typically drives required data recording for on-orbit detection and recovery, and post-event failure diagnosis
However, best efforts often fall short of capturing unexpected events
Consequences can include on-orbit failure or fail-safe events
  Processor resets
  Backup processor failover
  Safe mode entry
  Processor hang without recovery option
Post-event determination of root cause, recovery and long-term remedy requires high-confidence analysis of system conditions prior to the failure
  Relies on capture, retrieval and analysis of post-event data captured
Flight data recording for unanticipated faults is often more an art than engineering discipline
> The ability to determine root cause in a timely fashion fully depends on diagnostic information available after the event occurs
Notes: The Head is for your main idea. It should always be in Arial Black, 26 point
The Subhead is for a subordinate idea. If you don’t need it, delete the box.
The text box

## Slide 5: Research Goals and Approach
Goals
  Develop and compile: “General guidelines for flight software on-board data recording.” to provide recoverable forensic data for post-event analysis of unanticipated / unexpected anomalies and failures.
Approach
  Focus on more frequent events: (e.g., flight processor resets)
  Assess real-world anomalies, failures and successful recoveries
  Identify existing guidelines, standards, practices, and deficiencies
  Include major levels of spacecraft and software architectures
  Include guidance for mission risk-classes
  Propose a general engineering methodology
  Publish findings, best practices and effective guidelines.
Normal Ops
Diagnose
Recover
Normal Ops
Diagnose
Recover
Normal Ops
Normal Ops
Normal Ops
Notes: The Head is for your main idea. It should always be in Arial Black, 26 point
The Subhead is for a subordinate idea. If you don’t need it, delete the box.
The text box

## Slide 6: Considerations – Architecture Elements
Address FSW data recording to support unanticipated anomalies at all spacecraft architecture levels and elements
  Application Level - Spacecraft bus
    Bus FSW Subsystems
  Application Level – Payload
    Payload Flight Software subsystems (per each payload)
  Real-time Operating System (RTOS) and services layer
    Resource management, scheduling, memory management, file system
  Hardware Interface Level (Processors, Data Bus)
    Bootloader
    Board Support Package
    Discrete inputs, power and reset signals
    Registers, cache memory, stack pointers, device controllers
  Data Bus attached components
Notes: The Head is for your main idea. It should always be in Arial Black, 26 point
The Subhead is for a subordinate idea. If you don’t need it, delete the box.
The text box

## Slide 7: Considerations – Key Trade Offs
What to record?
  Safe mode, reset and related control triggers (digital, analog)
  External, internal messaging (e.g., data bus traffic)
  Watchdog timer and other failsafe mechanisms
  Interrupt and exception handling events
Where to record?
  Persistent vs. volatile memory (RAM, SDRAM, EEPROM)
  External recording capabilities (SSR, payload, etc.)
  Auxiliary or support memory (NIC card, adjunct processor / memory)
How to record ?
  Within FSW tasking (housekeeping and state-of-health task
  Adjunct tasking under FSW, services or RTOS
How much to record?
  Available memory vs. depth of information vs. length of recording time
How to retrieve after event
  Safe mode downlink capability
  Normal TLM vs. alternate (diagnosis) scheme, compression
> Cost-Benefit-Risk trade-offs for your program must be made
and understood to proceed!
What
?
Where ?
How
?
Recording requirements for my program
Notes: The Head is for your main idea. It should always be in Arial Black, 26 point
The Subhead is for a subordinate idea. If you don’t need it, delete the box.
The text box

## Slide 8: Candidate Guidelines
Tenets (to be applied)
  Data must be recorded to prove or exonerate all FMECA conditions (fishbones)
  Data must be readily retrievable during safe mode or post-event recovery
  Data recording must be inherent to FSW and avionics design
General Engineering Guidelines (to be tailored)
  Establish program risk tolerance (i.e., Mission Risk Class)
  Include data recording requirements for all anticipated and unanticipated failures in system, FSW and Fault Detection and Correction (FD&C) elements
  Verify all defined recording requirements where implemented
  Verify and validate retrieval requirements (component level and end-to-end)
  Exercise (validate) unanticipated failures as practicable through component-level structured stress testing
  Incorporate data recording and retrieval, signature determination, Operating Procedure update activities into overall FD&C strategy
Implementation Guidelines (to be adapted, HW dependent examples)
  Record discrete HW Reset signal interrupts on ( XYZ Processor) to SDRAM on ISR entry
  Record last (TBD minutes) of MIL-STD-1553 traffic to SSR device
  Safe Mode recovery process shall allow SCP SDRAM and EEPROM memory peek and poke commands
Examples
Notes: The Head is for your main idea. It should always be in Arial Black, 26 point
The Subhead is for a subordinate idea. If you don’t need it, delete the box.
The text box

## Slide 9: Way Forward
Engage willing and able stakeholders
  Primarily spacecraft contractors and their FSW engineers
  Flight processor manufacturers, RTOS vendors, component providers
  Mission assurance partners (FFRDC, Academia, other)
  Sponsor / customers (for concurrence and support)
Find forum for collecting, assessing, vetting and publishing guidelines
  This FSW Workshop
  Aerospace Mission Assurance Improvement Workshop (MAIW)
  Spacecraft Anomalies and Failures Workshop
  Maintain active community, participation
Publish biennial TOR or guidebook
If practicable, provide federated access to reference repositories
  Code examples, briefings, anomaly recovery data packages
The Key to Success: Information sharing for the benefit of space community
Notes: The Head is for your main idea. It should always be in Arial Black, 26 point
The Subhead is for a subordinate idea. If you don’t need it, delete the box.
The text box

## Slide 10: Related Publications and Events
TOR-2009(8591)-14 Effective Fault Management Guidelines S. Hogan et. al., Aerospace Corporation, 2009
TOR-2011(8591)-21 Mission Assurance Guidelines for A-D Mission Risk Classes
G. Johnson-Roth, Aerospace Corporation, 2011
TR-2013-00093 Recommended Satellite System Safe Mode Requirements
C. Sather et. al., Aerospace Corporation, 2013
ITAR Controlled
Spacecraft Anomalies and Failures Workshop (SCAF)
http://www.aerospace.org/education/technical-workshops/2016-spacecraft-anomalies-and-failures-workshop/
(See also Integrity-Applications Incorporated for SCAF Workshops in 2015 and prior)
Notes: The Head is for your main idea. It should always be in Arial Black, 26 point
The Subhead is for a subordinate idea. If you don’t need it, delete the box.
The text box

## Slide 11: Acronyms
Acronym | Definition
EEPROM | Electrically erasable programmable read-only memory
FD&C | Fault Detection and Correction
FFRDC | Federally Funded Research and Development Center
FMECA | Failure modes, effects and criticality analysis
FSW | Flight Software
ISR | Interrupt Service Routine
MTTR | Mean-Time-To-Recovery (Remedy)
RAM | Random Access Memory
SCP | Spacecraft Processor
SDRAM | Synchronous dynamic random-access memory
SEU | Single Event Upset
SEL | Single Event Latchup
SSR | Solid State Recorder
TLM | Telemetry
TOR | Technical Operating Report
TR | Technical Report
Notes: The Head is for your main idea. It should always be in Arial Black, 26 point
The Subhead is for a subordinate idea. If you don’t need it, delete the box.
The text box

## Slide 12: Thank you