## Slide 1: Concepts for the Mars 2020 Rover Onboard Scheduler
Eddie Benowitz
© 2016 California Institute of Technology. Government sponsorship acknowledged.

## Slide 2: Agenda & Thanks
Background/Introduction
Plan
Activity Types
Activity Attributes
More Features
Thanks to
  Stephen Kuhn
  Gregg Rabideau
  Elyse Fosse
  Glenn Reeves
  Steve Chien
  Steve Scandore
  Marcel Schoppers
  Corey Harmon
Planner Team
  Gregg/Eddie

## Slide 3: Background
Mars 2020 Rover
  Leverages heritage from Curiosity
  Will collect core samples of rocks and soils and set them aside in a "cache" on Mars.
http://mars.nasa.gov/mars2020/
(Above picture is from this web site)

## Slide 4: Terminology
Sequence
  A file containing a list of time-ordered commands
Sleep
  At night, we shutdown the rover to recharge
Preheating
  Heating up an actuator so that it is warm enough to safely use
Parameter
  A saved value this is only changeable by ground command.

## Slide 5: Prior Process on the Curiosity Rover
Any action taken by the rover is directed by a series of sequences
The process of creating sequences can take over 9 hours
Due to uncertainty, the operations team had to insert margin for duration estimates
  Resulting in wasted time and energy onboard
Can’t take advantage of onboard knowledge of available power and time
  If a sequence finishes early or fails, time is usually wasted
The operations team has to manage sleep activities and preheat activities

## Slide 6: Onboard Planner Overview
Goals
  Improve Operations Efficiency
    Run more activities onboard
    Less wasted resources (time, energy)
  Allow the ground to generate uplink products within 5 hours from receiving spacecraft data
Vision
  The onboard planner autonomously
    Runs more activities when more power is available
    Starts the next activity sooner, if the current activity finishes early
    Decides when the rover goes to sleep
We are just starting to prototype
Today, we’ll share some thoughts on planner features appropriate for a Mars rover.
Notes: This is not a planner in the AI sense. It is more of a scheduler.

## Slide 7: Onboard Planner Overview
Planner is responsible for scheduling all onboard execution on the surface
  Using the existing sequence engine underneath
What the planner does
  Reads a plan file
  Determines resource values in the future
  Checks for conflicts
  Decides when activities can run
1:00 | 2:00 | 3:00 | 4:00
 |  |  | Activity5
Activity1 |  | Activity3 | 
 | Activity2 |  | Activity6
 |  | Activity4 | 
Plan File
Onboard Planner
Ops Team
creates
gets
uplinked
Chart: 
 | 1 | 2 | 3 | 4 | 3 | 2 | 6 | 7 | 8 | 4 | 4 | 4 | 4
A schedule of when activities can run
Predicted power,
Predicted data volume
predicts
schedules
constrains

## Slide 8: Plan - Definition
Plan file: What is uplinked from the ground to the spacecraft
A plan consists of activities
A plan also contains
  Handover time
  Handover minimum state of charge
  Next plan filename
  End time
  Maximum delta data volume

## Slide 9: Activity Types

## Slide 10: Activity
Activity definition: The item that is scheduled
Activity Attributes
  Type
  Unique activity id
  Sequence
  Priority
    Priority range is divided into mandatory and optional ranges

## Slide 11: Activity Types
Generic Activity
  Most common type of activity
  Runs a sequence
  Has a fixed duration
Expanding Activity
  Has a variable duration
    Recall generic activities have a fixed duration
    The minimum duration is specified by the ground
  Typical use case is a drive
  Planner determines when the activity can end based on available resources and constraints

## Slide 12: Activity Types
Single Selection Groups
  A group of activities
  At most one of the activities in the group is allowed to be scheduled
  Purpose: If the most resource intensive activity in a group does not fit, run a less intensive activity instead.
Stay Awake Activity
  Prevents the planner from automatically shutting down the computer during this time period
  A ground-created activity

## Slide 13: Activity Types: Shutdown Related Activities
Categories of shutdown-related activities
  Planner
    Automatically generated by the planner
  Manual
    Included in the plan file by the ground
Each category has 3 phases
  Shutdown
  Sleep
  Wakeup
Planner Shutdown Activity | Planner Sleep Activity | Planner Wakeup Activity

## Slide 14: Communication Window Activities
Communication (Comm) windows are created by heritage commands.
The planner queries the communication behavior manager to become aware of, and plan around comm windows.

## Slide 15: Activity Attributes

## Slide 16: Modeled Activity Attributes
Modeled by the ground team
Uplinked from the ground as part of the plan file for each activity
Activity Attributes
  Duration
  Marginal energy usage
  Peak Power usage
  Delta data volume
  Max number of sequence engines used

## Slide 17: Activity Time Ranges
An activity has multiple tuples containing
  Start time range
  Cutoff time
In other words, an activity has multiple start time ranges
For example:
  Activity A can only start between
    10:00 -11:00 or 1:00 - 2:00

## Slide 18: Activity dependencies
An activity can have dependencies on prior activities
Example: B can only start after A has successfully completed
The dependency has the following attributes
  Prior activity’s id
  Prior activity’s status (COMPLETED, SUCCEEDED, FAILED, ABORTED, …)
An activity cannot be scheduled unless the dependency is satisfied
A
B
SUCCEEDED
dependency
Notes: Meets = continuity

## Slide 19: Constraining Parallelism
Sometimes we want to constrain activities so that they do not run in parallel.
  For example, we don’t want to drive while we move the mast (rsm)
Activities the have the same resource usage bit set cannot be scheduled to run in parallel
Resource usage bits will be specified for each activity by a future ground tool
Many (~100) extra resource usage bits are available for ground-defined meaning
  Ground can prevent arbitrary sets of activities from running in parallel.
These activities cannot be scheduled in parallel because they have the same resource bit set
time
1:00 | 2:00 | 3:00 | 4:00
Notes: Idea:
  Schedule activities onboard in advance such that arb would not encounter a conflict.

## Slide 20: Preheat and Thermal zones
Preheat definition: Heating up an actuator so that it is warm enough to safely use
Each activity can contain
  A list of the thermal zones the activity uses
The planner must autonomously generate preheat activities for a given activity that specifies thermal zones
Preheat activities are not uplinked as part of the plan
Planner must not dispatch the activity unless zone is ok to use
Preheat
Primary Activity

## Slide 21: ACM and DDIs
An activity may contain multiple ACM and DDI constraints
  ACM: A saved onboard variable typically allowing or precluding some action
  DDI: An unsaved onboard variable
Because ACM and DDI values can change, they are only evaluated when assessing whether an activity can be immediately dispatched
ACM/DDI constraints are not evaluated for scheduling future activities

## Slide 22: More Features and Definitions

## Slide 23: Limiting Data Storage Usage
Project the modeled delta data volume generated by each activity into the future
Use actual delta data volume for all activities in the past
Do not schedule optional activities that would push us over the plan-specified maximum delta data volume.
  Mandatory activities are allowed to push us over
The planner is not involved with tracking data stored on instruments

## Slide 24: Predicting Future State of Charge
Knowns
  For each uplinked activity, the plan file tells us
    Activity’s marginal average power (W)
    The activity’s duration (sec)
  Planner-generated activities get marginal avg pwr (W) and duration (sec) from parameters and tables
  Base marginal average power (W) when no activities are running is known from parameters
  Present state of charge estimation gives us
    The present estimate of the charge in the battery (W-hours)
    The estimate of the total battery capacity (W-hours)
Consumption (W-hours) is
  = consumption (W-hours)

## Slide 25: Peak Power Check
Each activity has an attribute giving its peak power usage
Activities cannot be scheduled in parallel if the total peak power usage is above a threshold (W).
The threshold is a parameter.

## Slide 26: Uses of State of Charge in Scheduling
Soft min state of charge parameter
  Optional and mandatory activities are not scheduled if they would cause a violation
  Mandatory are allowed to execute past if already dispatched
Hard min state of charge parameter
  Any currently running activities that violate are aborted
Handover state of charge plan constraint
  Optional activities are not scheduled if they would cause a violation
  Mandatory are allowed to be scheduled if they would cause a violation

## Slide 27: Planner Initiated Shutdown
Criteria
  Minimum sleep duration (parameter)
  Minimum awake duration (parameter)
  No activities could be scheduled during the proposed sleep
    Without violating the minimum state of charge (parameter)
  No optional activities could be scheduled during the proposed sleep
    Without violating the handover state of charge plan constraint
  To improve long-term battery health
    Do not sleep past maximum_state_of_charge (parameter)

## Slide 28: Cleanup Activity
A generic activity with a dependency that a prior activity finished with failure (aborted or completed with failure)
  Contains a sequence from the ground
    Establishes a known state
For most activities, execution of a cleanup is off-nominal

## Slide 29: Abort
The planner aborts an activity when
  Activity has not finished by its absolute cutoff time
  Activity is running when we hit the hard state of charge limit (parameter)
  An optional activity is running past the soft state of charge limit
  An optional activity is running past its duration
The effects of an abort
  The activity’s state changes to ABORTED
    This allows the planner to schedule a cleanup activity if present

## Slide 30: Conclusion
Showed features needed to do onboard scheduling for a Mars rover
  In particular, power estimation, sleeping, and pre-heating
Discussed some relevant constraints that will be evaluated onboard
Showed an enabling set of knowledge that needs to be uplinked from the ground
We hope the planner improves the Mars 2020 mission by
  Enabling more activities to run onboard
  Better utilizing onboard resources, such as time and energy
  Reducing the workload of the ops team with autonomous sleeps and preheats
Future work: Planner prototyping effort
  Determine RAM and CPU usage