## Slide 1: Benefits of a Virtual SIL
December 13-15, 2016
Brian Engelkemier, Chris Mason
Spacecraft FSW 16
This presentation does not contain ITAR restricted information

## Slide 2: Why Invest In The Virtual Systems Integration Lab (VSIL)
System Test Benches With Real Hardware Expensive And Limited
Demand For Access To Test Benches From Many Groups
  Hardware Verification Teams, Software Teams, Integration & Test Teams
Schedule Continually Pushed To The Right
  Hardware Taken Away At Various Points In Lifecycle
Bench May Not Have All Hardware Of Real System
  FSW and Test Environment Must Handle This
Virtual Platform
Payload |  | 
Single Board Computer | External Interface | Processor Board
Embedded Software

## Slide 3: What Is The VSIL?
Hardware Simulation Using Wind River Simics
  Runs Unmodified Software Binaries
Simulates Hardware From Software Viewpoint
Provides Each User Their Own Platform On Their Desktop PC
  Flight Software, Test Software, I&T, Hardware Verification Team
About 4 FTEs For 6 Months To Get Basic VSIL Running For FSW Team
Virtual Platform
Virtual Payload |  | 
Single Board Computer | External Interface | Processor Board
Simics Model
Simics Model
Simics Model
Virtual Platform
Payload |  | 
Single Board Computer | External Interface | Processor Board
Embedded Software

## Slide 4: Simics: The technology which enables the VSIL
Model Library
Virtual Platform
Full System Simulation Tool For Software Development
  Models All Boards In System
Simics Core Runs On Desktop Windows PC
No Custom compile Switches Necessary!

## Slide 5: VSIL Provides Better FSW Development Environment
Virtual Platform
Virtual Payload |  | 
Single Board Computer | External Interface | Processor Board
Simics Model
Simics Model
Simics Model
Kernel, BSP, Device Driver and FSW Development Environment
  Simics Models Target CPU
  Accurate Hardware Environment
  Model Runs All Software Without Modification
Allows Debugging By Stopping The Entire System
  All Threads Stop Running
  Hardware Stops Running -- Interrupts Stop
  Examine State of Software AND Hardware
Reverse Execution Of System
Within 2 Hours Determined Root Cause For Random Crash Plaguing Team For 6 Months

## Slide 6: VSIL Provides Environment For Fault Detection And Insertion
Virtual Platform
Virtual Payload |  | 
Single Board Computer | External Interface | Processor Board
Simics Model
Simics Model
Simics Model
Add Extra Checking In Board Models
  Board Interactions Controlled By FSW
  Timeline Verification
Insertion Of Faults From Hardware Boards
Insertion Of Flash Memory Faults Without Destroying Real Flash
  Able To Insert Block Level Recoverable And Non-Recoverable Errors
  Exhaustively Test Detection Of Errors, Fail Over, And Recovery Process

## Slide 7: Moving Schedule To Left
Primary Selling Point For Investment Was Need To Gain Schedule
Tracked By Cost Avoidance
  Compared Hardware Availability And Use To Real VSIL Usage
    Hardware Shared Among Teams And Team Members
  VSIL Actual Hours Then Projected Onto Hardware Availability
  Number Of Additional Weeks Required For Same Work
  Per Week Cost Of Team For Additional Work
ROI + 100% Within 6 Months

## Slide 8: Northrop Grumman ATLA2S Testing Framework
ATLA2S Is A Reusable Framework For Testing
  Performance Testing
  Functional Testing
  Calibration
  Used For Software, Hardware And System Verification
ATLA2S Provides
  Control Of Specialized Test Equipment (STE)
  Control Of Unit Under Test (UUT)
  “One Touch” Control For All Activities
  Automated Pass/Fail
Captures And Archives
  STE Telemetry
  UUT Telemetry
  UUT Output
  Results Of All Activities
Operator
STE
ATLA2S
Data
Mgmt
UUT

## Slide 9: Why Use ATLA2S With VSIL?
Provides A Resource For Many Other Engineering Disciplines
  System and FSW Test Script Development
Capture Output Of All Tests To Track Problems
Hundreds Of Existing Testing Scenarios
  Functional And Performance Tests
Operator
STE
Data
Mgmt
UUT
ATLA2S

## Slide 10: Integrating ATLA2S With The VSIL
Remove STE From ATLA2S Configuration
  Already Handles Missing STE
Replace UUT With VSIL
Change Bus Emulator for Missing 1553 Hardware In Test Set
  Messages Sent Into VSIL Model To Place in 1553 Hardware
Operator
STE
Data
Mgmt
UUT
ATLA2S

## Slide 11: Why Use ATLA2S With VSIL? (The Real Reason)
Release Rhythm (For FSW And TSW Teams)
  Weekly or Fortnightly Engineering Build and Regression Tests
    Engineer Coming In At 2 am To Run Tests Because Of Test Bench Availability
  Monthly Release Build And Full Regression Testing
Replace With Nightly Automated Testing
  No Concern About Damaging Limited, Expensive Hardware
Change ATLA2S For Headless Operation
  Command Line Parameters
Operator Replaced By Jenkins (https://jenkins.io/)
Jenkins Logo Courtesy of https://jenkins.io/
Operator
STE
Data
Mgmt
UUT
ATLA2S

## Slide 12: Implementing Automated Testing
Part Of Nightly Build Processing
Runs On Multiple Baselines
Created Spreadsheet Interface To Add Tests
Subset Run Nightly
Full Set Run Every Weekend
Developers Emailed Results Every Morning
Jenkins Logo Courtesy of https://jenkins.io/)
Check In Code
Build
Deploy
Test
Report
STE
Data
Mgmt
UUT
ATLA2S

## Slide 13: Other Benefits
Earlier Integration With HW
  New Programs Starting To Have FPGA Designers, Model Developers and FSW Team Define Model Behavior
  Hardware Engineers Developing Acceptance Tests Earlier
  FSW Running On Hardware Before Hardware Available
Virtual Payload |  | 
Single Board Computer | External Interface | Processor Board
Simics Model
Simics Model
Simics Model

## Slide 14: Summary of Benefits
Better Development Environment
Accurate Hardware Environment
Reduce Cost and Schedule
Reduce Hours Needed On Limited and Expensive Hardware
Increase Reliability
Automated Unit, Regression, And Functional Tests
Kernel, BSP, Device Driver and FSW Development
Fault Insertion Not Previously Possible
Stop Entire System For Debugging
Reverse Executions
Useful for FSW, TSW (FSW Scripts), Integration & Test, Hardware Acceptance Test Development
Start FSW Development Before Hardware Available
More “Test Like You Fly” Testing
Full Payload Always Available
Fault Insertion

## Slide 15: Lessons Learned
Start Small In Model First
  Start With Just What FSW Requires
  Increase To Include Data Payload Processes
Still Doesn’t Replace Full Payload
  First Access To Full Payload Resulted In Minor Number Of Problem Reports
VSIL Introduces Second Source Of Bugs
  Problem Seen On Real Hardware -- Why Wasn’t Problem Seen In VSIL?
Iterate On Timing Of Model
  Board Models Need Provide Consistent Timing To Match Real Hardware