## Slide 1: Introduction to Deos/RTEMS: A FACE Safety Base Operating System Solution
Gedare Bloom Howard University
Joel Sherrill
OAR Corporation
Gary Gilliland
DDC-I, Inc.
FSW 2016
Pasadena CA

## Slide 2: Open Group Future Airborne Capability Environment (FACE)
Aviation-focused professional group formed in 2010 to define an open avionics environment
"Voluntary Consensus Standards Body" as defined by the National Technology Transfer Act and OMB Circular A-119
  Facilitates US government participation
Approximately 90 member organizations
Promotes a competitive open market of portable and reusable software components
http://www.opengroup.org/face/consortium

## Slide 3: FACE Architecture

## Slide 4: FACE OSS Profiles
Profile | Multi-process | Multi-threaded | ARINC 653 | Number of POSIX Methods
Security | No | Yes | Yes | 136
Safety Base | No | Yes | Yes | 246
Safety Extended | Yes | Yes | Yes | 335
General Purpose | Yes | Yes | Optional | 812
Profiles are designed for different levels of criticality
Smaller profiles reflect RTOS configurations that have passed safety certification reviews

## Slide 5: Example Differences Between FACE OSS Profiles
General Purpose is only profile to include:
  stdin, stdout, and stderr
  wide character support
  full math library
Safety Base is typical of many embedded systems
  does not allow deletion of objects or free()
  application likely to never exit
Security is typical of information gateways
  does not include FILE * methods
  focus is device I/O

## Slide 6: FACE Safety Base: ARINC 653 Requirements for Conformance
ARINC 653 Part 1: All services associated with Avionics Application Software Standard Interface Part 1 – Required Services
Services associated with the following categories of Avionics Application Software Standard Interface Part 2 – Extended Services:
  File System
  Sampling Port Extensions
  Memory Blocks
Satisfied by Deos653 Runtime Library

## Slide 7: FACE Safety Base: POSIX Requirements for Compliance
FACE Safety Base POSIX profile has 246 APIs
Initial audit of RTEMS identified 8 missing methods. Most of these have subsequently been added:
POSIX API Function | Status
pthread_condattr_getclock() | Added. Available at rtems.org.
pthread_condattr_setclock() | Added. Available at rtems.org.
mmap() | To be added to git master December 2016
shm_open() | To be added to git master December 2016
pthread_setschedprio() | Added. Available at rtems.org.
posix_devctl() (per POSIX 1003.26) | Under development
pthread_getconcurrency() | Added. Available at rtems.org.
pthread_setconcurrency() | Added. Available at rtems.org.
Satisfied by RTEMS

## Slide 8: Status of RTEMS vs. FACE POSIX Security Profile
Header Missing Methods (with networking)
devctl.h posix_devctl
sys/mman.h shm_open
Number of POSIX Methods | RTEMS - no networking | RTEMS - with networking
161 | 142 methods or 88% | 159 methods or 99%
Subset of Profile Targeted for FACE Conformance

## Slide 9: Status of RTEMS vs. FACE POSIX Safety Base Profile
Header Missing Methods (with networking)
devctl.h posix_devctl
sys/mman.h shm_open
Number of POSIX Methods | RTEMS - no networking | RTEMS - with networking
249 | 227 methods or 91% | 247 methods or 99%
Profile Targeted for FACE Conformance

## Slide 10: Status of RTEMS vs. FACE POSIX Safety Extended Profile
Header Missing Methods (with networking)
devctl.h posix_devctl
spawn.h all 9
sys/mman.h shm_open
Number of POSIX Methods | RTEMS - no networking | RTEMS - with networking
335 | 302 methods or 90% | 324 methods or 96%
Will Align With Profile but Is Limited to a Single POSIX Process

## Slide 11: Status of RTEMS vs. FACE POSIX General Purpose Profile
Header Missing Methods (with networking)
devctl.h posix_devctl
fenv.h all 11
inttypes.h imaxdiv, wcstoimax & wcstoumax
math.h acoshl, acosl, asinl, atan2l, atanhl, coshl, erfcl, exp2l, expl, expm1l, fdiml, fmodl, frexpl, ilogbl, ldexpl, lgammal, llroundl, log10l, log1pl, log2l, logbl, logl, lroundl, modfl, nextafterl, nexttoward, nexttowardf, nexttowardl, powl, remainderl, remquol, scalblnl, scalbnl, sinhl, & tgammal
spawn.h all 21
sys/mman.h mlock, mlockall, msync, munlock, munlockall, shm_open, & shm_unlink
sys/select.h pselect
sys/socket.h sockatmark
unistd.h confstr
Number of POSIX Methods | RTEMS - no networking | RTEMS - with networking
815 | 682 methods or 84% | 734 methods or 90%

## Slide 12: FACE Conformance Challenge
FACE Safety Base Conformance requires both ARINC 653 and POSIX interfaces
RTEMS had robust POSIX support, no ARINC 653
Deos had mature ARINC 653 support, no POSIX
Neither alone was capable of meeting the requirements for FACE Safety Base

## Slide 13: FACE Conformance Approach
  Address technical requirements
    Deos provides the ARINC-653 interfaces
    RTEMS provides the POSIX interfaces
  Provide robust, mature combined solution
    Deos has 18 years of certification experience
    RTEMS has 27 years of RTOS experience in space and military domains
Deos+RTEMS leverages strengths of both RTOSs to satisfy the FACE Safety Base OSS profile

## Slide 14: Deos+RTEMS FACE Concept
Portable Components Segment
Transport Services Segment
I/O Services Segment
Platform-Specific Services Segment
ARINC-653
Runtime
Health Monitoring
POSIX
Runtime
Certifiable
Real-time
Operating System
TM
OS
OS
OS
OS
IO
TS
TS
Device Driver
Operating System Segment
Device Driver
Notes: Operating System Segment (OSS)
Input/Output Services Segment (IOSS)
Platform-Specific Services Segment (PSSS)
Transport Services Segment (TSS)
Portable Components Segment (PCS)

## Slide 15: Deos High-Level Architecture
Target Hardware
Target Software
User Mode Device Drivers
Network
Application 2
Partition 5
Partition 4
Platform hardware
(RAM, flash, timer, interrupt)
CPU
Application 1
Partition 3
Partition 2
Partition 1
Deos kernel
Registry
PAL
I/O
Interrupts
Application hardware
(I/O devices, Serial buses, etc)
I/O
Interrupts
Ethernet chipset
Driver library
Graphics chipset
Graphics
User Space
Kernel Space
Driver library
Driver library
USB
CAN
Driver library
Audio
RAM
Notes: Deos is a fully modular micro-kernel architecture. The Deos kernel is a module that is dynamically linked with other components to provide the functionality of the system.
The Hardware Abstraction layer provide CPU family interface to the kernel.
The Platform abstraction layer provide the interfaces to the platform hardware required for the kernel, timers, memory and interrupt controller.
The registry is the personality of the system. It is an input file that defines the resource allocation for all components of the system.
Note that this is all the code that is required to run in Kernel space, the rest of the software including the device drivers run in User space.
With Deos, we note that most device drivers execute in user mode, rather than in kernel mode as is the case with many other RTOS’s. Consequently, the design assurance level (DAL) of device driver software only has to be as high as the partition or process that it is a part of.

## Slide 16: RTEMS High-Level Architecture
Notes: In this figure, we see the layered architecture of RTEMS along with highlights of the functionality it supports.
Starting at the bottom of the figure, we see that the lowest level of RTEMS. This is the CPU dependent portion of the SuperCore together with CPU dependent libraries, the peripheral chip library libchip, and your custom BSP combine to provide the foundation for all RTEMS services.
In the middle, we see the various threading and synchronization APIs supported by RTEMS including the Performance Monitoring services and SAPI which includes configuration and initialization support.
In the top third of the figure, we see higher level functionality including the TCP/IP stack and associated services (e.g. httpd, telnetd, ftpd, etc) along with various open source libraries and graphics packages that have been ported to RTEMS. RTEMS supports Ada95 and Ada05 by providing a run-time and binding packages for the GNU Ada (GNAT) compiler. RTEMS supports a variety of remote debugging by providing a number of target resident debugger stubs for gdb providing both serial and network based debugging. Finally, we see the variety of optional file systems that RTEMS supports including an In Memory File System (IMFS), DOS/FAT file system, NFS client, and Device only file system. The TAR file system is the ROM-based file system for RTEMS.

## Slide 17: Deos+RTEMS Architecture
Target System Hardware and CPU
PAL
Deos Registry with WAT
Deos Kernel
User
Kernel
RTEMS/Deos Adapter
POSIX User Executable
POSIX API Library and scheduler
POSIX Partition
Deos 653 Partition
Shared Memory
Deos RMA Process
Shared Memory
IOI Lib
653 User Executable
ARINC 653 P1 API and scheduler
IOI Lib
TCP/IP (LWIP)
User Executable
Deos API

## Slide 18: Integration Challenges
Adapt RTEMS for paravirtualized environment
  Always assumes kernel mode even in user app
  Device driver responsibility shared by (user) BSP
  Ensure behavior and performance maintained
  Solution: Add Deos paravirtualization adapter which uses Deos for supervisor mode services and IO
Add missing POSIX services
  Really a conformance need. If they had been used by apps, RTEMS would have already had them
  Solution: Implement the missing services

## Slide 19: Integration Challenges
Development Tools
  RTEMS: GNU tools on *NIX and Windows
  Deos: GNU tools on Windows Eclipse-based IDE
  Solution: Provide pre-built RTEMS tools which are integrated into Open Arbor on Windows
Performance
  Concern: Does the combined environment suffer?
  Solution: Deos was unmodified and maintains its certification package. Other than interrupt disable, RTEMS compiles to the same assembly instructions as on bare hardware

## Slide 20: Paravirtualizing RTEMS
Remove protected/sensitive instructions
  Replaced interrupt enable/disable with hypercalls in paravirtualized BSP
  Address use of protected instructions in newlib
  RTEMS now has paravirtualized support for:
    x86, PowerPC, SPARC
Deos/RTEMS available for:
  x86, PowerPC
Other architectures including ARM possible

## Slide 21: Time Management
Partitions lack accurate global time knowledge
Need to track passage of time in RTEMS partition
Approach
  Consume entire partition budget – never yield
    Good design choice for real-time
  Use Deos “time budget exceeded exception” to calculate time consumed outside of RTEMS
  Query Deos for uptime to mark start of each RTEMS partition scheduling window
  Also get uptime in clock driver for elapsed time within a window

## Slide 22: ARINC 653 and POSIX Scheduling
Partition
A
Partition
B
Partition
A
PA1
PB1
PB2
Partition
C
PD2
PA2
PA2
Major Frame
Scheduling of 653 processes or pthreads
Scheduling of POSIX threads
PA3
TC1
TC2
RTEMS POSIX
ARINC
653
ARINC 653
ARINC
653
Partition
C
Partition
D
ARINC 653 Processes scheduled ARINC 653 partitions.
POSIX threads scheduled by RTEMS in POSIX partitions.
Deos kernel schedules partitions
TCP/IP
PD1
RMA
Threads
Scheduling of RMA threads
RTEMS POSIX
TC1
TC2
TC3
TC3
TC2
RTEMS POSIX
Scheduling of Exception Handler
w0
w1
PA1

## Slide 23: Summary
FACE Conformance requires ARINC 653 and POSIX
  Deos has certified ARINC 653 support
  RTEMS has robust POSIX support
Combining Deos and RTEMS leverages the strengths of both to provide a FACE Safety Base OSS solution
Future Work
  Submit for formal The Open Group FACE Conformance Certification
  Performance tuning and design optimization
Notes:   Pedigree
    An RTOS with a proven record of deployment, support & certification.
  Reuse
    An RTOS that enables reuse of software & certification artifacts.
  Features
    An RTOS with a rich feature set that enables advanced user-visible functionality and differentiable avionics products.
      time, space & resource partitioning
      IOI & binary modularity
      RMA & 653 scheduling
      slack scheduling & time budget transfer
  Performance
    An RTOS that enables hard-real time, high-performance applications and high levels of resource utilization.
    An RTOS that allows applications to safely exploit the performance capabilities of multicore processors.

## Slide 24: Contact Information
Joel Sherrill
Joel.Sherrill@oarcorp.com
Gary Gilliland
ggilliland@ddci.com
Gedare Bloom
cs.cea.howard.edu/users/gedare
www.ddci.com www.rtems.com

## Slide 25: Extra Slides

## Slide 26
  DDC-I, Inc.
  Leading provider of mission/safety-critical software solutions for 30 years.
  Headquarters in Phoenix, AZ
    World-wide presence
  Primary market: Certifiable avionics software
  Gary Gilliland
  Technical Marketing Manager at DDC-I
  25+ years experience in embedded design, avionics and RTOS
  Electrical Engineering degree from University of Texas

## Slide 27
  OAR Corporation
  Software and systems engineering for mission critical software solutions for almost 40 years
  Headquarters in Huntsville Alabama
    World-wide customer base
  Primary market: Critical real-time embedded systems
  Original developers and constant maintainers of RTEMS
  Joel Sherrill, Ph.D.
  Director of Research and Development for OAR Corporation RTEMS Project Lead
  30 years experience with real-time operating systems including the design, development, and fielding of embedded applications in a variety of commercial, research, and military domains
  BS Computer Science, University of Tennessee at Chattanooga MS Computer Science, University of Alabama in Huntsville Ph.D. Computer Science, University of Alabama in Huntsville

## Slide 28: DDC-I Core Competencies
  Certifiable, safety-critical RTOS products
    Deos (ARINC-653, RMA, or hybrid)
      First certification in 1998
  Integrated Development Environment (IDE)
    Development, testing & analysis tools
  DO-178/ED-12 certification expertise
    First DO-178 DAL-A (Ada) product released in 1992
    We perform our own certification work
    We defend our certification artifacts during all audits
    We do not reverse engineer certification artifacts

## Slide 29: OAR Core Competencies
Real-Time Embedded Systems Development
Operating Systems Experts
Advisors, Consulting
Standards Development
Software Architectures & Software Engineering
DEFENSE SYSTEMS - We support the entire lifecycle of today’s advanced weapon systems. Emphasis in design, development, testing, and oversight of advanced technical solutions for today’s and tomorrow military.
COMMERCIAL SYSTEMS - We provide software development and systems engineering services ranging from simple device drivers to complex applications and systems of systems.

## Slide 30: Deos Highlights
Pedigree – Record of deployment, support & certification
    >10,000 aircraft, >10 Million flight hours, > 40 aircraft types, >100 certs
Features
    Time, space & resource partitioning with ARINC 653 and/or RMA scheduling
    DAL-A Linker/loader for binary modularity - Enables reuse of software & certification credits, and minimizes change impacts
    TCP/IP, File system, ARINC 664/AFDX, ARINC-615 TDL, USB
Performance
    Cache partitioning, low system tick overheads
    Slack scheduling & time budget transfer
    Multicore option
Tooling
    Ethernet & FTP based development – with PC-based processor simulator
    Compiler independent (i.e., current version)
    All tooling applicable through V&V (and deployment in some cases)
    Tooling to determine WCE for apps and target
    Source/Object code coverage tool provided

## Slide 31: RTEMS Highlights
RTEMS is an Industrial Grade open source RTOS
Twenty five year history of deployment on multiple planets, unique instruments, automotive systems, and critical industrial infrastructure
Low overhead with predictable resource consumption
TCP/IP, network services, multiple file systems, USB, dynamic loading, RMA, pluggable schedulers, shell, and much more
Supports over a dozen CPU architectures
Multicore Support