## Slide 1: SpaceFibre Flight Software Workshop 2016
Steve Parkes, University of Dundee
Albert Ferrer Florit, Alberto Gonzalez Villafranca, Chris McClements
STAR-Dundee Ltd.
David McLaren, University of Dundee

## Slide 2: Contents
Next Generation SpaceWire
Links, Lanes, Packets and Virtual Channels
Quality of Service
Multi-Lane Operation
Virtual Networks
SUNRISE SpaceFibre Routing Switch
RC64 Core DSP Processor
Conclusions

## Slide 3: SpaceFibre Next Generation SpaceWire

## Slide 4: Driving Applications for SpaceFibre
High data-rates for SAR and high-resolution multi-spectral imagers require:
  10s Gbits/s data rates
High performance mass memory units require:
  Multi-Gbit/s network interconnecting memory modules
Integrated control and payload data handling requires:
  Deterministic data delivery for AOCS/GNC
  Concurrent with asynchronous payload data delivery
  Simple configuration
  Galvanic isolation
Space transportation and human space flight requires:
  Long distance (100m)
  Deterministic data delivery – safety critical
  Carry video traffic without interfering with deterministic traffic
Backwards compatible with SpaceWire

## Slide 5: SpaceFibre
SpaceFibre is
  A spacecraft on-board data link and network
SpaceFibre runs over
  Electrical and fibre optic cables
A substantial improvement on SpaceWire
  Performance x10 to x100 (multi-lane)
  Power per bit x0.2
  Lower mass x0.75 electrical, x0.5 fibre per cable
  Robustness: galvanic isolation, FDIR
  Capabilities: virtual links, virtual networks, time distribution, event signalling, deterministic data delivery
Small footprint
  Through efficient protocol design
  E.g. 3-6% RTG4 FPGA (2-8 VCs)

## Slide 6: SpaceFibre Key Features
High performance
  2.5 Gbits/s current flight qualified technology
  3.125 Gbits/s Microsemi RTG4 FPGA (6.25 Gbits/s coming)
  Multi-laning of up to 16 lanes (40 Gbits/s)
Integrated QoS
  Priority
  Bandwidth reservation
  Scheduling
Integrated FDIR support
  Transparent recovery from transient errors
  Error containment in virtual channels and frames
  “Babbling Node” protection
Low latency
  Broadcast messages
Compatible with SpaceWire at network level
SpaceFibre
Designed for Spaceflight
Applications

## Slide 7: Links, Lanes, Packets and Virtual Channels

## Slide 8: Links and Lanes
A SpaceFibre link is made up of one or more lanes
Lanes carry information from one end of link to other end
SpaceFibre lanes can run over
  Electrical physical layer
  Fibre optic physical layer
A multi-lane link
  Can have some unidirectional lanes
  Provided that at least one lane is bi-directional
Link provides
  Quality of Service
  Error recovery

## Slide 9: SpaceFibre Packets
Destination
  Represents either
    path to destination node e.g. 1,3,7,2
    identity of destination node e.g. 67
Cargo
  Data or message to be transferred from source to destination
End of Packet Marker
  Indicates end of packet
Destination
Cargo
EOP

## Slide 10: Virtual Channels
Links carry packets through virtual channels
Maximum of 32 virtual channels
Numbered consecutively from 0
Traffic entering VCn at one end of link comes out of VCn at other end
Each virtual channel is independent
  Is given:
    Priority
    Bandwidth allocation
    Schedule
  These three QoS parameters work together to
  Determine the precedence of one virtual channel over another

## Slide 11: Links, Lanes and Virtual Channels
Lane 1
Lane 2
Lane 1
Lane 2
Lane 0
Lane 0
Packets
Link
Near End
VC 1
…
VC N
VC 0
Link
Far End
VC 1
…
VC N
VC 0
Packets
Physical
Lane/Multi-Lane
Data Link
Network

## Slide 12: Quality of Service

## Slide 13: Virtual Channels
VC sends when
  Source VC buffer has data to send
  Destination VC buffer has space in buffer
  QoS for VC results in highest precedence
A SpW packet flowing through one VC does not block another packet flowing through another VC
VC1
VC2
VC3
MAC
VC1
VC2
VC3
DEMUX

## Slide 14: QoS: Bandwidth Reserved
time
Precedence
Bandwidth Credit Counter

## Slide 15: QoS: Bandwidth Reserved
time
Precedence

## Slide 16: QoS Priority
time
Priority 1
Priority 2
Priority 3

## Slide 17: QoS Babbling Node Protection
time
Priority 1
Priority 2
Priority 3

## Slide 18: Multi-Lane Operation

## Slide 19: Multi-Lane Operation
Multi-lane layer provides
  Data rate increase x number of Lanes
  Any number of lanes 1 to 16
  Can change number of lanes dynamically
    Saving power in system mode where lower data rate acceptable
  Graceful degradation when a lane fails
    Without loss of critical (high-priority) information
    Including deterministic traffic
  Asymmetric operation
  Small footprint design

## Slide 20: Multi-lane capabilities
Asymmetric links
  High data rate instruments pass data mainly in one direction
  Allow lanes to be unidirectional
  Provided there is at least one bi-directional lane
Lane 3
Lane 4
Lane 3
Lane 4
Lane 5
Lane 5
Unidirectional lane
Unidirectional lane
Unidirectional lane
Lane 6
Lane 6
Inactive unidirectional lane
Lane 1
Lane 2
Lane 1
Lane 2
Bi-directional lane
Bi-directional lane
RxOnly
RxOnly
RxOnly
RxOnly
TxOnly
TxOnly
TxOnly
TxOnly

## Slide 21: Graceful Degradation
AOCS/GNC
Control
Essential Data
Important Data
Other Data
AOCS/GNC
Control
Essential Data
Important Data
Other Data
AOCS/GNC
Control
Essential Data
Important Data
Other Data
Top Priority, Scheduled
High Priority
High Priority
Middle Priority
Low Priority
Lane 1
Lane 2
Lane 3
Lane 1
Lane 2
Lane 3
Lane 0
Lane 0

## Slide 22: Graceful Degradation
Lane 1
Lane 2
Lane 3
Lane 1
Lane 2
Lane 3
Lane 0
Lane 0
AOCS/GNC
Control
Essential Data
Important Data
AOCS/GNC
Control
Essential Data
Important Data
Other Data
Other Data
AOCS/GNC
Control
Essential Data
Important Data
Other Data
Top Priority, Scheduled
High Priority
High Priority
Middle Priority
Low Priority

## Slide 23: Graceful Degradation
Lane 1
Lane 3
Lane 1
Lane 3
Lane 0
Lane 0
Lane 2
Lane 2
AOCS/GNC
Control
Essential Data
Important Data
AOCS/GNC
Control
Essential Data
Important Data
Other Data
Other Data
AOCS/GNC
Control
Essential Data
Important Data
Other Data
Top Priority, Scheduled
High Priority
High Priority
Middle Priority
Low Priority

## Slide 24: Graceful Degradation
Lane 1
Lane 3
Lane 1
Lane 3
Lane 0
Lane 0
AOCS/GNC
Control
Essential Data
Important Data
AOCS/GNC
Control
Essential Data
Important Data
Other Data
Other Data
AOCS/GNC
Control
Essential Data
Important Data
Other Data
Top Priority, Scheduled
High Priority
High Priority
Middle Priority
Low Priority
Lane 4
Lane 4

## Slide 25: Graceful degradation
When a lane fails in a multi-lane link
  Automatically reconfigured
  To run with remaining lanes
  Takes a couple of µs
Using QoS
  Deterministic and high priority traffic gets through
  Less important, low priority, traffic is held up
If another, redundant lane, is available
  It can be enabled
  Full service then resumed
In the meantime, critical traffic is maintained
This capability is integrated in the SpaceFibre hardware

## Slide 26: Virtual Networks

## Slide 27: SpaceFibre Virtual Network
SpaceFibre
Routing
Switch
VC 0
VC1
VC 2
VC 3
VC 4
VC 0
VC 1
VC 2
VC 3
VC 4
VC 0
VC 1
VC 2
VC 3
VC 4
VC 0
VC 1
VC 2
VC 3
VC 4
SpFi
Port 3
SpFi
Port 4
SpFi
Port 2
SpFi
Port 1
VC 0
VC 1
VC 2
SpFi
I/F
Control
Processor
VC 0
VC 1
VC 2
SpFi
I/F
Mass
Memory
Unit
VC 0
VC 1
SpFi
I/F
Instrument 2
VC 0
VC 1
SpFi
I/F
Instrument 1
Over a link, VCX at one end is connected to VCX at the other end
Virtual networks are mapped on to virtual channels

## Slide 28: SpaceFibre Virtual Network
SpaceFibre
Routing
Switch
VN 0
VC1
VC 2
VC 3
VC 4
VN 0
VC 1
VC 2
VC 3
VC 4
VN 0
VC 1
VC 2
VC 3
VC 4
VN 0
VC 1
VC 2
VC 3
VC 4
SpFi
Port 3
SpFi
Port 4
SpFi
Port 2
SpFi
Port 1
VN 0
VC 1
VC 2
SpFi
I/F
Control
Processor
VN 0
VC 1
VC 2
SpFi
I/F
Mass
Memory
Unit
VN 0
VC 1
SpFi
I/F
Instrument 2
VN 0
VC 1
SpFi
I/F
Instrument 1
Virtual channels are configured to support specific virtual networks
VC0 set of virtual channels is always mapped to VN 0, the Configuration Virtual Network

## Slide 29: SpaceFibre Virtual Network
SpaceFibre
Routing
Switch
VC 0
VC1
VC 2
VC 3
VC 4
VC 0
VN 1
VC 2
VC 3
VC 4
VC 0
VN 1
VC 2
VC 3
VC 4
VC 0
VC 1
VC 2
VC 3
VC 4
SpFi
Port 3
SpFi
Port 4
SpFi
Port 2
SpFi
Port 1
VC 0
VC 1
VC 2
SpFi
I/F
Control
Processor
VC 0
VN 1
VC 2
SpFi
I/F
Mass
Memory
Unit
VC 0
VC 1
SpFi
I/F
Instrument 2
VC 0
VN 1
SpFi
I/F
Instrument 1

## Slide 30: SpaceFibre Virtual Network
SpaceFibre
Routing
Switch
VN 0
VC1
VC 2
VC 3
VC 4
VC 0
VN 1
VN 2
VC 3
VC 4
VN 0
VN 1
VC 2
VC 3
VC 4
VC 0
VN 2
VC 2
VC 3
VC 4
SpFi
Port 3
SpFi
Port 4
SpFi
Port 2
SpFi
Port 1
VN 0
VC 1
VC 2
SpFi
I/F
Control
Processor
VC 0
VN 1
VN 2
SpFi
I/F
Mass
Memory
Unit
VC 0
VN 2
SpFi
I/F
Instrument 2
VN 0
VN 1
SpFi
I/F
Instrument 1

## Slide 31: SpaceFibre Virtual Network
SpaceFibre
Routing
Switch
VN 0
VC1
VC 2
VC 3
VC 4
VC 0
VN 1
VN 2
VC 3
VC 4
VN 0
VN 1
VC 2
VC 3
VC 4
VC 0
VN 2
VC 2
VC 3
VC 4
SpFi
Port 3
SpFi
Port 4
SpFi
Port 2
SpFi
Port 1
VN 0
VC 1
VC 2
SpFi
I/F
Control
Processor
VC 0
VN 1
VN 2
SpFi
I/F
Mass
Memory
Unit
VC 0
VN 2
SpFi
I/F
Instrument 2
VN 0
VN 1
SpFi
I/F
Instrument 1

## Slide 32: SUNRISE SpaceFibre Routing Switch

## Slide 33: SUNRISE: Capabilities
SUNRISE Router capabilities
8-port Router
  8 SpaceFibre ports
    2.5 Gbits/s on each port
    QoS with four virtual channels on each port
    Path and logical addressing
  4 SpaceWire ports
    Connected to one port of SpaceFibre router
    200 Mbits/s on each port
Virtual networks
SpaceWire to SpaceFibre bridge
Group adaptive routing

## Slide 34: SUNRISE Router Architecture
VC 0
VC 1
VC 2
VC 3
SpFi
Port 4
VC 0
VC 1
VC 2
VC 3
SpFi
Port 3
VC 0
VC 1
VC 2
VC 3
SpFi
Port 2
VC 0
VC 1
VC 2
VC 3
SpFi
Port 1
VC 0
VC 1
VC 2
VC 3
VC 0
VC 1
VC 2
VC 3
VC 0
VC 1
VC 2
VC 3
VC 0
VC 1
VC 2
VC 3
SpFi
Port 5
SpFi
Port 6
SpFi
Port 7
SpFi
Port 8
SpaceFibre
Routing
Switch
VC 0
VC 0
SpW1
VC 1
SpW2
VC 2
SpW3
VC 3
SpW4
Port 4
Port 3
Port 2
Port 1
Port 0
Port 5
Port 6
Port 7
Port 8
Port 9
Config
Reg.
&
Routing
Table

## Slide 35: SpaceFibre Router

## Slide 36: PXIe-RTG4 Board
PXI P1/J1
JTAG
Microsemi
RT4G150
FPGA
Clocks
Power Supplies
PXIe
Triggers
DDR
DDR
DDR
Buffers
SpFi Conn.
SpFi Conn.
Flexi
Flexi
Flexi
Flexi
Flexi
Flexi
Flexi
Flexi
Flexi
Flexi
Flexi
Flexi
Flexi
Flexi
Flexi
Flexi
SpFi
Program.
Clocks
5V
B0
B9
SerDes
B0
SerDes
B1
SerDes
B2
B4
B5
B6
B7
B8
B1
B2
B4
B5
B6
B1
B2
B7
B8
SerDes
1 & 2
refclk
SerDes0
refclk
sysclk
SerDes
B5
SpFi 1
SpFi 3
SpFi 2
SpFi 4
SpFi 5
SpFi 7
SpFi 6
SpFi 8
CML Switch
CML Switch

## Slide 37
Flexi
Connectors
FPGA
Microsemi
RTG4
DDR Memory Bank 1
DDR Memory Bank 2
PXIe Interface
Power Supply
SpaceFibre

## Slide 38: PXIe-RTG4 Under Test

## Slide 40: RC64 Many Core DSP Processor

## Slide 41: RC64
64 CEVA X1643 DSP cores
  300 MHz
  38 GFLOPS, 150 GOPS
HW scheduler
Modem HW accelerators
  LDPC and Turbo codecs
4 Mbyte shared memory
Fast I/O
  12 SpFi 6.25 Gb/s
  4 SpFi ports double as sRIO
  48bit DDR3 800 Mw/s
  48 LVDS-DDR 800 Mw/s
  96bit NAND Flash 200 Mw/s
  2 SpW control ports 200 Mb/s
  4 SpW instrument ports 400 Mb/s
Rad-Hard, FDIR
Advanced technology
  65nm LP TSMC
  10 Watt
  PBGA624 & CCGA624
Modular
  Payloads employ many RC64
Reprogrammable in space
Shared Memory
M
M
M
M
M
M
M
M
SpFi/sRIO
DDR2/3
AD/DA
SpW
NVM
DMA
scheduler
FEC
DSP
$
DSP
$
DSP
$
DSP
$
DSP
$
DSP
$
DSP
$
DSP
$
M
M
M
M
M
M
M
M
M
M
M
M
M
M
M
M

## Slide 42: Conclusions

## Slide 43: Conclusions: SpaceFibre Benefits
Supports high data-rate instruments (e.g. SAR)
  Very high data rates
Reduces cost, schedule and risk
  Easy to integrate with existing SpaceWire equipment
  Reduction of harness mass
  Simplification of redundancy
  Increase in reliability
  Very small footprint due to efficient protocol design
Supports integrated AOCS/GNC and payload network
  Quality of service
  Deterministic data delivery
Supports space transportation and human space flight
  Long distance
  Galvanic isolation
Small footprint design (3-5% RTG4 FPGA)

## Slide 44: Conclusions
Multi-lane layer provides
  Data rate increase x number of Lanes
  Any number of lanes 1 to 16
  Can change number of lanes dynamically
    Saving power in system mode where lower data rate acceptable
  Graceful degradation when a lane fails
    Without loss of critical (high-priority) information
    Including deterministic traffic
  Asymmetric operation
  Small footprint design

## Slide 45: Conclusions
SpaceFibre Network layer
  Builds on SpaceWire network layer concepts
  Backwards compatible with existing SpaceWire equipment
Virtual Networks
  Like several independent, parallel SpaceWire networks
  Separates different classes of traffic
  Avoids packet blocking problem
STAR-Dundee SUNRISE router
  Used to demonstrate and validate concepts
  Being ported to Microsemi RTG4 FPGA

## Slide 46: Acknowledgements
The research leading to these results has received funding from
  The CEOI-ST under University of Leicester contract numbers:
    RP10G0348A02
    RP10G0348B206
    RP10G0348A207
  The European Space Agency under ESA contract numbers:
    17938/03/NL/LvH - SpaceFibre
    4000102641 - SpaceFibre Demonstrator
  The European Union Seventh Framework Programme (FP7/2007-2013) under grant agreement numbers
    263148 - SpaceWire-RT (SpaceFibre QoS)
    284389 - SpaceFibre-HSSI (VHiSSI chip)

## Slide 47: Thank You Any questions?
Demonstration Outside
www.star-dundee.com