## Slide 1
2016 Flight Software Workshop
12/14/2016
Steven Doran
Adopting the Python language for On-board Programmable Payload Autonomy

## Slide 2: Introduction
On legacy systems Northrop Grumman (NGC) Azusa is task to maintain an autonomous commanding capability called “Stored Programs”
Stored Programs are pre-programmed sequences of executable statements stored as database items onboard the payload
  Provides pre-programmed delivery of commands to the Flight Software (FSW)
  Includes either Time or Conditional statements for execution
  Written in a Non-NGC Proprietary scripting language
    Requires training to learn the Stored Program Interpreter functionality and language
For future payloads, an NGC in-house ability for Stored Program functionality is being sought

## Slide 3: Stored Program Flow
Load
Execute
Complete
(Success / Fail)
Unload
Upload from Ground
Find and Store

## Slide 4: Replacement Candidate Requirements
An informal study was launched to find a replacement candidate for the legacy Stored Program Interpreter
Replacement Candidate Requirements
  Adopts a common high high-level programming language
    Requires no specialized training and eliminating a “niche” engineering skill
  Full use of Interpreter without restrictions
  Core Functionality
    Conditional Statements
    Delay Statements
    Read Telemetry Monitors in Real-Time
    Send FSW Commands (From Script)
Python Satisfies all Requirements so a Prototype Study was initiated to determine Feasibility

## Slide 5: Python Overview
Python is a high-level programming language
  Interpreted (vs. compiled)
  Open Source
  Readable Syntax
  Modular
  Extremely popular with wide use adoption

## Slide 6: Python / C++ API
Python/C API allows to embed Python source code into a C/C++ Application
  Built-in Python Interpreter
    Reads either a external file or String containing one or more Python statements
#include <Python.h>
int main (){
Py_Initialize();
PyRun_SimpleString("print Hello World\n");
Py_Finalize();
return 0;
}

## Slide 7: Python / C++ API Commands*
Py_SetProgramName(char *name) – Sets Program name (default is Python)
Py_Initialize() – Initialize the Python Interpreter
PyRun_SimpleString(const char *command, PyCompilerFlags *flags) – Runs a Python statement
PyRun_SimpleFile(FILE *fp, const char *filename) – Runs a Python file
Py_Clear() – Removes the internal reference (Python Objects) to the Python Module
Py_Finalize() – Removes all memory allocations and closes the Python Interpreter
* Refer to Python/C API Reference Manual

## Slide 8: Python / C++ Interconnectivity (Memory Management)
The C/C++ Python Interpreter involves a private heap containing all Python objects and data structures
  Managed by the Python memory manager
    Interfaces with the OS to ensure enough memory space is allocated for the embedded Python Program
    Area for concern for Statically-allocated FSW applications
      Not a show stopper
    Inefficient data transfers between C ↔ Python
      Potential issue w/ conditional statements within Stored Program where telemetry values are required
        One of the focuses of Prototype Demonstration
  Allows for Dynamic allocation of memory (malloc, realloc, free)
    Functionality will be prohibited on Stored Programs
      Not required and a reliability issue

## Slide 9: Python / C++ Interconnectivity (Exception Handling)
All functions in the Python/C API can raise exceptions
  If an exception occurs the object being referenced is deleted and an error flag is set
  Python try ... except statement
  Improved capability than the Legacy Stored Program interpreter

## Slide 10: Python Stored Program Constraints
Python Stored Programs must be contained in a Python try ... except Exception Block
Stored Programs cannot use the Python / C++ API Functionality
  Preserve FSW deterministic behavior
  Complex to debug
  No requirement to perform multi-threaded Stored Programs
Only one instance of a Python Stored Program can execute at a time
  Matches Legacy System
Python Stored Programs only have reference memory allocations to the FSW memory space
  Preserve FSW data integrity
Python Stored Programs are a maximum size
  Constrains the maximum API’s private heap space allocation
  Prototype testing to determine maximum size

## Slide 11: Python Stored Program Constraints (cont.)
Python Stored Programs cannot launch another Stored Program
  This is done w/ the legacy system due to the legacy systems Stored Program size constraint

## Slide 12: Python Stored Program (Containers)
Goal is to Prevent Stored Program Error from Propagating to
The Flight Software
When a Python Stored Program is initiated, it is contained in its own unique thread that is removed once Stored Program execution completes
The Python Stored Program’s memory access is limited to an allocated section of memory to prevent impacts to overall system
Python Interpreter is closed at the end of the Stored Program execution and allocated heap space cleared

## Slide 13: Python Stored Program (Containers) (cont.)
CMD
Scheduler
Stored Program
Thread
Launched
Python
Execute
Stored
Program
Completes
Stored Program Thread Killed
Thread Removed
From Scheduler
1
2
3
4
5
Scratchpad
Memory

## Slide 14: Commanding and Telemetry
Python Stored Programs read FSW telemetry monitor states by a reference table in its assigned Memory scratchpad
Python Stored Programs send FSW commands using command FIFO in its assigned Memory scratchpad
Python
Execute
Scratchpad
Memory
CMD
Queue
Fight Software (FSW)
Command
Manager
Telemetry
Manager
TLM Monitor Ref Table

## Slide 15: Timing
Python Stored Programs are required to use the System Time for command processing
Python Stored Programs read a System Clock reference register in its assigned Memory scratchpad
Python
Execute
Scratchpad
Memory
Fight Software (FSW)
System
Manager
System
Time

## Slide 16: Python Stored Program (Off-Nominal Processing)
The Flight Software monitors the execution of the Python Stored Program
If required, the Flight Software can abort the Python Stored Program
  Calls the Py_Clear() and Py_Finalize() API calls to clear heap space and close the Python interpreter
  Kills the Stored Program thread

## Slide 17: Demonstration Overview
A experimental FSW application is commanded to launch a small Python Stored Program
  The Python Stored Program contains a conditional statement if a telemetry monitor is True/False
  Command processed is based on True/False condition
  Telemetry monitor will be updated based on Stored Program processing
Demonstration Tests Core Functionality of Stored Programs

## Slide 18: Prototype Demonstration Environment
Test
Station
(Commanding /
Telemetry)
Development
Workstation
(FSW / Stored Programs)
ethernet
Command to launch Stored Program sent from test station
Communication via ethernet

## Slide 19: Current Status / Future Work
Higher Priority tasks prevented completion of the demonstration this year
  Prototype testing to date shows Python Stored Program scripting is feasible and easy to implement
Plan is to complete the demonstration next year and use more complex Stored Programs

## Slide 21: References
Python/C API Reference Manual
www.python.org

## Slide 22: Abstract
Abstract: This presentation describes the development and implementation of adopting the Python programming language for programmable autonomous commanding and mission processing for future spaced-based payloads. The presentation outlines the many advantages of adopting the Python programming language of autonomous commanding. The presentation also discusses the incorporation of the Python interpreter into the future On-orbit Payload (OP) Flight Software, including the implementation of the “container” strategy to prevent a processing error within the uploaded Python script from propagating to the OP Flight Software’s State of Health (SOH) and mission processing.