## Slide 1: Enhancement of ARINC 653 for Multi-core Hardware
Stephen Olsen VxWorks Product Line Manager
This presentation contains no export restricted information.

## Slide 2
VxWorks
Safe & Secure RTOS Platform

## Slide 3: Agenda
Industry Trends
What is ARINC 653?
Multicore issues
Overview of the VxWorks 653 Single and Multi-core Edition
Q&A

## Slide 4: Main Aerospace & Defense Trends
More Functionality – smarter avionics, SWaP, more payload
Autonomous systems
Global procurement/partnerships
Safe and Secure
Pressure on development costs, schedule
Pressure on operational costs (personnel, training, spares)
Aerospace
More Functionality – more lethality/survivability, integrated battlefield, more arms and armor
Cyber warfare (more computer-based systems)
Coalitions/interoperation
Secure and Safe
Pressure on development cost, schedule
Pressure on operational costs (personnel, training, spares)
Defense

## Slide 5: System Implications
More functions, “systems of systems,” more connectivity in less space, weight, and power (SWaP), reduced cabling
Hardware consolidation
(multiple applications on fewer processors)
Software “pressure”: larger volume of
Software comingled on fewer processors
New challenges to Safe and Secure

## Slide 8: Federated versus IMA
PROs
Traditional methodology (Well Understood)
Relative “ease” of Design and certification
Supply chain geared for this
CONs
SWaP – Each function is separate LRU
Poor S/W Re-use
Poor portability
Poor modularity
Tier 1 at mercy of Primes ($$ for Tier 1)
Federated
PROs
SWaP (multiple functions on single LRU)
Excellent S/W re-use
Excellent portability
Excellent modularity
CONs
“Modern” methodology (777, A380, 787…)
Poorly understood
Complexity of design and certification
Supply chain not setup for IMA projects
IMA

## Slide 9
What is ARINC 653?
aerospace

## Slide 10: ARINC 653
ARINC 653
  Avionics Application Standard Software interface
    APEX (Application Executive) APIs
  Space and Time partitioning
  Safety of Real Time Operating System (RTOS)
  Multiple applications with different safety requirements
  Integrated Modular Avionics (IMA)
VxWorks 653 is specifically tuned to address the needs of ARINC 653
Notes: Separate DO-297-based, role-based development for platform supplier, application suppliers, and system integrator
DAL: Design Assurance Levels

## Slide 11: ARINC 653 APEX (APplication EXecutive)
The ARINC 653 specification defines a general purpose APEX (Application/Executive) interface between the OS and the application software
Partition management
Process management
Time management
Inter-partition communication
Intra-partition communication
Error Handling

## Slide 12: VxWorks 653 Single/dual core
aerospace
7-themes.com

## Slide 13: VxWorks 653 Single/Dual-core (up to 2.x)
Certifiable to RTCA DO-178C, Level A
Support certification of multiple design assurance levels(DAL) on multiple cores running concurrently
Fault isolation and containment: Health Monitors
  The module operating system shall manage and enforce configuration of interconnect functions on the underlying architecture including IO, memory and caches
Static configuration and enforcement in accordance with ARINC 653
Role-based configuration per RTCA/DO-297

## Slide 14: VxWorks 653 2.x IMA Architecture
User
Mode
Kernel
Mode
ARINC 653
Partition OS
Flight Control (FC)
Application
Level A
POSIX
Partition OS
VxWorks Partition OS
Ada/Java
Partition OS
Radar
Application
Level B
Graphics
Generator
Application
Level C
Display
Application
Level D
Hardware
VxWorks 653
Application Executive
XML Configuration Data
Board Support
Package (BSP)
Architecture Support
Package (ASP)
Thread
Scheduling
Only
Partition
Scheduling
Only
Notes: IMA Integrated Modular Avionics

## Slide 15: High-Performance, Two-Level Scheduling
Partition OS
Partition 1
Partition 2
Partition OS
Partition 1 Time Slice
Partition 2 Time Slice
T1
T3
T2
T1
T2
T3
T4
Execution
Idle
Execution
Idle
Time
Notes:   This slide shows the second level of scheduling in the two level scheduler.
  This second level is application process scheduling which implements the ARINC 653 priority preemptive scheduling mechanism.
  One item to note that with ARINC 653 scheduling, improperly designed application can result in wasted time within a partition minor frame time.
  This is undesirable since this time could be used for other background type processing such as built in self test and other low priority processing.
  This effect is common when initially migrating applications from a federated system into the IMA environment, and must be addressed in order to achieve the performance desired.

## Slide 16: VxWorks 653 Multi-core Edition
aerospace

## Slide 17: Multi-core System Issues
Contention makes it difficult to prove that timing constraints are met
Most SoC’s uses hardware that is shared between cores
Designs and effects of sharing are often unavailable
Sharing effects may change as SoC microcode is updated
Addressing these issues can involve additional cert effort
Performance and certification costs depend on matching the choice of strategies of the multicore hardware and the software application

## Slide 18: Certification Authorities Software Team CAST-32A (Multi-Core Processors)
FAA-published guidance on usage of multi-core processors in aviation
Available free on FAA website
Topics Applicable to Multi-Core Processors (MCP) in Safety-Critical Applications
  Sixteen objectives on MCP Determinism
  Six objectives for MCP Software
  Two objectives for MCP Error Handling
  CAST paper addresses only 2 cores at this time, but is largely applicable to more than 2 cores
  Wind River Verification Activities will support many objectives, but integrators will need to conduct additional activities to ensure compliance
Released November 2016
CAST-32A Appendix has mapping from CAST 32 to 32A

## Slide 19: VxWorks 653 3 Multi-core Edition Requirements
Certifiable to RTCA DO-178C, Level A
Support certification of multiple design assurance levels(DAL) on multiple cores running concurrently
Fault isolation and containment: Health Monitors
  The module operating system shall manage and enforce configuration of interconnect functions on the architecture
Static configuration and enforcement in accordance with ARINC 653
Role-based configuration per RTCA/DO-297
Notes: Separate DO-297-based, role-based development for platform supplier, application suppliers, and system integrator
DAL: Design Assurance Levels

## Slide 20: VxWorks 653 3.0 Multi-core Edition Safety Architecture
Available 2015
ARINC Ports

## Slide 21: VxWorks 653 3.0 Multi-core Edition Time Scheduler
With the time partition scheduler, system integrators can schedule multiple guests in a specific time window to be scheduled on a core.

## Slide 22: Roles of the MOS and POS in 3.0 Multi-core Edition
Partition OS (POS)
  VxWorks Cert 6.6.7
    Native kernel
    BSP has Virtualization component
  Device drivers are distributed to each Partition OS
  APEX library
  Application IBLL
Module OS (MOS)
  Uses only devices required to enforce partitioning
  Manages access to common architecture specific resources
  Provides services for communication, health monitoring and emulation
  System Fault Handling
  Configuration management
MOS Kernel
Emulation
VM Interface
Core
Emulation
VM Interface
VM HW Platform
Module OS Services
BSP
Drivers
VM API
ASP
VxWorks Cert kernel
VxWorks Cert API
APEX
Module OS
BSP
Virtual Machine
Application
CV
VM HW access interfaces
Configuration Data
653 Platform Software
Notes: Is there an equivalent to the MOS? Where do I put my kernel code?
How/where do I register device drivers? In 2.x, I add them to the MOS.
IBLL independent build link and load
APEX: Application Executive

## Slide 23: VxWorks 653 MCE Use Case - Migration
Step 1
  Re-host existing uni-core platform using a single core of a multicore
  Minimizes risk but allows for characterization in the new environment to establish a baseline of performance and resolve any issues using existing techniques and understanding
  Criteria for success easily established and bounded
Step 2
  Redeploy platform by moving partition(s) to other core(s)
  Re-distribute IO to allow for dedicated resources per partition
  Perform characterization of new configuration against Step 1

## Slide 24
Avionics Bus (MIL STD 1553, ARINC 429, ARINC 664, SAE AS6802...)
Multi-Core Hardware
Board Support
Architecture Support
VxWorks 653 Application Executive
XML Data
Core 0
Core 1
Core 2
Core 3
Weather Radar Application
DAL C
VxWorks Cert
Partition OS
Flight Display Application
DAL A
VxWorks Cert
Partition OS
Flight Mission Application
DAL B
VxWorks Cert
Partition OS
Step 1
Rehost

## Slide 25
Avionics Bus (MIL STD 1553, ARINC 429, ARINC 664, SAE AS6802...)
Multi-Core Hardware
Board Support
Architecture Support
VxWorks 653 Application Executive
XML Data
Core 0
Core 1
Core 2
Core 3
Flight Display Application
DAL A
VxWorks Cert
Partition OS
Flight Mission Application
DAL B
VxWorks Cert
Partition OS
Step 2
Redeploy

## Slide 26
Avionics Bus (MIL STD 1553, ARINC 429, ARINC 664, SAE AS6802...)
Multi-Core Hardware
Board Support
Architecture Support
VxWorks 653 Application Executive
XML Data
Core 0
Core 1
Core 2
Core 3
Applications
DAL E
Wind River Linux
Guest OS
Application
DAL A
3rd Party
Guest OS
Flight Critical Application
DAL A
VxWorks Cert
Partition OS
Federated Application and OS example with new content added

## Slide 27
Avionics Bus (MIL STD 1553, ARINC 429, ARINC 664, SAE AS6802...)
Multi-Core Hardware
Board Support
Architecture Support
VxWorks 653 Application Executive
XML Data
Core 0
Core 1
Core 2
Core 3
Applications
DAL D
VxWorks 7
Guest OS
Applications
DAL E
Wind River Linux
Guest OS
Applications
DAL A – DAL E
3rd Party
Guest OS
Flight Critical Application
DAL A
VxWorks Cert
Partition OS
IMA platform with applications and OS example with new content added

## Slide 28
Avionics Bus (MIL STD 1553, ARINC 429, ARINC 664, SAE AS6802...)
Multi-Core Hardware
Board Support
Architecture Support
VxWorks 653 Application Executive
XML Data
Core 0
Core 1
Core 2
Core 3
IO Server
DAL A
VxWorks Cert
Partition OS
Applications
DAL E
Linux
Guest OS
Applications
DAL A
- DAL E
3rd Party
Guest OS
Weather Radar Application
DAL C
VxWorks Cert
Partition OS
Flight Display Application
DAL A
VxWorks Cert
Partition OS
Flight Mission Application
DAL B
VxWorks Cert
Partition OS
Redeploy

## Slide 29: DO-297 Role Separation
FMS
Multi-Core Hardware Platform
XML Compiler/Checker DO-178B Qualified Development Tool
Platform Supplier
System Integrator
XML Config File
Binary Configuration Data
XML Config File
XML Config File
XML Config File
XML Tables
XML Config File
Application Suppliers
XML Tables
XML Tables
XML Tables
Nav
Display
XML Tables
XML Business Rules
Notes: 29
29
DO –297, Integrated Modular Avionics (IMA) Development Guidance and Certification Considerations by the RTCA SC-200 described a number of stakeholders in the IMA design characteristics. Wind River has used this guidance and role definition to create a cohesive set of tools and processes to allow full realization of the DO-297 potential in any size project Through the extensive use of XML as described in ARINC 653 we allow separation of these roles to support dispersed development which has provided the ability to support such global programs such as the Boeing 787 Dreamliner.
By use of the DO-178B Qualified XML compiler/checker, the Wind River solution avoids costly and time consuming traceability steps that are required by other RTOS vendors without qualified development tools.

## Slide 30: Conclusion
Important industry trends are leading to integrated systems.
ARINC 653 addresses these needs both for single and multi-core.
VxWorks 653 addresses ARINC 653
Remember: Safety and Security paramount

## Slide 31: VxWorks MILS
aerospace