## Slide 1: Application Inventory
The Johns Hopkins University Applied Physics Laboratory
core Flight System Workshop
December 12, 2016
Susanne Strege – NASA Goddard Space Flight Center
susie.strege@nasa.gov

## Slide 2: Application Catalog
Over 100 applications hosted from:
  Goddard Space Flight Center
  Ames Research Center
  Johnson Space Center
  Glenn Research Center
  Independent Verification and Validation (IV&V) Facility
  Johns Hopkins University Applied Physics Laboratory
  Emergent Space Technologies
  DARPA
  Windhover Labs
Benefits
  Community app store
    Open to government and public
  Promotes sharing and reuse
  Promotes collaboration
  Free Advertising
  Insight into project/mission flight software work load, features, and overlap

## Slide 3: Where is the Application Catalog?
Currently available in electronic copy only (Working Excel and published .pdf formats)
  For a copy contact: Susie Strege – susie.strege@nasa.gov
Plans
  Publish the catalog on cFS public website: http://coreflightsystem.org
  Enhance with:
    Forms for adding new applications
    Configurable displays
    Search engine
    Improvements suggested by active users

## Slide 4
  For catalog additions contact: susie.strege@nasa.gov or cfs-community@lists.nasa.gov

## Slide 5: A Look Inside

## Slide 6: File Commander eXtended FCX
Susanne Strege – NASA Goddard Space Flight Center
susie.strege@nasa.gov

## Slide 7: File Commander eXtended (FCX)
Motivation
  Highly regarded application by GPM operations team. In use on multiple current GSFC projects.
Status
  Product under development
    Requirements, design, code, and unit tests complete
    Maintained by GSFC
Plans
  Develop and run build verification tests and release as open source

## Slide 8: FCX – Overview
FCX Sends CCSDS Packets from a file via the Software Bus
  Supports command and telemetry packet distribution
  Determines file type from cFE primary header sub-type field
    Processes two sub-types using commanded delay value
      FCX_FILE_SUB_TYPE packet data file has CFE primary header only
      FCX_DS_FILE_SUB_TYPE packet data file also has DS secondary header
    Processes one sub-type using Embedded Delay (ED) values
      FCX_ED_FILE_SUB_TYPE packet data file has packets separated by delay values
      FCX_ED_FILE_SUB_TYPE packet data file has CFE primary header only
      This is a new file type with ccsds packets separated by 32 bit delay values
      This file type should not be used for relative time sequencing due to the poor time resolution of the FCX child tasks
  Creates a child task for each packet data file being processed
    Each child task is terminated when its packet data file is closed
    The number of child tasks is limited by a configuration definition

## Slide 9: FCX – Context Diagram
Notes: testnotes

## Slide 10: Commands
Command | Description
No-op | General aliveness test – verifies command handler and event generation
Reset Counters | Reset housekeeping telemetry counters
Start Playback( filename, inter-packet delay time in ms, data array slot number) | Start playback of a file containing a header and CCSDS packets. If slot number = 0 then find UNUSED or STOPPED data array slot, else verify that commanded slot is not ACTIVE or PAUSED. Slot numbers start at one, not zero. Filename must contain a full path specification that is not already active. Initialize shared data array slot. Create child task. Read CCSDS packets from filename, and wait the specified time in milliseconds, then send the packet via the Software Bus.
Stop Playback (data array slot number) | Stops child task reading packets from file. Verify that commanded slot is ACTIVE or PAUSED. Close File. Terminate child task. Send event message.
Pause Playback (data array slot number) | Suspends a child task from sending any more packets until a resume command is received. Verify that commanded slot is ACTIVE. Set PAUSE state in shared data array to cause child task to pause playback.
Resume Playback (data array slot number) | Resume sending packets for a slot that is paused. Verify that commanded slot is PAUSED. Set ACTIVE state in shared data array to cause child task to resume playback.
Replay Playback (data array slot number) | Replays a slot from the beginning of the file that has either completed or error’d. Verify that commanded slot is not UNUSED. Replay the packet playback file in the selected slot using the previous playback command arguments.

## Slide 11: Generic CI - TO
Lorraine Prokop – NASA Johnson Space Center
lorraine.e.prokop@nasa.gov

## Slide 12: Software Tasks – Generic CI - TO
Motivation / Vision
  Provide general-purpose, configurable, and extensible command and telemetry functionality supporting a wide variety of communications protocols and transports for use in multiple current and future projects
Status
  Product finalized
    Received “government purpose release” status
    In use by Orion and AA-2 projects
    Provided to several NASA centers, Firefly space systems under SUA
    Maintained in cFS Community Server
Plans
  Enhance with improvements suggested by active users

## Slide 13: CI- TO Overview
What are the CI-TO Applications?
  Two reusable, configurable, and extensible onboard applications for performing spacecraft command uplink and telemetry downlink within the core Flight Software (cFS) Framework
  Command Ingest (CI) & Telemetry Output (TO)
  Metrics
    Command Ingest (CI) => 4100 SLOC, C code, Telemetry Output (TO) => 2200 SLOC, C code
    Reusable Libraries (ioLib, c3ILib) => 13,500 SLOC, C code (includes unit tests)

## Slide 14: CI/TO Component Design, Data Flow & Execution Architecture

## Slide 15: CI-TO Overview – Input/Output (IO) Library Components & File Structure
Application Program Interface (API) library “plug in’s” for communication services, protocols, transports
  Format protocols:
    TC and TM SDLP with their lower layer synchronization units
    C3I/DEM protocol
  Transport mechanisms:
    RS-422
    UDP
  Protocol Services:
    COP-1, for command sequence enforcement
    Packet framing and multiplexing services for TM_SDLP,
    frame pseudo-randomization for synchronization
    DEM to Space Packet Protocol conversion
Built for modularity - sequential protocol stack through atomic calls
Compile in as necessary, only use what is needed for each specific mission
Easy extensibility through addition of new protocol libraries in custom layer