## Slide 1: Simulink Interface Layer (SIL)
Steve Lentine GSFC/591 Chesapeake Aerospace

## Slide 2: History of SIL
Ames created original version for LADEE mission in partnership with Mathworks
GSFC-SIL forked from Ames-SIL version for use on NICER in 2013
  NICER software development completed in 2015, waiting for launch
  GSFC-SIL currently being used on GEDI
GSFC-SIL enhancements:
  CFE GetTime support
  Conditional Message sending
  Model reference support
  Multiple table support (coming soon)
Ames-SIL enhancements:
  Telemetry/commanding database support
  Usability improvements
Working towards merging Ames and GSFC versions in near future

## Slide 3: GSFC Autocoding Workflow
Software requirements created by pointing team in partnership with FSW team
  Pointing team knows needed functionality to meet mission requirements
  Considered FSW requirements, tested and verified by FSW testers
Pointing team develops and tests algorithms in Matlab/Simulink environment
Advantages:
  Use of existing GNC Simulink libraries
  High code reuse between FSW and High Fidelity Simulations (HiFi’s) which pointing team already produces
  Early end-to-end testing of models/code as they’re developed/implemented
Pointing team generates C code, delivers to FSW team for integration with FSW builds
CFE/SIL Autocoding workflow has been used on LADEE, NICER and GEDI
Notes: Creating flight-software quality simulations does require additional effort from pointing team. Beneficial to have a specific FSW leision on pointing team

## Slide 4: SIL in Operation
Simulink Application
Bus Out
Event Signals
Bus In
cFE Software Bus
Event Processing
Other Apps / Mission Ops
cFE Event Services
Mission Ops
Queue
Cmd/TlmMessages
Provide Sequence Numbers
Error Check Messages
SCH
Execute
House Keeping
Table Management
cFE Table Services
SIL
Mission Ops
cFE Time Services
Spacecraft Time
Fetch Time
Fault Flags
App
CFE
Tlm Data

## Slide 5: Autocoding Components
Model
  Contains task-specific code
  Includes blocks from CSL library to access SIL functionality
  Implemented by pointing team
Target Language Compiler (TLC) file
  Generates (model-specific) headers files for integration with (generic) SIL architecture
  Developed and maintained by Mathworks pilot engineers
Simulink Interface Layer (SIL)
  Generic wrapper code which provides interfaces between autocode and CFE
  Provides FDC reporting, CFE event generation, Message I/O handling, Table management
Notes: TLC file developed and maintained by mathworks pilot engineers

## Slide 6: Model Development – CFE Interfaces
GetTime
  In simulation: returns simulation clock + epoch
  In generated code: calls CFE_GetTime to return FSW time
FDC reporting
  Fills fields of message to Limit Checker

## Slide 7: Model Development – CFE Interfaces
CFE Event
  Generates event message
Conditional Messages
  Pass through bus signal with conditional message to control
  In simulation: only update signal when SendFlag is true
  In generated code: message is only sent when SendFlag is true

## Slide 8: Model Development – CFE Interfaces
Table definition
  Tunable Parameters
    Models must not contains model references
  Simulink.parameter objects
    For models with/without model references
    Simulink.parameter objects will be used to support multiple tables in GSFC-SIL
Referencing parameters:
  Variables:
  Structure Field (direct reference):
  Structure Field (bus routing):

## Slide 9: Code Generation
Initial Setup:
  Configure code generation settings as specified in SIL users guide
    System Target TLC
    Use provided custom TLC template
    Datatype size settings for hardware
Subsequent Builds:
  Click ‘Build’
  Deliver packaged code to FSW

## Slide 10: App Compilation
Initial Setup:
  Assign ApIDs
  Add to scheduler
  Add to Telemetry Output
  (Optional) Define table validation function
Subsequent Builds:
  Drag and drop new generated sources files
  Compile

## Slide 11: Software-In-The-Loop
With stubbed off CFE headers, can compile and run generated code in Simulink environment
Can also run software in real-time environments
  Simulink RealTime

## Slide 12: Autocoded Functionality
NICER:
  Pointing Control Algorithms
    2 axis gimbal controller
    Sensor data conditioning
    Generation of commands to hardware (Mechanism Electronics)
GEDI:
  Data Ingest
    Read raw data from sensors (ST, GPS, Mechanism Electronics, ISS Telemetry)
    Variable format, fixed length packets
  Pointing Control Algorithms
    1 axis gimbal controller
    Generation of commands to hardware (Mechanism Electronics)