## Slide 1
Core Flight System
Cryptography Library
John Lucas
John.P.Lucas@nasa.gov
www.ccsds.org

## Slide 2: Overview
Why do we need security?
What is CCSDS?
Space Data Link Security
Extended Procedures
Cryptography Library
Application
Testing
Demonstration
Future Work

## Slide 3: Why do we need security?
Spacecraft systems are a high-profile target
  An attacker can cause considerable harm to a nation or company by compromising a spacecraft
Obscurity and uniqueness are not sufficient protection
  The technology for spacecraft communication is more readily available
  Use of public ground networks to transfer mission control and monitoring data has increased vulnerability

## Slide 4: Consultative Committee for Space Data Systems
CCSDS
  Founded in 1982 by the major space agencies of the world
  Experts from 26 nations collaborate
  Primary goal is interoperability between space agencies
  More than 800 space missions flown
CFS was developed with these protocols in mind:
  Space Packet Protocol (SPP)
  CCSDS File Delivery Protocol (CFDP)
  Communications Operation Procedure – 1 (COP-1)
  Telecommand Space Data Link Protocol (TC-SDLP)
  Telemetry Space Data Link Protocol (TM-SDLP)
Goal to evolve with Space Data Link Security (SDLS)

## Slide 5: Space Data Link Security
Compatible with both the TC and TM protocols
  Those used with the CI and TO applications
Structured method for applying data authentication and/or data confidentiality at the Data Link Layer
Applies a security header and trailer to the payload

## Slide 6: Space Data Link Security
TC:
TM:

## Slide 7: Space Data Link Security
Security Header:
Security Trailer:

## Slide 8: Space Data Link Security – Extended Procedures
Extended Procedures provides three services:
  Key Management
    Ensures both communications endpoints are synchronized in terms of cryptographic keys and key states.
    Over-The-Air-Rekeying can be used to update session keys.
  Security Association (SA) Management
    Provides a means to setup, activate, check status, and control an SA of the remote system.
    As missions become more complex, dynamic management will be necessary.
  SDLS Monitoring and Control
    Ability to modify mission specific parameters
    Maintains the status of the security processor as a whole.

## Slide 9: Space Data Link Security – Extended Procedures
  Key Management
    Symmetric key management infrastructure
    Scalable to meet mission needs
    Master keys
      Used to decryption session keys
    Session keys
      Used for all other message types
    Over-The-Air-Rekeying (OTAR)

## Slide 10: Space Data Link Security – Extended Procedures
  2. Security Association (SA) Management
    Anti-replay counter / window size
    Authentication bit mask
    Direction – TC or TM
    Encryption cipher suite
    Linked keys
    Managed lengths of values

## Slide 11: Space Data Link Security – Extended Procedures
  3. SDLS Monitoring and Control
    Commands
      Ping
      Manage Logs
      Read Sequence Number
      Reset Alarm
      Self-Test
    Logs and Reports
      Frame Security Report (FSR)

## Slide 12: Cryptography Library
Cross-platform codebase
  Can be used by flight software and the ground system
  Developed in C
Minimal to provide only necessary functionality
  AES 128-bit block cipher
  128-bit Galois/Counter Mode for Authenticated Encryption
  128-bit CMAC authentication
Open-Source
  Currently pending approval
Simple to implement
  ApplySecurity(ingest, len_ingest)
  ProcessSecurity(ingest, len_ingest)

## Slide 13: Inter-Agency Testing
Goal to implement SDLS-EP baseline mode for publication

## Slide 14: Demo

## Slide 15: Future Work
Additional Encryption Cipher Types
Advanced Orbiting Systems (AOS) Support
Ground System Integration
  Utilizing COSMOS
Load Testing
  Implementation on AVR32 flight computer
Improved separation / explanation and support of mission specific parameters
Inclusion into simulator platforms
  NOS3
Integration into mission
Unit Tests

## Slide 16
Questions?
A special thanks for attending and to our sponsors!
John Lucas
John.P.Lucas@nasa.gov
www.ccsds.org

## Slide 17: Backup