## Slide 1: Autonomous On Board Mission Planning
Garcia Franchi Gaston, Alonso Roberto, Pucci Nadia, Kuba Jose
Comision Nacional de actividades espaciales (CONAE)
Argentina

## Slide 2: Table of Contents
Main Functions
Objective and Motivation
Geometrical View – Polytope
Software Design Overview
Applications to LEO Satellite
Extension to Constellation
Summary

## Slide 3: Introduction
  Current Mission Architecture
Telecommands
Telemetry
& Payload data
Teleommands
Telemetry
Satellite Executes the commands
The Mission Center computes the Telecommands

## Slide 4: Motivation for a Change
  Current status:
  The satellite is controlled by ground commands.
    The planning is done by sending the entry and exit times for each area of interest (polytopes).
    Each instrument or equipment is set by the adjustment of their operational parameters.
  Motivation:
  The resources allocate for the on-board computing often exceeds the routine operation needs. Spare capability for extra computation is available for the planner.
  Due to the limited time of access from the Ground Station (GS) the amount of commands to be uploaded is also limited. This is crucial in countries with reduced access to Ground Stations.
  Modifications in the Mission Plan generate a significant set of actions on the Mission Center to generate new commands because of new scenarios. The amount of commands increases.

## Slide 5: Proposal for Mission Improvement
Satellite generates the actions to accomplish the mission plan
The Mission Center monitors the automatism of the satellite

## Slide 6: Main Functions for the Planner
Main Functions
Monitor instrument’s operational parameters on each scenario
Facilitate the incorporation / modification of scenarios
Allow operating the payload by conventional procedures and rules
Generate automatically the planning of the following orbits
Automate on-board planning for data transmission / reception (The ground station is considered a polytope)
Advanced Functions
Autonomous. Calculate independently the state vector
Perform a systemic control of failures and alerts

## Slide 7: Functions of the Planner
  Determination of the satellite position by independent information which is complementary to GPS. Available in case of being necessary.
  Determination of the satellite attitude by independent information which is complementary to Star Tracker or Earth Sensor . Available in case of being necessary.
  Determination of the sub satellite point or sub camera point.
  Polytope construction by the uploading of a convex set of points which are defined by their latitude and longitude.
  Determination of the position of the sub satellite point (or similar) on the Earth surface.
  Generation of the events : Inside, Outside, Leaving or Entering of the polytope.
  These events can execute commands, scripts, check status of instruments or equipment, generate alarms and reports.
  The planner allows the addition o functions that are unique for each mission. Example: calculation of trends, determination of errors (position and/or attitude), memory allocation, etc.

## Slide 8: Example of Polytope : Calibration Area
  Image displayed using the program Cesium Viewer

## Slide 9: Geometrical View of the Polytope
Sub Satellite Point
(@Nadir)
Sub Camera Point
(inside)
Determination
Determination
Polytope
Mission Plan
Attitude
and
Orbit
Determination
Prediction of events and
trend analysis
Sub Camera Point
(outside)
Determination
Operational Mode
Instruments
Checking

## Slide 10: A Closer View of the Geometry
GOIN →
First step inside the polytope
GOOUT →
First step outside the polytope
INSIDE →
Inside the polytope
OUTSIDE →
Outside the polytope

## Slide 11: Box around the Polytope
Only executes the algorithm when the spacecraft is inside the box around the polytope
Polytopes inside polytopes!

## Slide 12: First Version of the Planner
Trigger: Events / Alarms (Device Status, etc.)
Generate: Reports / Telemetry
Execute: Commands / Scripts /
Flexible
OS Independence
ANSI C
Keep It Simple

## Slide 13: Software Design – Other Functions
  Extra functions:
        Create new polytopes and new scenarios.
        Change points in polytopes
        Change devices, commands, scripts, etc, in scenarios
        Change expected values of the devices
        Change commands and scripts
        Modify the planning table.
        The planning table has two operating modes: Realtime and Time Tagged (event predictor).

## Slide 14: Software Design Simple Aproach
GOIN, GOOUT, INSIDE, OUTSIDE
Operational Modes
Real time
Time tagged – or event predictor

## Slide 15: Software Design, cont’n

## Slide 16: Advanced Design of the Planner
Instruments Telemetry
Determination of:
  ORBIT,
  ATTITUDE,
  SUBSATELLITE POINT,
  SUBCAMERA POINT
Polytopes Points
Generation of new Scenarios
Timetagged planning / Event predictor
Trend Analysis
Eclipse Events
INPUT DATA
PLANNER
OUTPUT DATA
Range, Doppler, DOP
Vectors: position & velocity
GPS Time & TLE
Navigation Sensors
Attitude Sensors
Vectors: Magnetic Field & Sun
Stars Sensor
Filtered Orbit
2 Orbits Propagation
Robust Attitude
Sub Satellite Point
Sub Camera Point
Position respect to the polytope
Alerts

## Slide 17: Baseline Satellite
Platform
Computer
sensors
actuators
Power
Subsystem
Battery
Solar Array
Regulator
propulsion
Telemetry
and
Commands
State of
Health
Platform
+ Power+
Thermal
Payload
Payload
Computer
Instrument
Data
Storage
Data
Transferring
State of
Health
Instrument
Operability
Instrument
Instrument

## Slide 18: SABIA Mar Mission: First Test Case
Ocean Color mission.
Sun Synchronous Mission (9 days for revisiting the same track).
Three main cameras covering from UV to LWIR spectral bands.
Several operational scenarios for ascending and descending orbit.

## Slide 19: Simulation of the SABIA Mar Orbit
FOV
polytope

## Slide 20: Extension to Constellation
Ground
Polytope
Master
Satellite
x
v
q
w
master
=
Space
Polytope
slave_a = [ x ]
slave_b = [ x ]
slave_n = [ x ]

## Slide 21: Extension to Constellation, cont’n
The spatial polytope represents the volume
where each slave satellite must be located
at t_A and t_B times in order to satisfy the requirements for a cooperative mission with the other constellation satellites
orbit
slave
satellite
master satellite
Minimum information is needed
[x v q w ] for the master satellite
[ x ] for each slave satellite
sub satellite spatial point
The same algorithm used for
ground polytope is used for
space polytope
slave polytope
At each time the
algorithm computes if
the slave satellite is
Inside or outside the variant
space polytope. The
the same procedure than
for ground polytope is applied

## Slide 22: Summary
The feasibility of incorporating this mission planner on LEO satellites is introduced in the presentation. A reduced version of this planner is applied to manage the payload module of the SABIA Mar satellite.
The Mission Control Center changes its role from being the activator of the mission to the supervision of the actions performed by the payload. It is a change in the current paradigm.
The mission plan becomes a dynamic document where changes are easy to make and the addition of new polytopes do not generate an extra effort in the control center.
The extension to constellation using the baseline concepts is also feasible. Minor changes in the software code.

## Slide 23
  Thank you for the opportunity to present our research during this workshop.
  Any question?

## Slide 24: Back Slides

## Slide 25: Function: I/O Polytope
The Jordan curve theorem is used to know if a
point is inside or outside the polytope.
In the central area a point is considered outside if
any ray cuts the star in an even number of edges.