## Slide 1: Porting the core Flight System to the Dellingr Cubesat
Alan Cudmore
Code 582
NASA Goddard Space Flight Center

## Slide 2: Agenda
Background
Overview of the Dellingr Cubesat
  Hardware Overview
  Flight Software Overview
Simulation on a Budget
Flight Software Challenges
Port Details
Lessons Learned
Conclusion
Mission Status

## Slide 3: Background
Dellingr is a Heliophysics 6U Cubesat developed at GSFC
  “Dellingr” is named after the mythological Norse god of the dawn
Originally planned as a one year ”skunkworks” effort
  1 person/year for all flight software (FSW) including the Attitude Control System (ACS)
  Selected Gomspace Nanomind A712 platform for a 32 bit Central Processing Unit (CPU) with minimal power consumption
After a preliminary design review, I volunteered to port the cFS to the platform
  After cFS port to a development board, project decided to use the core Flight System (cFS)
Revised plan
  Original developer continued to work on the ACS
  I worked on the cFS implementation and created mission app templates
  Others worked on integrating device code, developing mission specific apps, and developing ground software

## Slide 4: Dellingr Cubesat Hardware Overview (1)
CPU:
Gomspace Nanomind A712d
ARM processor
DAGR:
Science
Magnetometers
(Internal and Boom Mounted)
Comm:
L3 CADET Radio
3 Mbits down/9600 up
4 Gbytes packet Storage
(antenna by home depot)
INMS:
Ion Neutral Mass Spectrometer
instrument
Tech Demos:
Thermal Louvre
Deployment Camera
Power:
Clyde Space EPS and Batteries,
SolAreo ZTJ body mounted cells
Dellingr Facts:
6U Cubesat
Delivered to ISS August 2017
Deployed from Nanoracks Deployer On November 20, 2017
ACS:
MEMS Gyro, Fine Sun Sensors, Coarse Sun Sensors, GPS, Magnetometers,
Reaction Wheels,
Torquers

## Slide 5: Dellingr Cubesat Hardware Overview (2)
Processor Card - Gomspace Nanomind A712d
  Atmel ARM7 CPU @ 40Mhz
  2 Megabytes SRAM
  2 x 4 Megabytes Flash Memory
  Micro Secure Digital card
  I2C, SPI, UARTs
  Real Time Clock
  Magnetometer, PWM, Analog Inputs

## Slide 6: Dellingr Cubesat Flight Software Overview (1)
OS Abstraction Layer
(FreeRTOS)
Platform Support Package
(Nanomind)
Gomspace Nanomind Firmware
Device Drivers, Shell, File Systems
core Flight Executive (cFE)
Gomspace Nanomind Hardware / ARM CPU
FreeRTOS
Operating System
Vendor
Supplied
Dellingr FSW
Porting Layer
Dellingr Hardware Library
Dellingr
ACS
App
Dellingr FSW
Apps and Libs
cFE/cFS
Reuse
Legend:
Vendor Supplied
cFE/cFS Reuse
New on Dellingr
cFS
Reuse
Apps
Dellingr
INMS
App
Dellingr
DAGR
App
Dellingr
SHK
App
Dellingr
CADET
App

## Slide 7
Vendor Software | Reuse Software | New Software
FreeRTOS OS | cFE Core | FreeRTOS OSAL Layer
Bootstrap/Startup Code | cFS Scheduler | cFE Platform Support Package
Device Drivers | cFS Stored Commands | Dellingr Hardware Library
File Systems | cFS Health and Safety | DAGR Instrument App
C Library | cFS Checksum | INMS Instrument App
 | cFS Limit Checker | CADET Radio App
 | cFS File Manager | ACS App
 | cFS Memory Dwell | Ephemeris/GPS App
 | cFS Memory Manager | Reaction Wheel App
 | Static Loader (MMS) | File Downlink App
 |  | File Downlink App
 |  | Spacecraft Housekeeping App
Dellingr Cubesat Flight Software Overview (2)

## Slide 8: Simulation on a Budget (1)
Dellingr did not have dedicated dynamic simulator such as the Goddard Dynamic Simulator (GDS) for ACS testing
Simulation is accomplished with a combination of:
  The open source dynamic simulator ”42” developed by GSFC Code 591
  The “Dellingr Hardware Library” with an interface to the ”42” simulator
Most of the ACS app debugging was done on cFS/Linux with 42
When the Satellite was complete, we were able to do a spin test using the reaction wheels and sun sensors

## Slide 9: Simulation on a Budget (2)
Dellingr Hardware Library Details
  A cFS Library that abstracts all mission specific hardware
    Focus is on the ACS Hardware
  Allows FSW to run in the following configurations:
    On-board computer with real hardware devices
    On-board computer talking to 42 Simulator over a serial port
    Linux computer talking to 42 Simulator over TCP/IP Socket
  The ability to run the Dellingr Flight Software on Linux with the 42 speeds up ACS development and test
  This model worked well and will be used for future efforts
ACS
FSW
Dellingr
Hardware
Library
Gyro Data
Hardware Gyro
Simulated Gyro on “42”

## Slide 10: Flight Software Challenges (1)
New Operating System: FreeRTOS
  Required a port of the Operating System Abstraction Layer (OSAL)
  Once the OSAL was working, the cFE core and portable cFS apps worked without modification
On-board computer only has 2 Megabytes of RAM
  The cFS code has to run in Flash, since 2 Megabytes of RAM is not enough
  Some cFS applications had to be left out to save room (CFDP file transfer, Housekeeping)
Flash file system is limited
  Only holds 64 files, not enough for all of the mission stored command sequences
  Workaround is to “bundle” multiple stored command sequences into a single file
  This is a generic solution that could be used on other missions
Cadet Radio Subsystem
  Half Duplex, not ideal for real time telemetry and commands
  Very low data rate between on-board computer and radio/recorder limits amount of data spacecraft can produce at one time

## Slide 11: Flight Software Challenges (2)
Limited Schedule and Budget
  The traditional FSW development lifecycle does not work here
  Framework of the cFE/cFS provided a model to follow for new software, saving us from re-inventing the wheel
No ETU or Flat-Sat
  There is only one copy of the satellite hardware, and it was not always available for FSW development
  FSW changes had accumulated right before Thermal Vacuum testing leading to last minute integration bugs and troubleshooting
Significant time spent working with device drivers and interfaces
  A Typical large mission has a limited set of known interfaces (1553/Spacewire, Serial)
  Dellingr uses Serial, I2C, SPI, Analog, GPIO, and I2C extended interfaces
  Multiple problems encountered with I2C and SPI interfaces that just needed more troubleshooting time and effort
  Engineers end up being multi-discipline ( FSW, Hardware, Mechanical, I&T )

## Slide 12: Port Details: OS Abstraction Layer
Kernel
  Basic FreeRTOS port was fairly straightforward
    All of the OS primitives are present
  FreeRTOS has a configurable set of priorities (used 256)
  Using FreeRTOS 8.x
File Systems
  FreeRTOS does not include a File System
  Gomspace integrated firmware that included:
    The “fatfs” open source Filesystem
    UFFS filesystem for the flash memory
    A POSIX API Virtual Filesystem Layer (VFS)
Network interfaces
  FreeRTOS does not include a network stack in the base kernel, but this was not needed for Dellingr
  The Gomspace Cubesat Space Protocol (CSP) was used to transfer files to the flash over the serial port
Dynamic Loader
  Used a combination of MMS Static Loader and linking apps directly with the cFE Core and base OS image
  Most mission apps were loaded from the file system

## Slide 13: Port Details: Platform Support Package
PSP / Startup code
  Wanted to leverage the Gomspace Nanomind firmware
    Modifications made to facilitate cFS port
    The original Gomspace Shell was used for a diagnostics console
  With only 2MB of RAM, the cFE/cFS code had to run in Flash
    Only selected mission apps could be dynamically loaded to RAM
1HZ Time Source
  There was no 1hz time source for this system (GPS is not always powered)
  The FreeRTOS 1000hz timer tick is used as the 1hz source
File Systems, Volume Table
  The /ram and /boot file systems are directly mapped to the OSAL
  No path translation is needed
Restart Code
  Ties to the Gompace firmware reset function
Watchdog
  Uses the CPU watchdog feature
Flash/Nonvolatile access
  Due to time and schedule, the flash is readable via memory map for checksum, but not writeable outside of the file system

## Slide 14: Lessons Learned (1)
Positive cFS Lessons:
  The cFS brought a development environment, FSW framework, and process to the project
    Work could be broken up in to modules or cFS apps for developers to focus on
    The modularity of an app helped isolate the code
  The cFS allows you to focus on mission specific code and start to work on that immediately
  The cFE and cFS functionality added a lot to the mission with little effort
    FDC, stored commands, Limit Checker, Table Services, saved a lot of time in re-inventing software
  The cFS cross platform capability allows us to develop and run on desktop Linux, Raspberry Pi, and other targets
    Very useful for getting high level application logic working
Negative cFS Lessons:
  The cFS was a poor fit for Gomspace Nanomind Processor card due to the limited amount of SRAM
  Experience was used to work around limitations of the processor card – This was not a recommended port for cFS beginners
  cFS experience helped with the selection and configuration of apps – Learning the cFS is beneficial before trying to develop a system

## Slide 15: Lessons Learned (2)
The 42 Simulator interface to the cFS enabled ACS development and debug
  ACS algorithm checkout would have been very hard without it
Not having a Flat Sat or second copy of the hardware was difficult
  Having the cFS and simulation capability from day 1 would ease this problem, but not eliminate it
Hardware devices were hard to work with, and hardware/software integration was time consuming
  This was unavoidable no matter what the framework
  I2C , SPI, UART interfaces are all “Finicky”
  Used Standalone diagnostic code and even Arduino to test out devices
  It was often easy to get a device working with a test program by itself but harder when in a multitasking environment with multiple devices operating

## Slide 16: Conclusion
Was the cFS the right choice for the Dellingr Cubesat?
  Yes : There were compromises, but valuable lessons were learned that can immediately be applied to the next generation of Cubesats
  We were able to leverage cFS experience and expertise to make up for shortcomings
What would we do differently if starting over today?
  If using the cFS, influence the hardware selection to take advantage of an existing port, or at least an easier port
  Start defining mission specific applications and building a version of the FSW that runs on Linux or similar desktop board
  Simulate hardware interfaces and integrate 42 simulator from early in the development
  Consider the ground system earlier

## Slide 17: Mission Status
Dellingr was deployed from the International Space Station (ISS) on November 20, 2017 and is currently going through commissioning and checkout

## Slide 18: Acronyms
Acronym | Meaning
ACS | Attitude Control System
CCSDS | Consultative Committee for Space Data Systems
CFDP | CCSDS File Delivery Protocol
cFS | core Flight System
cFE | core Flight Executive
CPU | Central Processing Unit
GDS | Goddard Dynamic Simulator
GPIO | General Purpose Input Output
GPS | Global Positioning System
GSFC | Goddard Space Flight Center
INMS | Ion Neutral Mass Spectrometer
ISS | International Space Station
OSAL | Operating System Abstraction Layer
PSP | Platform Support Package
PWM | Pulse Width Modulation
RTOS | Real Time Operating System
SHK | Spacecraft Housekeeping (cFS app)
SPI | Serial Peripheral Interface (bus)
SRAM | Synchronous Random Access Memory
UART | Universal Asynchronous Transmitter-Receiver