## Slide 1: Autonomous Vehicles Commonalities in state of the art Cars and Spacecrafts
Christian Fidi Product Manager
2017/05/12
Flight Software Workshop 2017

## Slide 2: Safety Control and Networking Reference Projects
Audi/VW zFAS: First Level 3 Autonomous Driving System
Audi A8 eABC: ECU for first Electro.-mech. active chassis
Volvo C30 electric: Inverter safety control
Level 4/5 automated driving projects
NASA Orion; Network
Ariane 6:
SoC
Boeing 787: Network
Airbus A380: Network
Embraer E2: Fly-by-wire
Vestas: Safety Control Platform
Claas: Ethernet Controller, Firewall
Automated driving for farming machines
Prinoth Snowgroomer
Kuka: Edge/Fog Computing
Morita Fire fighter: ECU

## Slide 3: Cross-industry synergies
Highest safety and certification
TTEthernet ARINC 664 switch
Communication controller
Flexibility and
reliability
Fog
computing
Network interface card
for industrial PCs
Networking
and Controls
Safety and
high-volume
Advanced Driver Assistance Systems platform
Switch IP design for Ethernet
Reliability and robustness
High-end ECU
Aerospace
Automotive
Industrial
Off-Highway
Notes: Farbgebung? Bunt oder grau/blau

## Slide 4
Audi A8 where all sensory data are processed and driving
decisions are taken
TTTech provides the safe software and communication platform for the new
First Level 3 Automated Driving System

## Slide 5: The need for Safety and Fail-Operational
Functionality
Customer Acceptance
Legislation
Cost
Compute Performance
Safety

## Slide 6: The need for Safety and Fail-Operational
              Safe Operation in normal scenarios
              Lane change to the side and stopping
              … and in rare scenarios
              Stop the car avoiding obstacles

## Slide 7: The Autonomous Driving Challenge Heatmap
12/5/2017
7

## Slide 8: The Autonomous Driving Challenge Heatmap
12/5/2017
8

## Slide 9: The Autonomous Driving Challenge Heatmap
12/5/2017
9

## Slide 10: System Classification by VDA
On the market today
SOP 2017
e.g. Audi A8
Planned for 2020+
Delegation of responsibility from driver to the car
12/5/2017
10

## Slide 11: The Fail-Operational Requirement
Stop the car (avoiding obstacles)
Lane change to the side and stopping
Level 4: “System can handle all situations automatically in the specific application case” [VDA]  Even in the case of component failures!
Lane change to the side and stopping
12/5/2017
11

## Slide 12: Safety assumptions
A fault can occur in an arbitrarily complex situation
Today’s Level 2/3 systems
  Driver shall take over within 10s error reaction time
  Reduced speed and limited complexity of driving situation (e.g. traffic jam pilot) allow fail-silent approach based on pre-calculated safety trajectory if driver fails to take over.
  Assumed safety requirement for ADAS ECU: no commands shall be sent on the car network in case of an error
Level 4 systems
  Highway speed 130 km/h (= 361 meters in 10 seconds)
  Other vehicles changing lanes, braking, …
  If driver fails to take over need to reach a safe place to stop (breakdown lane) (a few minutes)
  Therefore appropriate computational power and situational awareness is needed also in the fault scenario to continue operating (for ~5minutes up to full driving cycle)
   Redundant configuration required!
12/5/2017
12

## Slide 13: Why is it Difficult?
Airplanes are fly-by-wire and fail-operational …
… but they use triple or more redundant diverse electronics
TTTech provides the fly-by-wire network for Embraer E-Jet E2 Family
12/5/2017
13

## Slide 14: Why is it Difficult?
TTTech provides the fly-by-wire network for Embraer E-Jet E2 Family
Boeing 777 Flight Computer
3 x 3 Architecture
HW Diversity
12/5/2017
14

## Slide 15: ISO 26262 Approach
Fault avoidance according to ASIL
Systematic Faults
Random Faults
Hardware
Processes more strict for higher ASIL
Examples
Formal reviews
Fault injection tests
Analysis
Hardware
Lower fault probability for higher ASIL
Examples - self checking design
Dual core lockstep
ECC
Clock supervision
ASIL A
ASIL B
ASIL C
ASIL D
QM
ASIL: Automotive Safety Integrity Level
Software
Processes more strict for higher ASIL
Examples
Strict traceability
MC/DC test coverage
Formal methods
12/5/2017
15

## Slide 16: System and Network Partitioning
Cache
Core 0
Core 1
Core 2
Core 3
Hypervisor
RTOS
Control Apps
virtual machine
Rich OS
IT / Media Apps
Secure OS
Security Apps
virtual machine
Deterministic Ethernet
TTEthernet
Partitioned memory
Virtualized Network Interface
Scheduled DMA
virtual machine
Safe OS
Safety
Apps
virtual machine
compute level virtualization
Network virtualization
TTEthernet based
  Memory partitioning on the host interface
  Memory partitioning in the switch
  Time-partitioning on the network
12/5/2017
16

## Slide 17: TTEthernet – Traffic Classes
SAE AS6802
synchronous
jitter < 1 ms
known latency
ARINC664p7
AFDX
asynchronous
low jitter (< 500ms)
latency typical 1-10ms
IEEE802.3
Ethernet
best effort Ethernet
no performance guarantee
Quality of Service
SAE AS6802
Time-Triggered
synchronous/periodic
very small jitter (< 1ms)
known latency
12/5/2017
17

## Slide 18: Fault-Tolerant Synchronized Global Time
Fault-tolerant synchronization services are needed for establishing a robust global time base in the sub-microsecond area
12/5/2017
18

## Slide 19: Time-triggered Traffic Timing
Full control of timings in the system
Defined latency and sub-microsecond jitter
Minimum memory needs
Fault-containment regions
I’ll transmit M at 10:45
I’ll accept M only between 10:40 and 10:50
I’ll forward M at 11:00
I’ll accept M only between 10:55 and 11:05
I’ll forward M at 11:10
Let’s see if I can receive M
…a switch
I’ll expect M between 11:05 and 11:15
M
M
M
M
12/5/2017
19
Notes: …but sender and receiver still only do “I’ll transmit M at…” and “I’ll expect M at…” – the added complexity is in the network, not in the nodes

## Slide 20: Fault-Containment Regions
TTEthernet defines Switches and End Systems as two kinds of Fault-Containment Regions. Frame loss is mapped to the respective sender.
Depending on cost and reliability targets, switches and or end systems may be implemented with standard or high-integrity in order to be able to scale from single to dual fault tolerance.
Protocol mechanisms can be configured to handle Strictly Omissive Asymmetric switch faults (HI) and fully Transmissive Asymmetric end system faults (SI).
12/5/2017
20

## Slide 21: TTE-Controller
 Switch Controller COM
 Switch Controller MON
 End System
  For the connection of the CPU to the switch controller
 CPU
  Management &
  Diagnostics
Switch Commander (COM)
6 x 10/100/1000 RGMII/RMII
19 x 10/100 RMII (PBGA) 12x10/100 RMII (CQFP)
1 x 10/100 on-chip (for E/S in management mode)
4096 VLs (messages)
1MB frame memory
12/5/2017
21

## Slide 22: TTE-Controller
 Switch Controller COM
 Switch Controller MON
 End System
  For the connection of the CPU to the switch controller
 CPU
  Management &
  Diagnostics
Switch Dual-Core Lock-Step (COM/MON)
Same parameter set as COM
Delayed clock between the COM and MON
Share the same frame memory
Separate configuration memory
Internal comparison of output
Separate silicon area
Observation of clock
12/5/2017
22

## Slide 23: TTE-Controller
 Switch Controller COM
 Switch Controller MON
 End System
  For the connection of the CPU to the switch controller
 CPU
  Management &
  Diagnostics
End System
3 x 10/100/1000Mbps ports (RGMII/RMII)
256 send VLs, 512 receive VLs
IP/UDP/ARINC653 support
IP fragmentation/defragmentation (8kByte)
Diagnosis and status registers
PCI, (Q)SPI, SpaceWire interface
12/5/2017
23

## Slide 24: TTC - Communication
Interfaces Layers:
UDP-COM (TT & RC)
IP-COM (TT & RC)
MAC-COM (TT, RC & BE)
MAC-RAW (TT, RC & BE)
Via:
Sampling or
Queuing ports
12/5/2017
24

## Slide 25: TTC – Partition Sync State
The TTC supports up to 8 independent partitions for input and 8 partitions for output traffic.
A partition is defined as:
an independent address space with
a configured size separated for
input or output traffic with
defined communication ports (sampling, queuing or SAP)
12/5/2017
25

## Slide 26: TTE-Controller
 Switch Controller COM
 Switch Controller MON
 End System
  For the connection of the CPU to the switch controller
 CPU
  Management &
  Diagnostics
CPU for Management and Diagnostics
Leon2FT @ 125MHz
Simple SNMP functions
Simple TFTP data loading
Bootloader
Switch driver
End System driver
User tasks
12/5/2017
26

## Slide 27: Conclusion
Automotive:
  Higher Integration needed to handle high data-rates and processing
  Cost shift from ECU hardware to SW function development and validation – reuse mandatory
  Cost and Complexity of Integration is growing rapidly
  Fail operational architecture required for Level 4 autonomous driving
  High bandwidth and determinism demands requires upgrade of communication backbone
AeroSpace:
  Recent developments for space are applying automotive concepts to space products e.g. high integration and high integrity
  Shifting redundancy management and communication into the hardware to reduce complexity and software overhead
  Reduce cost by cross industry approach essential to support the space domain
  Provide a standard solution to support all future needs from standard Ethernet – non safety critical to deterministic redundant Ethernet – safety critical to decrease the costs

## Slide 28
Vienna, Austria (Headquarters) | USA | Japan | China
Phone +43 1 585 34 34-0 office@tttech.com | Phone +1 978 933 7979 usa@tttech.com | Phone +81 52 485 5898 office@tttech.jp | Phone +86 21 5015 2925-0 china@tttech.com
www.tttech.com |  |  | 
Copyright © TTTech Computertechnik AG. All rights reserved.
Notes: altbacken