## Slide 1: Levels of Software Assurance in SPARK
Presented by Steve Baird
FSW 2017

## Slide 2: SPARK – Flow Analysis
Specification of effects
Flow analysis
Program implements specification

## Slide 3: SPARK – Proof
Specification of properties
Proof
Program implements specification

## Slide 4: Levels of Software Assurance

## Slide 5: Stone Level
Strong semantic coding standard
Program respects all the SPARK language legality rules
Enforces safer use of language features:
  Restricted concurrency (Ravenscar profile)
  Expressions and functions without side-effects
Forbids language features that make analysis difficult:
  Unrestricted pointers
  Exception handlers

## Slide 6: Bronze Level
Initialization and correct data flow
Program passes SPARK flow analysis without violations
Detects programming errors:
  Read of uninitialized data
  Problematic aliasing between parameters
  Data race between concurrent tasks
Checks user specifications:
  Data read or written
  Flow of information from inputs to outputs

## Slide 7: Silver Level
Absence of run-time errors
Program passes SPARK proof without violations
Detects programming errors:
  Divide by zero
  Array index out of bounds
  Integer, fixed-point and floating-point overflow
  Integer, fixed-point and floating-point range violation
  Explicit exception raised
  Violation of Ceiling Priority Protocol

## Slide 8: Gold Level
Proof of key integrity properties
Program passes SPARK proof without violations
Checks user specifications:
  Type invariants (weak and strong)
  Preconditions
  Postconditions
Checks correct use of OO wrt Liskov Substitution Principle

## Slide 9: Platinum Level
Proof of full functional correctness
Program passes SPARK proof without violations
Checks complete user specifications:
  Type invariants (weak and strong)
  Preconditions
  Postconditions
Checks loop termination (loop variant)

## Slide 10: Industrial Practice

## Slide 11: Established Practice at Altran UK
Software Integrity Level |  | SPARK Software Assurance Level |  |  | 
DAL | SIL | Bronze | Silver | Gold | Platinum
A | 4 |  |  |  | 
B | 3 |  |  |  | 
C | 2 |  |  |  | 
D | 1 |  |  |  | 
E | 0 |  |  |  | 

## Slide 12: Past Projects at Altran UK
C130J: 1996 - now
Bronze (Lockheed Martin) and Gold (UK RAF and BAE Systems)
iFACTS: 2006 - now
Silver (NATS)
SHOLIS: 1995
DEFSTAN 00-55 SIL4
First Gold

## Slide 13: Adoption Experiments at Thales
Use case 1: porting to new platform context: 300 klocs radar software target: Stone level significant manual refactoring (several days) on the way to completion on 300 klocs | Use case 2: demonstrate compliance to LLR context: small numerical function target: Gold level difficulties in expressing suitable contracts property was not proved automatically
Use case 3: identify and fix weakness context: 100s slocs code generator target: Gold level half a day to reach Silver property related to inner memory bounds two days to reach Gold | Use case 4: guarantee safety properties context: 7 klocs command & control target: Gold level one day to reach Silver property expressed as automaton four days to reach Gold

## Slide 14: Adoption Guidelines with Thales
For every level, we present:
  Benefits, Impact on process, Costs and limitations
  Setup and tool usage
  Violation messages issued by the tool
  Remediation solutions
Guidance was put to test:
  During adoption experiments at Thales
  On the example (SPARK tool) presented in last section

## Slide 15: Features that Matter

## Slide 16: Stone Level – Large Language Subset
SPARK_Mode => On
  Ada types, expressions, statements, subprograms
    SPARK_Mode => Off
      Ada pointers
      Ada exception handlers
  Ada generics
  Ada object orientation
  Ada concurrency
  Ada pointers
work in progress to include safe Rust-like pointers in SPARK
SPARK_Mode => On
  Ada types, expressions, statements, subprograms
    SPARK_Mode => Off
      Ada pointers
      Ada exception handlers
  Ada generics
  Ada object orientation
  Ada concurrency

## Slide 17: Bronze/Silver Level – Generation of Contracts
Example: SPARKSkein Skein cryptographic hash algorithm (Chapman, 2011)
target: Silver level
initial version (SPARK 2005) | current version (SPARK 2014)
41 non-trivial contracts for effects and dependencies | 1 – effects and dependencies are generated
31 conditions in preconditions and postconditions on internal subprograms | 0 – internal subprograms are inlined
43 conditions in loop invariants | 1 – loop frame conditions are generated
23 annotations to prevent combinatorial explosion | 0 – no combinatorial explosion

## Slide 18: Silver/Gold Level – Combination of Provers

## Slide 19: Silver/Gold Level – Combination of Provers
Example: Safe bounds on trajectory computation (submitted to VSTTE 2017)
target: Gold level

## Slide 20: Gold/Platinum Level – Auto-Active Verification
2
1
4
5
3
Example: Functional correctness of red-black trees (NFM 2017)
target: Platinum level
Auto-Active = portmanteau of Automatic and interActive
supported by ghost code: contracts, loop invariants,
intermediate assertions, lemma procedures
ghost code used to:
  define model of data used in specifications
  prove intermediate lemmas (e.g. for inductive proofs)
  provide witness for property (e.g. for transitivity relation)

## Slide 21: Gold/Platinum Level – Auto-Active Verification
Chart: 
| Binary Trees | Search Trees | Red-black Trees
Code | 92 | 127 | 67
Contract | 250 | 188 | 118
Ghost | 548 | 780 | 325

## Slide 22: Conclusion

## Slide 23: Levels of Software Assurance
From strong semantic coding standard to full functional correctness
Every level implicitly builds on the lower levels
Lower levels require lower costs/efforts
Good match from DAL/SIL to Bronze-Silver-Gold-Platinum
Adoption greatly facilitated by detailed level-specific guidance
Catchy names are easy to remember!

## Slide 24: SPARK Resources
SPARK toolset
http://www.adacore.com/sparkpro http://libre.adacore.com/
SPARK adoption guidance
www.adacore.com/knowledge/technical-papers/implementation-guidance-spark
SPARK blog and resources (User’s Guide)
http://www.spark-2014.org
SPARK online training
http://u.adacore.com