## Slide 1: Simulink Interface Layer (SIL) – Overview and Future
Steve Lentine GSFC 591 / Chesapeake Aerospace

## Slide 2: Agenda
SIL – “Simulink Interface Layer”
  Not “Software-In-the-Loop” in this context
Where did SIL come from?
What does SIL do?
How is SIL used?
Where is SIL headed?

## Slide 3: History of SIL
Ames created original version for LADEE mission in partnership with Mathworks
GSFC received SIL from Ames for use on NICER in 2013
  NICER software development completed in 2015, launched in 2017, currently operating.
  GEDI software development completed in 2017, expected launch 2019.
  PACE development starting, expected launch 2022.
  Several enhancements were necessary to meet GSFC mission requirements
    CFE GetTime support
    Remove Ames naming requirements
    Conditional Message sending
    Model reference support
    Multiple table support
    Support multiple command ApIDs
    Moved table definition out for csc_sl_interface.h
    TLC updated through release 2017a
Notes: This presentation is written by me from the Goddard perspective, so I’m not up-to-date on the activities at the other centers

## Slide 4: History of SIL (con’t)
Ames-SIL:
  Development continued for use on BioSentinel, RP rover, and drone project
  Several enhancements necessary to meet Ames mission requirements:
    Model variants and data dictionary integration
    Code cleaned up and optimized
    Simulink Buses include full CCSDS messages (similar to GSFC)
    Ansynchronous (conditional) messaging
    app_mid.h and csc_model_hz.h no longer needed
    Autogeneration of supporting files
      CMakeList.txt and cFS app folders
      cFE table file
      Install and Readme for cFS integration
JSC-SIL:
  Unknown capabilities/history
Notes: This presentation is written by me from the Goddard perspective, so I’m not up-to-date on the activities at the other centers

## Slide 5: SIL in Operation
Simulink Application
Bus Out
Event Signals
Bus In
cFE Software Bus
Event Processing
Other Apps / Mission Ops
cFE Event Services
Mission Ops
Queue
Cmd/Tlm Messages
Provide Sequence Numbers
Error Check Messages
SCH
Execute
House Keeping
Table Management
cFE Table Services
SIL
Mission Ops
cFE Time Services
Spacecraft Time
Fetch Time
Fault Flags
App
CFE
Tlm Data

## Slide 6: Autocoding Components
Model
  Contains task-specific code
  Includes blocks from CSL library to access CFE functionality
  Implemented by pointing team
Target Language Compiler (TLC) file
  Generates (model-specific) headers files for integration with (generic) SIL architecture
  Developed and maintained by Mathworks pilot engineers
Simulink Interface Layer (SIL)
  Generic wrapper code which provides interfaces between autocode and CFE
  Provides FDC reporting, CFE event generation, Message I/O handling, Table management
Notes: TLC file developed and maintained by mathworks pilot engineers

## Slide 7: GSFC Autocoding Workflow
Software requirements created by pointing team in partnership with FSW team
  Pointing team knows needed functionality to meet mission requirements
  These are FSW requirements, formally tested and verified by FSW test team
Pointing team develops and tests algorithms in Matlab/Simulink environment
  Use of existing GNC Simulink libraries
  High code reuse between FSW and High Fidelity Simulations (HiFi’s) which pointing team already produces
  Early end-to-end testing of models/code as they’re developed/implemented
Pointing team generates C code, delivers to FSW team for integration with FSW builds
At GSFC this CFE/SIL Autocoding workflow has been used on NICER and GEDI, and now PACE
Notes: Creating flight-software quality simulations does require additional effort from pointing team. Beneficial to have a specific FSW liaison on pointing team

## Slide 8: Model Development – Message Interfaces
Message Input
  Inport with datatype set to bus matching naming convention
Message Output
  Outport with datatype set to bus matching naming convention
Conditional Output Messages
  Pass through bus signal with conditional message to control
  Used to support asynchronous/periodic messaging

## Slide 9: Model Development – Table Interface
Table definition
  Define Simulink.Parameter object with datatype set to bus type matching structure
  GSFC-SIL will soon support multiple (separately managed) tables
Referencing parameters:
  Structure Field (direct reference):
  Structure Field (bus routing):

## Slide 10: Model Development – Time/FDC Interfaces
GetTime
  In simulation: returns simulation clock + epoch
  In generated code: calls CFE_GetTime to return FSW time
FDC reporting
  Fills fields of message to LC (Limit Checker)

## Slide 11: Model Development – Event Interfaces
CFE Event
  Generates event message

## Slide 12: Code Generation
Initial Setup:
  Configure code generation settings as specified in SIL users guide
    Use provided custom TLC template to generate interface header file
    Specify datatype size settings for hardware
  Click ‘Build’
  Deliver packaged code to FSW
Subsequent Builds:
  Click ‘Build’
  Deliver packaged code to FSW

## Slide 13: App Compilation
Initial Setup:
  Assign ApIDs values
  Assign PerfID values
  Add Wake-Up and HK request ApIDs to scheduler
  Add ApIDs to TO (Telemetry Output) tables
  Add application to startup script
  (Optional) Define table validation function
Subsequent Builds:
  Drag and drop new generated sources files
  Update Makefiles
  Compile

## Slide 14: Future of SIL
GSFC/Mathworks work currently underway:
  Finish implementation of multi-table support (expected in 2017)
  Refactor SIL implementation to move away from TLC (which Mathworks is slowly depreciating)
3 versions of SIL exist (that we know of….)
  GSFC-SIL
  Ames-SIL
  JSC-SIL
  Others??
Looking to unify into a NASA-SIL
  Currently gathering requirements for the unified SIL to address common needs for each center/group

## Slide 15: Splinter Meeting – 4pm
Splinter meeting at 4pm with GSFC, Ames, and Mathworks representatives to discuss path forward
Please attend if you have interest in using the SIL and/or defining requirements for future updates

## Slide 16: Thanks

## Slide 17: Backup

## Slide 18: Baseline SIL Requirements
Shall provide a method of receiving and issuing messages from/to the software bus
  Support asynchronous message output from model signals
  Support for arbitrary number of command APID in autocode
Shall utilize CFE Table Management to provide tunable parameters to model
  Support generation of table from Model Simulink.Parameter objects
  Support for management of multiple tables
  Support updating/validating via hand-coded table validation function
Shall provide a method of issuing events
  Support for setting Event ID, Mask, and Type
Shall provide a method of reporting FDC status
  Support for setting FDC ID, enabling/disabling by ID
  Automatic tracking of latch state, generation of telemetry packet

## Slide 19: Baseline SIL Requirements (con’t)
Shall support generation of housekeeping telemetry generation
  Includes command execution/rejection and packet counters
Shall support a method of accessing FSW time
  In simulation, block is a clock with settable epoch
  In codegen, results in hooks to get CFE time
Shall support code generation from a model reference hierarchy

## Slide 20: Future SIL Requirements?
Support for multirate model
  Current workaround is to separate rate groups into separate models/CFE apps
  Could potentially be supported via CFE Child Task API, but may be complicated
  If not officially supported, perhaps prepare ‘official’ recommendation and/or examples on how to implement these models
  APL request
Support for performance monitoring of sections of model
  Would be a block, placed into an atomic unit of the model (ie model reference, atomic subsystem)
  In simulation, would do nothing (or maybe run tic toc)
  In codegen, would code performance entry/exit API calls at the subsystem boundary

## Slide 21: Future SIL Requirements? (con’t)
Support for autogenerated table validation functions
  Utilize matlab coder to generate c code for a matlab function which implements checks on table parameters
Support for issuing events/getting time within Matlab blocks
  Supports alternative modeling paradigms
  Allows issuing events within Matlab-based logic
Support a method of logging FDC/Event signals
  In current implementation separate logging of these signals are required because blocks do not function in simulation mode
Direct generation of app from code generation
  Advantages: Simplifies integration of code since no separate code or header files are required… everything is generated
  Disadvantages: Code generation process must now be aware of CFS API and updated to match rather than using header file as interface between generated and hand code