## Slide 1: cFS Community Day Platform Technology Roadmap
JHU / APL
core Flight System Workshop
December 4, 2017
Alan Cudmore – NASA Goddard Space Flight Center

## Slide 2: Disclaimer
OSAL and PSP roadmaps
https://coreflightsystem.org/mapudates

## Slide 3: Agenda
What are we talking about?
  Platforms
    APIs
    Operating Systems
    Hardware
Where are we?
  Current Status
What’s next?
  Upcoming platform technologies
Current Device model thoughts
OSAL
PSP
cFE Core
cFS Apps/Libs

## Slide 4: What are we talking about?
The cFS is a set of portable libraries and applications that depend on the platform layer
The Platform Layer(s) consists of:
  APIs
    Operating System Abstraction Layer
    Platform Support Package
    Device Drivers
  Operating Systems
    Real Time Operating Systems
    Linux / Posix Operating Systems
    Partitioned Operating Systems
  Hardware
    Generic / Simulated ( Linux, VM, QEMU, etc )
    Class B processor platforms
    Cubesat / COTS processor platforms

## Slide 5: Where are we?
In a word – everywhere
The cFS project has a small number of supported platforms
  vxWorks 6.x on PowerPC ( MCP750 , RAD750 )
  RTEMS 4.10/4.11 ( Generic )
  Posix ( Generic Linux )
There are many other unsupported platforms
  GSFC Missions
    MMS ( RTEMS 4.10 / Coldfire )
    NICER / GEDI (vxWorks Broadreach PPC)
    Spacecube
    Dellingr Cubesat ( FreeRTOS / ARM )
    CeRES Cubesat ( Linux / ARM / Zynq )
    Balloon missions
  Many other missions and platforms outside of GSFC

## Slide 6: What’s Next?
Upcoming platform technologies to integrate (cFE is involved here as well)
  64 bit compatibility
  Cmake
  Next Generation OSAL
  Symmetric Multi Processing (SMP)
Operating systems to update or integrate
  RTEMS 4.11 / 5.0 – Dynamic Loading , SMP
  vxWorks 7.x - SMP
  FreeRTOS
  ARINC
  Xenomai
Hardware Platforms
  Many Cubesat Platforms
  LEON4
  High Performance Spacecraft Computer (HPSC)
  And many more..

## Slide 7: What’s Next – Short Term?
  OSAL
    Next Generation OSAL
    SMP Support ( Linux, vxWorks, RTEMS )
    vxWorks 7.0 support
    RTEMS 4.11/5.0 Support including the dynamic loader
    FreeRTOS port from Dellingr and STF-1
  PSP
    Cmake / Next Gen / 64 bit support
    SMP Support
    vxWorks / Generic
    RTEMS / Generic
    FreeRTOS / Generic ( Is there such a thing? )
    Device/Plugin model?
      Smallsat group is considering adding portable SPI/I2C/UART/GPIO interfaces

## Slide 8: What’s Next – Long Term?
Long(er) Term Platform work
  Document the PSP APIs
  Create a PSP integration test suite
  Create a PSP Porting guide
  Formalize a PSP device model
Need to keep the OSAL and PSP APIs relatively simple
  This will be key to the maintenance and portability to all platforms
How can we create a sustainable collection of OSAL and PSP ports?
  Operating Systems and Platforms
    What can we reasonably support?
    Simulators (QEMU, etc) may be the key to testing and maintaining platforms
  Support a limited number of important operating systems
  Support a limited number of hardware platforms and simulators

## Slide 9: Current Device Model Thoughts
OS Abstraction Layer
Platform Support Package
RTOS Board Support, File Systems, Drivers, Firmware Libraries, etc
core Flight Executive (cFE)
Processor , Memory, Peripherals, and other hardware
Real Time Operating System
Mission Hardware Library
( All Mission hardware accessed through this library)
cFE/cFS
Legend:
Vendor Supplied
cFE/cFS Reuse
New on Dellingr
cFS
Reuse
App
Mission
App
Dellingr Cubesat Model
42 Simulator

## Slide 10: Current Device Model Thoughts
OS Abstraction Layer
Platform Support Package
RTOS Board Support, File Systems, Drivers, Firmware Libraries, etc
core Flight Executive (cFE)
Processor , Memory, Peripherals, and other hardware
Real Time Operating System
Mission Hardware Library
( All Mission hardware accessed through this library)
cFE/cFS
Legend:
Vendor Supplied
cFE/cFS Reuse
New on Dellingr
cFS
Reuse
App
Mission
App
SPI, I2C,
UART,
GPIO Model
Goddard Smallsat Device Model – Adding common device APIs
Mission
App
Mission
App
Mission
App