## Slide 1
Advanced Exploration Systems (AES)
Core Flight Software (CFS) Project
CFS Product Highlights
CFS Projects @ JSC
Upshots of SW development with CFS
Tam Ngo/Software Manager
NASA/Johnson Space Center (JSC)
Software, Robotics & Simulation Division
Spacecraft Software Engineering Branch (ER6)
December 2018

## Slide 2: CFS Product Highlights
Generic Command Ingest (CI) & Telemetry Output (TO) CFS applications
  Can be easily expanded and customized
  Supports multiple channels
  Supports multiple communication protocols: UDP, TCP & RS-422
  Supports CCSDS Space-Data Link Protocols: TM-SDLP, TC-SDLP, COP-1
  Works with CFDP (CF) application to do CFDP file transfers
Time-triggered scheduler (SCH_TT) CFS application
  Uses TTE network scheduling for scheduling messages

## Slide 3: CFS Product Highlights (cont.)
Software Bus Network (SBN) CFS application
  A collaborative work with Ames Research Center (ARC)
  Serves as a data bridge between cFS systems
  Makes distributed network of cFS systems possible
  Supports multiple communication protocols: UDP, TCP, serial
Protobetter tool
  Generates code for serializing/de-serializing CCSDS messages for transmission across the network
  Generated code is compiled into its own CFS library
  Works with CDD databases to access message definitions
  Can run stand-alone if given message definitions
  Is used by the SBN application, and eventually CI & TO applications

## Slide 4: CFS Product Highlights (cont.)
Command & Data Dictionary (CDD) Tool
  Is used to define system command & data definitions
  Information is stored in a relational database, PostgreSQL
  Provides a set of APIs for users to access the data via scripts
  Provides a set of standard scripts that can be customized to generate output files like C headers, XTCE files, copy tables for HK application, and eventually, scheduling tables for SCH application.
  Available at https://github.com/nasa/CCDD
CFS-101 Training
  A self-guided training package
  Comes with a virtual machine as the tutorial workspace & a step-by-step tutorial guide
  The virtual machine is equipped with the latest CFE, OSAL & PSP from https://sourceforge.net and all the necessary CentOS libraries.
  Available at https://github.com/nasa/CFS-101

## Slide 5: CFS Projects @ JSC
Orion Multi-Purpose Crewed Vehicle (MPCV)
  Class A, safety-critical FSW
  Vision Processing Unit (VPU) Flight Computer
    VxWorks on Leon3 SPARC processor
    Backup Flight System (BFS) apps
  Camera Controller Units
    Ubuntu Linux on I5 Intel processor
    Optical Navigation (OpNav) app
Orion Ascent & Abort 2 (AA2) Flight Test (May 2019)
  Class B, safety-critical FSW
  VxWorks on SP0 PPC processors

## Slide 6: CFS Projects @ JSC (cont.)
Advanced Extra-vehicular Mobility Unit (xEMU) Flight Experiment – Caution & Warning System (CWS)
  Class A, safety-critical FSW
  VxWorks on Leon3 SPARC processor
  An advanced space suit
Seeker Flight Experiment on ISS (July 2019)
  Class C, non-safety-critical FSW
  Wumbo GNU/Linux on CHREC space processor
  An external, free-flying robotic inspector
Certification of cFE on VxWorks ARINC-653
  Class A, safety-critical FSW
  VxWorks ARINC-653 on SP0 processor
Avionics & Software Platform for Exploration Capabilities & Technologies (ASPECT) as ISS payload
  Class C, non-safety-critical FSW
  VxWorks on SP0-S processors

## Slide 7: CFS Projects @ JSC (cont.)
AES integrated testing project
  A&S platforms for multi-center collaborations to integrate autonomous systems & operations in a distributed run-time environment
Next Space Technologies for Exploration Partnerships (NextSTEP) program
  Seeks commercial development of deep space exploration capabilities
  Assists private companies in applying NASA-invested technologies to develop their capabilities

## Slide 8: Upshots of SW Development with CFS
From SW development perspective,
Having a common SW framework increases SW productivity
  Modular application code with the same “look-n-feel”
    Same code template
    Same naming conventions
      File names, function names, message ID names, command code names
    Same build template
    Same source directories
  Minimal time to stand up an initial running system from scratch before any mission-specific capabilities are implemented
    SW re-use actually works and with minimal effort !
  Quicker to get up to speed with the new project for CFS-experienced developers, even when joining at a later phase of the development life cycle
    Already familiar with the code setup
    Can detect & fix application bugs in shorter time
    Know where to look
  Easier to pre-train newbies to become CFS-proficient before they join the project

## Slide 9: Upshots of SW Development with CFS (cont.)
From SW development perspective (cont.),
Collaborations within the CFS user community
  Enable tool & code sharing
    Increase the level of SW re-use at minimal cost
    Open source SW makes this possible
  Dissemination of lessons learned & best practices
    The TODOs and the NOT-TODOs
    Minimize development risks
  Provide leverage for future projects with current & past projects
    Emulate the existing system HW/SW configurations or tweak it to suit the new missions’ needs

## Slide 10: Upshots of SW Development with CFS (cont.)
From project management perspective,
Making use of high quality flight software
  CFS has its pedigree in flight software!
    CFS has been tested, certified & flown in space in numerous HW/SW configurations.
Better grip on SW development schedule & risk mitigation
  Using metrics, lessons learned & best practices from other CFS projects to help planning for new CFS projects
Increase in management buy-ins on new SW projects that use CFS framework
  Costs & schedules of past & current CFS projects show the productivity, benefits & effectiveness of the paradigm
  Increasing number of CFS projects that are at various level of certifications