## Slide 1: Core Flight Software Projects on Orion Multi-Purpose Crew Vehicle
Flight Software Workshop
December 3, 2018
Lorraine E. Prokop, Ph.D
NASA – Johnson Space Center / ER6
lorraine.e.prokop@nasa.gov

## Slide 2: Outline
Orion Program Overview
CFS Projects on Orion
  Orion Ascent Abort 2 Flight Test
  Optical Navigation Software
  Backup Flight Software

## Slide 3: Orion Vehicle

## Slide 4: Orion Program Mission Schedule (Wikipedia)
Mission | Acronym | Rocket | Crewed | Launch date | Status | Duration | Destination
Pad Abort 1 | PA-1 | Orion LAS | No | May 6, 2010 | Success | 95 seconds | Troposphere
Exploration Flight Test 1 | EFT-1 | Delta IV Heavy | No | December 5, 2014 | Success | 4 hours, 24 minutes, two orbits | High Earth orbit
Ascent Abort Test 2 | AA-2 | Orion Abort Test Booster | No | April 2019 | Under development | Less than 3 minutes | Stratosphere
Exploration Mission 1 | EM-1 | SLS Block 1 Crew | No | 2020 | Under development | 26–40 days | Lunar orbit
Exploration Mission 2 | EM-2 | SLS Block 1B Crew | Yes | 2023 | Under development | 8–21 days | Multi TLI free-return flight
Exploration Mission 3 | EM-3 | SLS Block 1B Crew | Yes | Between 2023 and 2024 | Planned | 16–26 days | Gateway station
Exploration Mission 4 | EM-4 | SLS Block 1B Crew | Yes | 2025 | Planned | 26–42 days | Gateway station
Exploration Mission 5 | EM-5 | SLS Block 1B Crew | Yes | 2026 | Planned | 26–42 days | Gateway station
Exploration Mission 7 | EM-7 | SLS Block 1B Crew | Yes | 2027 | Planned | 191–221 days | Gateway station
Exploration Mission 9 | EM-9 | SLS Block 2 Crew | Yes | 2029 | Planned | 1 Year | Lunar orbit
Exploration Mission 11 | EM-11 | SLS Block 2A Crew | Yes | 2033 | Planned | 2 years | Martian orbit
Current CFS Projects in Development/Test

## Slide 5: Exploration Mission 1 Overview

## Slide 6: Exploration Mission 2 Overview

## Slide 8: CFS Projects On Orion
CFS Projects on Orion Missions
  Orion Ascent Abort 2 Flight Test
    CFS Framework for Primary Flight Software
    Hardware: AiTech SP0 processor
    Operating System: VxWorks
  Orion Exploration Mission 1 & 2
    Vision Processing Unit (VPU)
      Backup Flight Software
        EM-1: Entry phase, EM-2 & beyond: All Flight Phases
      Hardware: Sparc LEON 3
      Operating System: VxWorks
    Camera Controller Units – Crew Module & Crew Module Adapter
      Camera controlling software (still image & motion video)
      Optical Navigation Software
      Hardware: Intel I5 NUC
      Operating System: Ubuntu-64

## Slide 9: AA-2 Project Introduction
Ascent Abort 2 (AA-2) Flight Test
AA-2 is a Development Flight Test for the Multi Purpose Crew Vehicle (MPCV) Program
Single launch planned for April 2019 from Space Launch Complex 46
AA-2 will test the LAS under flight-like conditions to help certify the system for crewed missions
AA-2 uses a surrogate low cost, less complex booster and Crew Module
AA-2 Avionics & Software
Designing to use COTS avionics wherever possible
Dual string design using cFE/CFS on VxWorks
Reuse of ANTARES Trick Simulation
CFS wrapped GNC Matlab/Simulink Autocode from mainline MPCV
Apollo Pad Abort Test
Apollo Ascent Abort Test
(Little Joe II Booster)
Orion Pad Abort Test
AA-2 Flight Test Vehicle
Orion
Notes: The purpose of this slide is to provide objective evidence of and/or support the accomplishment of the following CMMI requirements:
  IPM-IPPD SG 1Use the projects Defined Process
  IPM-IPPD SG2 Coordinate and Collaborate with Relevant Stakeholders
  IPM-IPPD SG3 Apply integrated product & process development
  GP 2.3 Provide Resources
  GP 2.4 Assign Responsibility
  GP 2.7 Identify and Involve relevant stakeholders

## Slide 10: AA-2 Flight Test Profile
Event Description
1 ATB ignites.
Vehicle departs on eastward trajectory.
ATB boosts the FTA to the test condition.
2 Test Condition is reached
ATB sends signals to the FTA
CM triggers the abort event.
CM ignites the LAS AM and ACM
CM separates from SR
LAS propels CM away from ATB.
3 LAS AM burns out.
CM/LAS continue coasting to apogee.
While coasting,
ACM reorients CM heat-shield forward.
4 CM/LAS reorientation is completed.
5 CM ignites LAS JM
CM separates the LAS from the CM
LAS is jettisoned away from the CM.
6 ATB, LAS, and CM free-fall into the ocean.
Flight Test is completed.
No planned recovery. Will depose
of items that are hazards to marine navigation
Note: Trajectory and event times are based on preliminary data.
AA-2 Flight Test Profile

## Slide 11: High-Level AA-2 Avionics Architecture
Flight Computer 1
PCU, Battery
CM – Crew Module
Cmd - Command
LAS – Launch Abort System
PCU – Pyro Control Unit
DFI – Development Flight Instrumentation
SIGI – Space Integrated GPS/INS
GPS – Global Positioning System
INS – Inertial Navigation System
Tlm - Telemetry
PDU – Power Distribution Unit
Pyros
1553 Bus
Flight Computer 2
PCU, Battery
PDU
DFI
SIGI
SIGI
Ethernet & RS422 Busses
EDR
CM & LAS Interface, RS422 & Discrete Pyro
LAS

## Slide 12: AA-2 Top Level Software Block Diagram
12
Linux OS
Command & Data Dictionary
ITOS Infrastructure (Goddard)
(Data Com/Decom, Recon, Distribution, Display, Scripting, Recording, Post processing)
Linux OS
Displays & Controls
Database
(postgreSQL)
Simulation Software
Ground Software
AA-2 Custom Applications
CFS Core
Apps
Custom
Sensor/
Effector
Apps
CFS Infrastructure (Goddard)
I/O Devices (NAI)
VxWorks Operating System
C/C++
Flight Software
  VMWare (local PC/Mac)
  Eclipse (local IDE)
  Scientific Linux (local WS OS)
  GNU C/C++, Java (compile/Xlate)
  UCC (code count metrics)
  Understand (standards checker)
  Bitbucket/Git (CM)
  JIRA (change tracker)
  Bamboo (continuous integration)
  mREST (Test Framework)
  Windriver Workbench
Tool Chain
Dynamics, Time, Environment Models
Generic Systems
Models
Specific System & I/O Models (RAMTARES)
Scripts
Aitech SP0 Processor, cPCI
Open Source
C++
JEOD
Valkyrie
Trick Simulation Core (JSC)
EDGE Visualization
Test Framework
Java
Decom System
Linux OS
Payload Telemetry Processor
12->8 bit down select & packetization
MPCV GNC Autocode
EDR
Rasberry Pi
AA-2 Custom Application
C/C++
Notes: Simulation: Changed ANTARES to RAMATRES
Added Decom box
Put TBD next to hudson and C++ test in tool chain box

## Slide 13: AA-2 Flight Software Architecture
Command
Ingest
(10 Hz)
Telemetry
Output
(40 Hz)
Executive
Services
Event Services
Table
Services
A IO
(40Hz)
Mission Specific Apps
cFE Core Services
CFS Configurable Applications
Mission Specific I/O Apps
Time
Services
SIGI
IO
(40 Hz)
Software
Bus
Inter-task Message Router (SW Bus – Publish/Subscribe)
D IO
(40 Hz)
GNC 40 Hz
(40Hz)
SIGI
Automated
Flight
Manager
(AFM)
(40Hz)
SSRs, Avionics temps, voltage, etc.
1553
DFI
Framed CCSDS
1.28 Mbps (combined)
Scheduler /
Sync
(40 Hz)
House-
Keeping
(10 Hz)
GNC 1 Hz
(1Hz)
Pyros, ATB discrete signals
LAS I/O
(40 Hz)
Manchester Encoded
RS-422
RS-422 (two channels)
Launch Abort System
Ethernet
EDR
IO
(40 Hz)
EDR
RS-422
Telemetry
Output Serial
(40 Hz)

## Slide 14: Optical Navigation Project Overview - Background
Optical Navigation (OpNav) Application Software
  NASA/JSC/Engineering Directorate Government Furnished Equipment (GFE) software project authorized October 2016, delivered April 2018
  Orion (EM-1, EM-2) software producing navigation data for onboard GNC flight control in the event of loss of communication with ground
    Determines position and range of spacecraft based on optical image recognition of either earth or moon from images taken by dedicated fixed-mounted camera (Pixelink) on bottom of Orion Command Module
    Self calibrates images onboard prior to navigation use by imaging starfields, high accuracy required
  Functions as Orion backup navigation sensor in the event of comm loss
    Orion requires nav updates from ground, if comm is lost, poses LOC/LOM risk during entry
    Provides autonomous navigation updates upon Loss of Comm
    Class A Safety-Critical Software
  For EM-1, images taken every 30s during approximately 8, 2-hour “passes”
    Dedicated “calibration passes” image star field to determine camera distortion & orientation
    Dedicated “imaging passes” image earth or moon to derive navigation solution
    Function validated on “outbound leg” to moon for EM-1, evaluated as a DTO for this phase
    Activated on the “inbound” from moon for loss-of-comm
      Solution fed to Orion FCM-GNC and downlinked
  Located in Camera Controller (CC) unit on Orion EM-1 vehicle, Linux computer running the Core Flight Software (CFS) framework

## Slide 15: How Optical Navigation Works
Apollo
Space Sextant
Still images of Moon or Earth are processed to find apparent angular diameter and centroid in camera focal plane
Raw data is transformed into range and bearing angle measurements using planetary data and precise star tracker inertial attitude
Measurements are sent to the main flight computer’s Kalman filter to update the onboard state vector
Images are collected over an arc (~2hrs) to converge the state and estimate velocity
The same basic technique was used by Apollo to satisfy loss-of-comm, but Apollo used manual crew sightings with sextant instead of autonomously processing optical imagery

## Slide 16: Loss of Comm Navigation

## Slide 17: MPCV Camera Locations
Star Tracker & OpNav Camera Locations

## Slide 18: OpNav System Architecture

## Slide 19: OpNav Application Software Architecture
File System
Mass Storage
Video,
Still Imagery
Executive
Services
Time
Services
CFS Application Framework (32-bit)
Inter-task Message Router
(Software Bus – Publish/Subscribe)
Software
Bus
Data
Storage
(DS)
Table
Services
File System
Imagery
CFDP
-File
Transfer
Scheduler
(Sch)
File
Manager
(FM)
Video System (VID) Apps
CFS Core Services
CFS Reuse Apps
Camera
Controller
App
OpNav App & Data
OpNav
(1 Hz)
OpNav
Application
Software
cFE (core Flight Executive)
Services
CFS Reuse
Apps
Other
Mission Specific CFS Apps
Operating System Abstraction
Layer (OSAL)
Platform Specific Package
(PSP)
Application
Layer App
OpNav
FileData
Stored
Command
(SC)
House-
Keeping
(HK)
Data To/From Vehicle Systems
Data To/From Ground
External I/O Apps:
DEM telem
DEM cmd
UDP I/O
(via Data Util Network)
VEPC I/O (via RS-422)
GoPro
App
OpNav within
CFS Layered Framework
Pixelink OpNav Camera
Pixelink Camera Drivers, I/O Apps
(64-bit)
OpNav
App

## Slide 20: Orion EM-1 OpNav Pass Visualization

## Slide 21: Practice Earth Pass Sample Image, Trajectory Time 39065

## Slide 22: 8.5.5 Cert 2 Backup Moon Pass Sample Image, Trajectory Time 415275

## Slide 23: Sample Off Nominal – Earth and Moon in Image during DRO

## Slide 24: Sample Off Nominal / VT-Image – Over-Underexposures (exposure bit) for each Pass

## Slide 25: Orion Backup Flight Software
Human-rated spacecraft require high degree of redundancy / fault tolerance
  Redundant hardware systems (example: quad-voting systems)
  Redundant software systems
    If primary software fails to operate, backup system is needed
    Backup Flight Software (BFS) exists to mitigate the risk of software common cause failure in the primary flight system
      Strive for dissimilarity in all life cycle phases, process, tools, platform, etc.
Orion backup software
  EM-1 BFS written to support backup during Entry
  EM-2 BFS will be expanded to support all flight phases
    EM-2 project started October 2018
      Joint team with NASA and Lockheed-Martin (Orion prime contractor)
        Mix of C & C++ applications running within CFS framework
        LEON3 processor
        VxWorks OS
    Reduced set of capabilities compared to primary, but can “take over” in event of a primary software failure
      Complete/perform dynamic flight events such as ascent, entry, and burn targeting
      Maintain knowledge and control of vehicle attitude and state during quiescent flight phases
      Maintain control of life support, power, and communication systems
      Monitor and mitigate crew environmental hazards
      Provide manual commanding and piloting capabilities to the crew

## Slide 26: Orion BFS vs. Primary Toolchain
Item | BFS | Primary FSW
Hardware and Operating System |  | 
CPU | LEON 3 | PPC-750
Operating System / compiler | VxWorks | Green Hills Integrity
Framework | CFS Framework | ARINC653
Development Tools / Language |  | 
Algorithm Implementation | Hand-Coded | Auto-generated C++
Development Environment(s) | Eclipse, VxWorks Workbench | Rhapsody/Green Hills
Programming Language(s) | C or C++ | C++
Software, Documentation, and Data Configuration Management |  | 
Data Management | CCDD -> ODS | ODS
In-Flight Reconfiguration | CFE tables | SLDB
Documentation Storage | NASA SharePoint, Windchill | Windchill
Requirements Linkage | Excel, DOORS | Rhapsody, DOORS
CM | Git -> Perforce | Perforce
Documentation Tools | Microsoft Office, Doxygen, DOORS, Windchill | Rhapsody, DOORS
Integration, Test, and Simulation |  | 
Unit Test Framework (UTF) | GoogleTest & UTAssert | LDRA
Code Coverage | gcov (Linux and VxWorks) | LDRA
Static/Standards Analysis | ucc code check, cpp check | Klockwork
Code Review | Gitlab, Crucible / Code Collaborator | Crucible/Code Collaborator
Simulation / Test | RAMTARES, CFS Test Framework, OrionSim | OrionSim
Development Process / Standards |  | 
Coding Standards | C – NASA, C++ - Orion SDP | Orion SDP
Software Development Process | NPR 7150.2B, BFS SDP Addendum | NPR 7150.2, Primary SDP

## Slide 27: High-Level Orion Avionics Architecture
VMC
FCM
FCM
DCM
CCM
ACU – Audio control Unit
CC – Camera Controller
CCM – Communications Control Module
CFS – core Flight Software
DCM – Display Control Module
DU – Display Unit
FCM – Flight Control Module
FSW – Flight Software
ODN – Onboard Data Network
VMC – Vehicle Management Computer
VPU – Vision Processing Unit
DU
DU
DU
CC
CC (opnav)
VMC
FCM
FCM
DCM
CCM
Utility Network
VPU
Backup Flight Software
VxWorks, CFS, Leon3
Primary FSW
Integrity ARINC653 OS,
PPC 750
ACU
ACU
Onboard Data Network (time triggered)

## Slide 28: EM-2 Backup Flight Software Architecture within VPU’s CFS Framework (Planning Purposes)
MD
(Memory
Dwell)
HS
(Health &
Safety)
Time
Services
CFS Software Bus
File System
BFS-Mission Specific Apps/Sequences
CFS Core Services
CFS Reuse Apps
Data To/From ODN
CF
(CCSDS
File Xfer)
DS
(Data Store)
FM
(File
Manager)
stor
CS
(checksum)
refs
HK
(house-
keeping)
LC
(Limit-
Checker)
(EM-1 only)
MM
(Mem-
Mgr)
SCH
(Scheduler)
vpud
SCB
(Stored Command –
Sequencer)
(40Hz)
LCB
(BFS Limit
Checker)
(hazards)
BEX
(BFS
Executive)
NAV
(Navigation)
GCE
(Entry Guid &
Ctrl)
gnc apps
MP (Manual
Piloting)
MC
(Manual Commanding &
Routing)
CSM (SM Control)
VPUD Mission Specific Applications
EM1 BFS Apps/Sequences
ECS
(Environment
Ctrl &Suits)
SOL -Solar
Arrays & Pwr
Mon&Ctrl
Table
Services
Excutive
Services
Software
Bus
cfe
Vpud apps
DemCmd
DemTlm
Diag
SBNx
UDP
VHC
Cmt
Odl
PRP
(Prop
Mon & Mgmt)
GSM
(SM Guidance)
MULTIDISIPLINARY
Custom App (BFS & VPU requirements)
  BFS condition & hazard monitoring
  Mode change events
  Sequence Triggering
  Possible refactor BEX from EM-1
40 Hz
40 Hz
40 Hz
40 Hz
1 Hz
40 Hz
40 Hz
40 Hz
10 Hz
1 Hz
20 Hz
BFSLib
(C++, C?
Lib)
BIF
BFS I/F
Lib)
GNCLib
(Common
GNC)
BFS Libraries
bfs shared libs
IOlib
cpplib
CFSlib
ODNlib
Vpud libs
MULTIDISIPLINARY
Modified SC for higher rate time response, sub second times
Multi-Discipline Cmd Sequences (RelTime & AbsTime:
  Ascent Sequences
  Entry Sequences
  Config heaters
  Config pressurization
  Manual Burn Attitude
  BFS Config sequences
  CM RCS prop pressurize
  Functions of EVE (EM-1’s EVE App refactored possibly)
  Possible Incorporate BEX from EM-1
CFS Framework & apps VPU and CC/VID

## Slide 29: Backup
Questions?