## Slide 1
Core Flight System (cFS)
Platform Update
FSW Workshop 2018
Alan Cudmore
December 3, 2018

## Slide 2: Agenda
Background
State of cFS Platforms
  Current Supported Platforms
  Current/Upcoming Platforms for GSFC Projects
Planned cFS Platform Updates – Near Term
  Generic Platform Updates
  Operating System Updates
Planned cFS Platform Updates – Medium/Long Term
  API Documentation and Porting Guide
  Platform Support Package Integration Test Suite
  File Systems support – EEFS and others
On the Radar – Unknown Timeframe
  FreeRTOS ?
  Static Loader?
  Support for Constrained resource environments
  What platforms would you like to see supported?

## Slide 3: Background
A cFS Platform refers to:
  The Operating System Abstraction Layer (OSAL)
  The Platform Support Package (PSP)
  And the underlying:
    Operating Systems / board support packages
    Device drivers
    File Systems
    Development tools
For a cFS project or mission, the OSAL should not have to be modified.
For a cFS project or mission, there will be some level of customization required to the PSP
With proper documentation, test suites, and a way to independently release PSPs, it should be possible to develop and exchange PSPs without them being part of the “official” release.
A goal of the cFS project to provide complete OSAL implementations and reference Platform Support Packages to serve as project starting points

## Slide 4: State of cFS Platforms (1)
Current Supported cFS Platforms
  Operating Systems
    POSIX/Linux
    RTEMS (4.10/4.11)
    VxWorks (6.9)
  Reference Platform Support Packages
    mcp750-vxworks6.4
      Original board and OS that cFE was developed on
    sp0-vworks6.9
      Freescale 8548, e500 core VxWorks 6.9
      This is an updated platform to replace the MCP750
    pc-linux
      Used as the starting point for a number of linux based platforms (x86, ARM, microblaze, etc)
    grut699-vxworks6
      Early work used in porting the cFS to the LEON3/VxWorks GR699 development board
    pc-rtems
      RTEMS 4.11 / i686 QEMU

## Slide 5: State of cFS Platforms (2)
Current/Upcoming GSFC Project Platforms
  Completed CubeSats:
    Dellingr – In orbit for over 1 year
      FreeRTOS 9, Gomspace Nanomind A712D
      This is not a complete platform port, and has not been merged into the cFS repositories
    STF-1 – Delivered for Launch – target date 12/2018
      FreeRTOS 9, Gomspace Nanomind A3200
    CeREs – Delivered for Launch – target date 12/2018
      Cubesat/Chrec Space Processor Xlinux Zynq – ARM A9 Linux
  Upcoming Cubesats:
    PetitSat amd BurstCube
      Cubesat Space Processor Xilinx Zynq – ARM A9 Linux
    GTOSat
      Custom LEON3-FT / RTEMS
  GEDI / NICER
    PowerPC 440 / VxWorks 6.7
  PACE / OCI
    MUSTANG (custom LEON3 Dual core + LEON3-FT in RTG4 FPGA) / VxWorks
  WFIRST
    Custom LEON4 / RTEMS 5.x

## Slide 6: Planned cFS Platform Updates Near Term (1)
Generic Platform Updates
  Symmetric Multi Processing (SMP) Support
    Updates to OSAL API, PSP, and cFE Core Executive Services were made during a joint GSFC/APL IRAD
    These updates have been integrated into the latest OSAL/PSP/cFE Core releases for the PACE project
    The cFS community is currently evaluating these changes and developing an integration plan for the next official releases
  OS Abstraction Layer Next Gen (OSAL NG)
    The OSAL ”Next Gen” is an API compatible OSAL refactoring that:
      Eliminates redundant code in the OSAL
      Makes it easier to port the OSAL to new operating systems
    The OSAL NG drops in to the source directory and co-exists with the current OSAL
    Has been advanced to the development branch in the bablefish repository
    Targeting the next release
  Network Stream API in the OSAL
    Used to abstract network socket communication

## Slide 7: Planned cFS Platform Updates Near Term (2)
Upcoming Operating System Updates
  RTEMS
    Update to RTEMS 5.x
    Support SMP
    Support the new Dynamic Loader
    Consider switching to the “self contained” mutexes for performance
  VxWorks
    Support SMP in VxWorks 6.9
  Linux
    Support SMP
    Xenomai support?
Goal: To have easy to use reference platform support for VxWorks, Linux/POSIX, and RTEMS 5.x

## Slide 8: Planned cFS Platform Updates Medium to Long Term
API Documentation and Porting Guide
  The PSP API document and Porting Guide are long overview
  Goal is to make some progress on this in FY19
Platform Support Package Integration Test Suite
  A PSP integration test suite would help validate new PSPs
GSFC Compatibility/Test lab
  Would like to start building up a GSFC compatibility lab
Goal: Provide the tools that the users need to develop and test Platform Support Packages for unique missions

## Slide 9: On the Radar Unknown Time Frame
FreeRTOS support ?
  There is continued interest in cFS on FreeRTOS
  Requires extra components
    Dynamic Loader
      GSFC Static Loader or NuttX elf module loader
      Or just support single binary images without dynamic loading
    File System API
      Ideal would be a Virtual File System Layer (VFS)
    File systems
      RAM Disk (fatfs with ram driver)
      Non Volatile disk for tables and startup script
        Could use GSFC EEPROM File System
Simplification of the OSAL file system code?
  Lightweight layer over the POSIX file system API
  Simple path mapping API instead of volume table
  Do not have code in OSAL to create and format volumes
GSFC Static Loader and EEPROM file system?
  Both used on MMS
  Static loader used on Dellingr

## Slide 10: On the Radar Unknown Time Frame
Device Abstraction ideas
  Several ongoing efforts, but no official direction
  Hopefully more traction in FY19
What platforms would you like to see supported?
  ARINC 653 reference platform integrated into the official repositories?
  NuttX, Zephyr RTOS?
  cFS for Resource constrained environments?