## Slide 1: Using CCDD to Automate Software development on AA2
Robert Hirsh
Robert.l.Hirsh@nasa.gov
NASA/ Johnson Space Center
12/3/2018

## Slide 2: Agenda
AA2 Background
cFS Command and Data Dictionary (CCDD) Overview
CCDD Products used on AA2
Development on AA2
Next Steps

## Slide 3: Ascent Abort 2 (AA-2)
AA-2 is a development flight test for Multi Purpose Crew Vehicle (MPCV)
  Launch planned for May 2019 from Space Launch Complex 46
  AA-1 test was dropped, but AA-2 was not renumbered
  Pad Abort 1 (PA1) demonstrated similar LAS functionality from a launch pad. (May 2010)
Largely a test of the Launch Abort System (LAS) on Orion
  Safety system to quickly separate crew capsule from the Booster (during a failure)
  Verify LAS works under flight-like conditions to help certify system for crewed missions
Two identical CPU’s running, only 1 is required (redundancy)
  Each CPU is cFS instance running on vxWorks ( on a PPC)
  Each CPU has separate serial link to the LAS, but only 1 is needed (redundancy)
  Code is essentially identical on each computer, but each computer used a different value for each MID that it sends on the Software Bus (SB)
Notes: since various groups use various types of computer hardware (32/64-bit, big/little endian, Linux/VxWorks/Windows) many additional complications exist in interfacing all the various components into a final integrated system. cFS is used on the majority the flight software (FSW) in running in Habulous.

## Slide 4: AA-2 Background
AA-2 Avionics & Software
Designed to use COTS avionics wherever possible
Dual string design using cFE/CFS on VxWorks
Reuse of ANTARES Trick Simulation
CFS wrapped GNC Matlab/Simulink Autocode from mainline MPCV
Apollo Pad Abort Test
Apollo Abort Test
(Little Joe Ascent II Booster)
Orion PA-1 Test
AA-2 Flight Test Vehicle
1
2
3
4
5
6
7
8
9
10
11
12
5,000
10,000
15,000
20,000
25,000
30,000
35,000
40,000
45,000
13
50,000
Downrange (statute miles)
Altitude (feet)
1
ATB
Ignition
2
Begin
Reorientation
3
4
Reorient
Complete
5
LAS
Jettison
6
ATB
Impact
LAS
, CM Impact
Initiate Abort
LAS/CM Separate from ATB
6
6
Notes: The purpose of this slide is to provide objective evidence of and/or support the accomplishment of the following CMMI requirements:
  IPM-IPPD SG 1Use the projects Defined Process
  IPM-IPPD SG2 Coordinate and Collaborate with Relevant Stakeholders
  IPM-IPPD SG3 Apply integrated product & process development
  GP 2.3 Provide Resources
  GP 2.4 Assign Responsibility
  GP 2.7 Identify and Involve relevant stakeholders

## Slide 5: CCDD Background
CCDD stands for cFS Command and Data Dictionary
Goddard’s Core Flight System (cFS) has been, is, and is intended to be used by many projects
  Examples: Lunar Reconnaissance Orbiter (LRO), Morpheus, Exploration EMU (xEMU) spacesuit, Orion Backup Flight Software (BFS)
  Success of the cFS concept is shown by the number cFS projects at FSW-2018
A command and data dictionary (CDD) defines telemetry/command messages
Each cFS project must select a way to manage their CDD
  Frequently involves using a spreadsheet, with custom SW to convert into useful files
cFS Command and Data Dictionary utility (CCDD) was designed as a generic utility to eliminate duplication of effort in order to make CDD management easier

## Slide 6: CCDD Goals
Create a configurable CDD utility that runs on multiple operating systems
  Written in Java for maximum portability
Easy creation/modification of CDD information
  Graphical user interface (GUI) to interact with the database
Store all CDD information into a standard database (postgreSQL)
Bidirectional transfer of information to/from the CCDD
  Cut-n-paste to Excel, import/export via XTCE/CSV/JSON
Easy access to CDD information (via scripting languages and web applications )
  Allows user to code in various languages (ruby/python/js) and access CDD information
    Create vehicle and ground software products, data summary, etc
    Generate complicated CFS products: Schedule or network tables, copy table, etc

## Slide 7: CCDD at a glance
Data is accessible to scripting languages (JavaScript, Python, etc.)
  Example scripts provided for common products
Web-based dataserver (JSON)
Imported/exported via:
  CSV (comma-separated values)
  JSON (JavaScript Object Notation)
  XML (Extensible Markup Language)
    EDS (Electronic Data Sheet)
    XTCE (XML Telemetric and Command Exchange)
  OS clipboard (“cut & paste”)

## Slide 8: CCDD Demo

## Slide 9: CCDD Products in AA-2
C header files defining SB command/telemetry messages
  Define the structure for all software bus (SB) messages.
MID file generation ( Same file used by both CPUs )
  Defines all the MIDs for each cFS message sent/received on each CPU
    CPU2 adds 0x100 to all the MID values sent out by CPU1
    Allows Ground SW to know which computer sent a message
HK copy table generation
  Telemetry link is constrained. Select various parts of messages to go at different rates
  2 separate telemetry paths (per CPU), so 4 separate messages are sent
ITOS “rec” files (ground control system)
  Used to define commands/messages in ITOS
Data decom config files (post-flight data processing)
  Provides CSV files with desired parameters to be analyzed
  Custom built utilities to decode data from “raw” recorded telemetry files
    Significantly faster than data replay and seqprt utility in ITOS

## Slide 10: Major AA-2 Activity in 2018
Worked to develop the CDD before the SW development was complete
  CDD not treated as an “as built” post-development documentation effort
  Required iterations on data structures and MIDs, but minimized interface issues
Added ability to track ~900 DFI system parameters (in addition to OFI)
  Allows additional insight into vehicle for all ground controllers
Automated data processing and “quicklook” of key parameters after tests
  Allows rapid verification of how the system performs during simulation runs
Automated regression testing to perform SW verification activities
  Test framework consumed CCDD-generated files to define CCSDS messages
  Can verify any parameter (of any messages) meets expected values (at specific times)
Automated remote control/monitoring of ground power supplies
  Quite useful since people need to stay miles away during launch window

## Slide 11: Future Work
Launch (with a successful abort!) in May 2019
Working with Education/Outreach on student outreach contest
  Build a real-time application to show the position of the vehicle during the test
  Winning team to view KSC launch (and see app in use)
The CCDD tool has successfully been used to automate/autocode a large amount of software used on AA-2.
  Pass on the lessons learned so they can be leveraged on other programs