## Slide 1: Using the cFS Command and Data Dictionary (CCDD) to Automate Software Development on Habulous
Robert Hirsh
Robert.l.Hirsh@nasa.gov
NASA/ Johnson Space Center
12/3/2018

## Slide 2: Agenda
Habulous Background
CCDD Overview
CCDD Products used on Habulous
  C header files that define all software bus commands/telemetry messages
  Generating file defining the Message ID’s used (cfs_msgids.h )
  XML Telemetry and Command Exchange (XTCE) files (displays)
  “Protobetter” code (to manage different endian-ness/architectures)
Development on Habulous
  CCSDS_v2 extended headers
  Extending/customizing SBN to pass messages among computers on multiple networks
  Using SBN_lib to allow non-cFS node to communicate with cFS nodes
Next Steps
  Developing TTE network and schedule tables for all the various CPUs to use

## Slide 3: Habulous Background
The Habulous project is an Earth-based testbed (HW/SW)
  Prototyping future space habitat unit and technologies
  Representation from various NASA centers and aerospace organizations
    ARC/JSC/GRC/Goddard/Stennis
  Distributed nature of the team makes data interfaces especially critical
    Massively heterogeneous computer architectures and operating systems
      32/64-bit, Big/Little Endian, Linux/VxWorks/Windows, x86/PPC/RaspberryPi
  Multiple CPUs use the SBN application to communicate
    Most CPUs run cFS (use SBN app and Protobetter)
    Non-cFS CPU (use SBN_lib with Prototbetter)

## Slide 4: Habulous Block Diagram

## Slide 5: CCDD Background
CCDD stands for cFS Command and Data Dictionary
Goddard’s Core Flight System (cFS) has been, is, and is intended to be used by many projects
  Examples: Lunar Reconnaissance Orbiter (LRO), Morpheus, Exploration EMU (xEMU) spacesuit, Orion Backup Flight Software (BFS)
  Success of the cFS concept is shown by the number cFS projects at FSW-2018
A command and data dictionary (CDD) defines telemetry/command messages
Each cFS project must select a way to manage their CDD
  Frequently involves using a spreadsheet, with custom SW to convert into useful files
cFS Command and Data Dictionary utility (CCDD) was designed as a generic utility to eliminate duplication of effort in order to make CDD management easier

## Slide 6: CCDD Goals
Create a configurable CDD utility that runs on multiple operating systems
  Written in Java for maximum portability
Easy creation/modification of CDD information
  Graphical user interface (GUI) to interact with the database
Store all CDD information into a standard database (postgreSQL)
Bidirectional transfer of information to/from the CCDD
  Cut-n-paste to Excel, import/export via XTCE/CSV/JSON
Easy access to CDD information (via scripting languages and web applications )
  Allows user to code in various languages (ruby/python/js) and access CDD information
    Create vehicle and ground software products, data summary, etc
    Generate complicated CFS products: Schedule or network tables, copy table, etc

## Slide 7: CCDD at a glance
Data is accessible to scripting languages (JavaScript, Python, etc.)
  Example scripts provided for common products
Web-based dataserver (JSON)
Imported/exported via:
  CSV (comma-separated values)
  JSON (JavaScript Object Notation)
  XML (Extensible Markup Language)
    EDS (Electronic Data Sheet)
    XTCE (XML Telemetric and Command Exchange)
  OS clipboard (“cut & paste”)

## Slide 8: CCDD Demo

## Slide 9: CCDD Products on Habulous
Using the CCDD information to automatically generate the C-header files
  Define the structure for all software bus (SB) commands/telemetry messages
Generate XML Telemetry and Command Exchange (XTCE) files
  Used by display team to make displays for any CPU
Generating “Protobetter” code for communication with other CPUs
  Manages packing and different endian-ness/architectures
cfs_msgids.h file generation
  Same file compiled by all CPUs
  Defines all the MIDs for each cFS message sent/received on any of the various CPUs
  Using CCSDSv2, so each MID is a combination of APID/SystemID/SubSystemID

## Slide 10: Habulous MID definition
Telemetry
Command
2018 used by AES

## Slide 11: Major Habulous Activity in 2018
Updating to CCSDS_v2 (and using CPU# as subsystem ID)
  Running out of room for unique MIDs on all CPUs for the 11-bits of version 1
  See next slide
Exporting XTCE files to allow drag-n-drop display development for all CPUs
Extending/customizing SBN to pass messages to computers
  Computers with multiple interfaces act as a “bridge” to CPUs that can’t talk directly
  “Protobetter” developed to manage packing/endian differences
Using SBN_lib to allow non-cFS node to communicate with cFS nodes
  Allows non-cFS nodes to “impersonate” a cFS node and talk to SBN on other CPUs
Worked to develop the CDD before the SW development was complete
  Not treat CDD as an “as built” post-development documentation effort
  Required iterations on data structures and MIDs, but minimized interface issues

## Slide 12: Future Work
The CCDD tool has successfully been used to automate/autocode a large amount of software used on Habulous
Working to allow the CCDD to define even more products including
  Time-triggered Ethernet (TTE) network tables/maps
    Coordinate message passing between various synchronized machines
  cFS schedule table (for each CPU)
  Automated CCDD to SysML export