## Slide 1: CubeSat vs. Science Instrument Complexity
Chad Loeffler

## Slide 2: Topics
Introduction
Processor Boards and Software
Operations
Fault Management
Testing
Stakes Of Destruction
Conclusion

## Slide 3: Introduction
Are “low-budget” CubeSats more complex than science instruments?
Are they more similar or more different than expected?
Two instruments are compared to two satellites:
  SO-HIS (science instrument)
  JUNO-JADE (science instrument)
  CUSP (CubeSat)
  CYGNSS (SmallSat)

## Slide 4: Processor Boards and Software
JUNO-JADE (science instrument)
  4 MB SRAM, 0.5 MB EEPROM, 24 MHz CPU
SO-HIS (science instrument)
  16 MB SRAM, 2 MB MRAM, 25 MHz and 50 MHz CPU
CUSP (CubeSat)
  4 MB SRAM, 2 MB MRAM, 4 GB FLASH, 50 MHz CPU
CYGNSS (SmallSat)
  4 MB SRAM, 4 MB MRAM, 4 GB FLASH, 25 MHz CPU

## Slide 5: Operations
Science Instruments
  Receive commands and send telemetry
  Perform fault management and detection
  Collect and process science data, including use of high-voltage
  Operations Planning only has to handle reactions to thruster firings and orbit change maneuvers, not how to accomplish them
  Operations Planning only has to focus on data production to mass memory, not on storage and downlink to ground
  Usually no heater control

## Slide 6: Operations
CubeSats and SmallSats
  Control radio for uplink and downlink
  Process commands and telemetry
  Perform fault management and detection
  Perform thruster firings and orbit change maneuvers
  Perform ADCS pointing and stability
  Maintain heater control for all components
  Maintain power levels and battery charging
  Store all data in mass memory, handle partitioning and downlink

## Slide 7: Fault Management
Science Instruments
  Isolate faults to lowest level
  If fault is contained completely within a single sensor, but has multiple sensors, then can remain in science mode with unaffected sensors
  For off-nominal but not critically dangerous faults, when isolation of a component is not possible, then stay in Safe Mode
    No high voltage
    No science data collection
    No power to sensors
  For critical or dangerous faults, send Power-Off request to spacecraft

## Slide 8: Fault Management
CubeSats and SmallSats
  “Fail Operational” instead of “Fail Safe”
  Most components, except for the payload, are critical and must remain operational, even if only in a minimal capacity
    Communications Radio
    Power System
    ADCS (Attitude Determination and Control System) and Thrusters
  Faults usually result in payload instruments being powered off
  “Safe Mode” means Sun-pointing instead of Earth-pointing

## Slide 9: Testing and Integration
Science Instruments
  Test with a single spacecraft interface simulator or emulator
  Minimal external interfaces, either to the spacecraft or component between instrument and spacecraft
  Can have multiple internal interfaces, possibly with different protocols
  Sensors and detectors go through science calibration beam testing

## Slide 10: Testing and Integration
CubeSats and SmallSats
  Test with multiple instrument interface simulators or emulators
  Test with multiple spacecraft component interface simulators or emulators
  Many interfaces
    Each payload instrument
    ADCS (Attitude Determination and Control System) and Thrusters
    Power System
    Communications Radio
  Each interface may have different software or hardware protocols

## Slide 11: Stakes Of Destruction
Science Instruments
  Overwrite non-volatile memory with junk data and have no software to run
  Improperly use high-voltage and cause loss of science capability in sensors and detectors
  Low-voltage short-circuit in main electronics or non-switched component
  Mass produce too much data and fill up spacecraft mass memory (with caveats)

## Slide 12: Stakes Of Destruction
Science Instruments
  A properly isolated science instrument can only end in its own destruction, not impacting the spacecraft or other science instruments
  Usually draws power from a switched source and has limiting or monitoring on power input
  Usually limited in mass-memory partition size and cannot overwrite other instruments buffers
  Can only cause mission end if not completely isolated from spacecraft and other science instruments, sharing power circuits or memory partitions

## Slide 13: Stakes Of Destruction
CubeSats and SmallSats
  Failure to deploy solar panel arrays and start battery charging
  Failure to de-tumble and stop spinning
  Enable maximum power draw and point away from sun
  Fire thrusters too long or too little and change attitude or orbit
  Overwrite non-volatile memory with junk data and have no software to run
  Low-voltage short-circuit in main electronics or non-switched component

## Slide 14: Stakes Of Destruction
CubeSats and SmallSats
  Unrecoverable faults in hardware and software can lead to mission end, either in loss of spacecraft or loss of payload

## Slide 15: Conclusion
Stakes are higher for the CubeSat: loss of mission vs loss of single instrument.
Complexity of operations, fault management, and testing is higher for the CubeSat.
FSW processing needs are similar, such that similar or common processing board architectures can be used.